# The Seawolf Project

Object Exchange Protocol
Image Format
Reference Praxis

Version 0.01
June 8, 2008

Proprietary and confidential
# Assumptions

This document describes the reliable object exchange protocol for wireless devices in immediate proximity. The protocol assumes that the devices can communicate directly, i.e., they appear within each other's transmission range. The protocol is carried out outside TARP, preferably in a way that does not interfere with (low-bandwidth) TARP transmissions, e.g., using a separate channel (and a different transmission rate setting). The interested devices will have to switch to a special mode before an object exchange can be carried out.

As a prerequisite, the interested parties are supposed to know their distinct 16-bit identifiers, which can be extracts from their 32-bit ESNs or separate identifiers pre-negotiated in the low-bandwidth mode. Objects to be exchanged are identified by 16-bit types and 16-bit numbers. Objects of different types can share the same number while being different. The protocol is primarily intended for exchanging pictures to be displayed on the LCD; however, general file-like objects whose length may be considerable and whose integrity of reception is of essence can be accommodated.

# Packet format

Figure 1 shows the general layout of all packets exchanged in the protocol. All multi-byte components are sent in little endian order. The trailing CRC field is not directly visible to the program and is only included for completeness. The initial LID (Link ID) component formally belongs to the PHY; however, the protocol interprets it and sets as required. For this purpose, the RF driver must be put into the transparent network ID mode, which is accomplished by setting the node's network ID to 0xFFFF (with PHYSOPT_SETSID). In this mode, the driver will pass to the praxis all received packets (regardless of the LID field) and also honor the LID value inserted into an outgoing packet by the praxis.

Figure 1: Packet format
The CM field indicates the packet type, i.e., the specific “command” of the protocol. The RN field carries the request number used for matching replies to requests. The idea is this. When a node requests something from another node, then it will send a packet with its own LID and set RN to some value of its choice. Typically, the node will increment RN (modulo 256) with every new request. Any packet constituting a reply (or part of a reply) to the request will carry the LID and RN matching the original values from the request packet. This way that requester will recognize packets that are relevant to its request (e.g., ignoring any late packets from previous requests).

The length of the PAYLOAD field depends on the packet type (CM). For some CM codes, the payload length is fixed; for some others, it may vary. The packet length attribute (returned by tcv_left) can be used in such cases to determine the actual payload length. In all cases, that length is even.

# The object exchange protocol

One of the two nodes, call it the retriever, decides that it wants to acquire an object from another node, which we shall call the provider. A scenario is possible whereby the exchange is initiated by the provider, which tells the other node to retrieve an object from it; however, in such a case, the initiating message does not formally belong to the exchange protocol.

Figure 2: WTR packet format
The retriever starts the exchange by sending a WTR (Willing To Receive) packet in the format shown in Figure 2. The LID field of the packet contains the Link ID of the retriever (i.e., the request originator). The RN value is chosen by the retriever. From now on, until the end of the exchange (successful or not), the pair [R_LID, RN] will identify the request. This means that all packets belonging to the exchange will have identical contents of these two fields.

The three payload fields have the following meaning:

P_LID	This is the Link ID of the provider. Any node receiving the packet will	check this field and ignore the packet if P_LID does not match the	node's Link ID.
OTYPE	This is the type of the object to be retrieved.
OID	This is the ID of the object. As we said earlier, objects are uniquely	identified by these two numbers.
The retriever will be retransmitting periodically the WTR packet at reasonable intervals, until it receives a reply from the provider, or until its timer expires (in which case it will give up). In the reference implementation, the retriever tries 24 times at slightly randomized 0.5 s intervals. There are two possibilities regarding a valid reply from the provider. If it has the requested object and is willing to send it, it will respond with an RTS (Ready To Send) packet shown in Figure 3.

Figure 3: RTS packet format
The RTS packet contains the R_LID and RN values from the WTR packet sent by the retriever. The first element of the payload is the object's size expressed as the number of 54-byte chunks. The layout of the remaining components, covered by the blanket name ODESC (object description) depends on the object type. Thus, the total size of an RTS packet may be different for different object types.

The purpose of the RTS packet is to convey to the retriever the relevant parameters of the object, notably its size. The reason why this size is expressed in 54-byte chunks is that those chunks are the transmission units, i.e., each chunk will be sent in a separate packet. The retriever is expected to keep a tally of the received chunks and be able to notify the provider which chunks are still missing.

Some other attributes may be relevant for specific types of objects. For example, for an image, the retriever may want to know the geometry and encoding, such that it can immediately begin rendering the image as its chunks arrive.

Figure 4: ACK packet format
If the provider is unable to send the requested object, it will respond with a negative acknowledgment. The general layout of an acknowledgment packet (acknowledgments may also be sent in some other circumstances, not necessarily as part of the object exchange protocol) is shown in Figure 4. The LID and RN fields are related to the request being acknowledged. CODE identifies the acknowledgment status. If it is zero, the acknowledgment is positive; otherwise, the nonzero value of CODE tells the reason for the failure.

At this particular stage of the object exchange protocol, should an acknowledgment arrive in response to WTR, it can only be negative (i.e., CODE cannot be zero). The LID field must be equal to R_LID of the request, and RN must match the request number. Otherwise, the retriever is free to ignore the packet.

Here is the list of possible CODEs. Only some of them can be issued in response to a WTR packet.

1	General failure (no explicit reason given)	.
2	Busy. The node is currently handling some request.
3	Reject.
4	Not found (e.g., the node does not have the requested object).
5	Request format error.
6	Already done or already have it.
7	Unimplemented operation.

Only codes 2 and 4 can be returned in response to WTR. Erroneous WTR packets are ignored in the reference implementation (thus, no code 5 is returned), but this can be changed.

A negative acknowledgment packet is sent only once. If it is lost, the retriever will re-issue the WTR packet, which should trigger another negative acknowledgment (unless, e.g., the busy condition of the provider has been cleared). Regarding the RTS packet, the provider should retransmit it periodically until a response arrives from the retriever, or a timeout is triggered. The reference implementation will retransmit the RTS packet 24 times at slightly randomized 0.5 s intervals before giving up.

Having received the RTS packet, the retriever has two options. First, having seen the parameters of the requested object, it can conclude that the object is not needed after all, or, perhaps, that the object is too big to be accommodated at this time. In such a case, the node will respond (once) with a negative acknowledgment using CODE 3 (reject). This is the reason why the RTS packet should be retransmitted periodically by the provider (rather than being triggered once on every WTR). If the retriever still wants to receive the object, it will initiate the first round by sending a GO packet.

From now on, the actual transmission of the object will be taking place. It will consist of rounds, whereby the retriever first notifies the provider which chunks of the object are still missing, and then the provider sends those chunks back-to-back, without expecting anything from the retriever until all chunks in the round have been sent. At the end of a round the retriever tallies up the chunks and, if some are still missing, requests (all or some of) them from the provider, which then sends another batch of chunks as required. This operation continues until all chunks have been received or any of the two parties hits a timeout while expecting a reply from the other.

Figure 5: GO packet format
The retriever notifies the provider about missing chunks with a GO packet (see Figure 5). The payload consists of the list of missing chunks numbered from 0 up to the total number of chunks in the object –1. This list may contain individual chunk numbers (little-endian 16-bit numbers) or ranges. For as long as the numbers in the list are increasing, they stand for individual chunks. A decreasing pair of numbers represent a continuous range of chunks between and including the two. For example, the sequence 3, 5, 6, 9, 13, 8, 17 describes chunks 3, 5, 6, 9, 8 through 13, and 17. Normally, the initial GO packet sent by the retriever specifies N-1, 0, i.e., the complete range of all chunks (its payload length is 4 bytes). Note, however, that if the retriever has a partially received version of the object (e.g., connectivity was lost during a previous download session), it can naturally resume the operation in the exact place where the previous reception was aborted.

In any case, a round is always started by a single GO packet, which means that the provider may only be able to learn about a subset of all those chunks that are still missing at the retriever. This will happen if the complete description of all the missing chunks cannot fit into a maximum-sized GO packet (23 16-bit numbers). Note, however, that the first GO packet of a reception starting from scratch tells the provider to send all chunks of the object. Thus, in the first round, the provider will always send the entire object.

Having created a GO packet for the next round, the retriever should retransmit it periodically until it sees the first CHUNK packet arriving from the provider (or until it hits a timeout). The reference implementation will retransmit a GO packet 24 times at slightly randomized 0.5 s intervals.

If the retriever finds out that it has received all the chunks, it should notify the provider that the reception is over by sending it an empty GO packet (empty list of chunks). There will be no reply to such a packet: the provider will just shut down its part of the protocol. If the retriever wants to improve the chance that the provider has seen the packet, it can send the empty GO a few times. This isn't critical, as the provider will eventually time out while expecting a GO from the retriever and end the session anyway. The reference implementation sends the empty GO packet twice separated with a slightly randomized 0.5 s interval.

Figure 6: CHUNK packet format

The only valid response to GO is a CHUNK packet. Normally, the provider sends multiple CHUNK packets in response to a single GO: as many of them, as many have been requested. The layout of such a packet is shown in Figure 6. N is the chunk number (counting from zero). The number of bytes in a chunk is always 54, with the possible exception of the last chunk, which can be partial. But in all cases that number is even. Consequently, if the object consists of an odd number of bytes (and this fact is relevant), this information must be conveyed to the retriever in the RTS packet.

Note that chunks are not expected to be sent (or arrive) in any particular order. The provider is free to send them in any order, possibly duplicating some, possibly missing some from the requested list. The latter could have been missing due to losses in the wireless channel, so it should make no difference to the retriever. For example, the provider may not have enough memory to be “accurate” about the retriever's request. The protocol operates according to the principle of pushing the system towards the target state, with the quality of the “pushes” self scalable to the circumstances, be it the node footprint or the channel quality.

Having completed the current round, i.e., transmitted all the chunks that it was going to send in response to the last GO request from the retriever, the provider sends an empty CHUNK packet, i.e., one with no payload. This packet is sent periodically until the provider sees another GO from the retriever (or until it hits a timeout). The reference implementation retransmits the empty CHUNK packet 24 times at slightly randomized 0.5 s intervals.

# Image format

The praxis directory contains a script named cbm.tcl for converting Windows bitmap images to the internal format for storing them at nodes and displaying on their LCDs. The present version of the script converts only 24-bit images. This is how you call it:

cbm.tcl image.bmp image.nok

Converts file image.bmp (containing a 24-bit Windows bitmap image) to image.nok in 12-bit format. This is equivalent to:

cbm.tcl -12 image.bmp image.nok

This way:

cbm.tcl -8 image.bmp image.nok

you will create an 8-bit version of the image.

The program will prompt you for a “label”, which can be any piece of string intended to briefly describe the image. Its maximum useful length is 34 characters. When images are stored at nodes, the labels can be used to identify them.

The maximum resolution of an image accepted by the script is 130x130 pixels (this is the maximum size picture that can be displayed on the LCD).

Here is the layout of the image file (all numbers are little endian):

Bytes 0-3	ASCII characters 'o' 'l' 's' 'o' intended as a magic code.
Bytes 4-5	An integer number identifying the image type. Only two values are	used at present: 0 = 12 bits per pixel, 1 = 8 bits per pixel.
Bytes 6-7	X resolution (the number of pixels in a row).
Bytes 8-9	Y resolution (the number of rows).
Bytes 10-11	Label length in bytes.

This is followed by the label (exactly the specified number of bytes), which, in turn, is followed by the pixels stored by rows. With the 8bpp format, each pixel takes exactly one byte (encoded as described in the reference documentation for Nokia LCD – Phillips PCF8833). With the 12bpp format, two consecutive pixels take three bytes. If the total number of pixels is even, the total number of bytes is divisible by 3. Otherwise, the last pixel takes two bytes.

# The reference praxis

The sample praxis built around the object exchange protocol described above is meant to test the capabilities of the device and provide a seed for a true application. It has two interfaces: wireless (whereby a node can talk to other nodes running the same praxis) and UART. The latter essentially emulates wireless in the sense that 1) the UART operates in the TCV mode (i.e., handles packets), 2) the same set of commands is available over both interfaces. The node runs a pair of identical threads listening to the two interfaces and treats them in (almost) the same way.

The praxis directory includes a script named oss.tcl, which can be used to converse with a node over the UART. The selection of commands (packets) that the script can issue is larger than than available to the praxis in its present implementation, but, in principle, a wireless node (running a slightly different version of the praxis) could use those “extra” commands to emulate the script over the RF channel.

Additional packet types

All packets used by the praxis employ the same format as the object exchange protocol. In addition to the packet types required by the object exchange protocol, the praxis defines a few additional packet types described below:

HELLO (LID = 0, CM = 1, RN irrelevant)

The payload consists of 4 bytes representing the sending node's ESN in little endian format. The node sends this packet approximately every 8 seconds (the intervals are randomized) to indicate its presence in the neighborhood. The packet is sent on both interfaces, but not necessarily at the same time (the two interfaces are handled by independent threads).

Figure 7: OSS packet layout.

OSS (LID = sender's Link ID, CM = 2, RN = sender's request number)

The packet (see Figure 7) carries an OSS request, primarily intended to support conversation between the OSS script and one node interfaced to it over the UART. However, there are no formal reasons why a regular node couldn't issue such requests as well. The first two bytes of the payload (following the RN byte) contain the recipient's Link ID (this way the target node can recognize that the request is addressed to it). The third byte of the payload, which we shall call OSS RQ, indicates the OSS action that the recipient is asked to carry out. The fourth byte is ignored at present: its role is to even-out the boundary of the subsequent parameters (specific payload), which depend on OSS RQ. The total packet length can vary depending on the request.

STAT (LID = recipient's Link ID, CM = 8, RN = recipient's request number)

The packet is sent in response to a specific OSS RQ (PING – see below) and reports on the node's status. The payload is fixed length (10 bytes) and carries these items (in the order of their occurrence):

ISTAT: a single-byte collection of global status bits related to images stored at the node. Only one bit (number 0, i.e., 0x01) is used at present to indicate an inconsistency detected in the image file system.

NIMG: a single-byte integer value indicating the number of images stored in the node's EEPROM.

FFREE: a two-byte little endian value indicating the number of free (logical) pages of EEPROM (available for storing images). Logical page size is 8KB.

RILO: Received Image List Owner. This is the two-byte Link ID of the owner of the list of images that the node has acquired from one of its neighbors. This is explained below. In a nutshell, a node can ask a neighbor for a list of its images. When acquired, such a list is stored at the receiving node (at most one at a time) and can be propagated to other neighbors. If there is no acquired image list at the node, this value contains zero (which can never be a legitimate Link ID).

NNBR: the two-byte number of neighbors. This is the number of nodes from which the sending node has received HELLO messages within the last 2 minutes.

RNLO: Received Neighbor List Owner. Similar to images, a node can receive a list of neighbors from another node and store it, possibly to pass it on to other neighbors. If this two-byte value is nonzero, it tells the Link ID of the owner of the acquired neighbor list currently stored at the node.

DEBUG (LID irrelevant, CM = 0, RN indicating the type of debug content)

These packets are intended for passing debug information to the OSS script. This is why they do not attempt to identify the sending or receiving party (it should be always clear). The content type can be:

Text line (RN = 0). The payload consists of two 16-bit values (two bytes each) followed by a NULL-terminated ASCII string, up to the total length of 52 characters (including the NULL byte). Such packets are generated by the diagg function (defined by the praxis), whose header is:

void diagg (const char *msg, word a, word b);

where a and b are arbitrary values to be passed to the OSS script in the DEBUG packet.

Memory dump (RN = 1). The payload consists of a sequence of bytes copied from memory (up to 56 bytes, always an even number). Such a packet is sent in response to a DUMP request from the OSS script, so the address of the chunk is implicitly known to the recipient.

EEPROM dump (RN = 2). As above, but the bytes have been extracted from the EEPROM.

Various OSS requests (described below) can trigger ACK packets with OSS-related codes (which extend the set of codes defined by the object exchange protocol). Note that there is no implied reliability in the delivery of OSS requests or their feedback. Consequently, the OSS script should verify the effect of its request to make sure that it has been carried out by the node. For example, if you request the node to erase its images from EEPROM, and no feedback (ACK OK) arrives in response, you should poll the node for its STATUS to confirm the erasure.

Neighborhood information is only collected from those HELLO packets that arrive over the RF channel, i.e., the OSS script can send HELLO packets, if it pleases so, but they will be ignored by the node. The node does not have to know the neighbor to receive and honor a request from it, be it an OSS request or an object exchange request (WTR). Such a request identifies the originating neighbor, and the node knows how to respond, even if the neighbor is not present in the node's neighbor list. The present OSS script uses the Link ID of 1, which should not be used by any node.

Exchangeable objects

As we said earlier, the object exchange protocol can (in principle) handle objects of different types. Three types of objects are defined by the present praxis: Image (OTYPE = 0), Image List (OTYPE = 1), and Neighbor List (OTYPE = 2). The interpretation of the object identifier (OID) is as follows:

For an image, the OID is a numerical identifier of the image and can be any 16-bit value.

For an image list, OID = 0 refers to the node's own image list, while OID = 1 refers to the image list that the node has received from another node. These are the only legitimate values of OID for OTYPE = 1.

Similarly, for a neighbor list, OID = 0 refers to the node's own neighbor list, while OID = 1 refers to the neighbor list that the node has received from another node. These are the only legitimate values of OID for OTYPE = 2.

Images

Images acquired by a node are stored in EEPROM in such a way that one image occupies an entire number of 8KB (logical) pages, with each page being a continuous chunk of EEPROM starting at an 8KB boundary. A page can be of one of three kinds:

Free, if its first two bytes look like 0xFFFF. In particular, immediately after the EEPROM is erased, all pages are free.

The first page of an image. Such a page has 0x7F00 (little endian) in the first two bytes. When looking for a specific image, or counting images stored in the EEPROM, the praxis only looks at such pages.

Other. Such a page may belong to an image (be one of its non-first pages) or contain something else (which is of no concern to the image file system). The first two bytes of an internal (non-first) page of an image can never 0xFFFF or 0x7F00.

Here is the layout of the first page of an image (see Figure 8).

Bytes 0-1	0x7F00.
Bytes 2-3	Image number, i.e., the OID of the image.
Bytes 4-5	The total number of chunks in the image. This many chunks have to be sent	to pass the image to another node.
Bytes 6-7	The row size, i.e., the width of the image expressed in pixels. If the image is 8bpp, 0x8000 is or'red into this value, i.e., the most significant bit indicates the pixel encoding and should be removed before the value is interpreted as the image width. The maximum width is 130.
Bytes 8-9	The image height in pixels (the maximum is 130).
Bytes 10-11	The total number of pages occupied by the image. This number is never greater than 5 (thus, the upper byte is always zero).
Bytes 12-21	This is a 5-word array containing the numbers of all pages occupied by the image, starting with this page number. Only the number of entries indicated in bytes 10-11 are valid. A page number is the address of the first byte of the page shifted by 13 bits to he right.
Bytes 22-55	The label, i.e., an arbitrary sequence of characters associated with the image to be used as its brief description. It is reasonable to assume that the label is an ASCII string. If its length is exactly 34 characters, then it doesn't have to end with a NULL byte.

Figure 8: The first page of an image stored in EEPROM.
The above bytes are followed by the list of chunks constituting the image's pixel data. Each chunk is preceded by its two-byte number counting from zero, thus, it takes 56 bytes altogether. Each page accommodates an entire number of chunks, which is 146. As 146 x 56 = 8176, the last 16 bytes of a page are not used.

Note that the representation does not assume that the chunks must be stored in the file in order. This is because when an image is received, some of its chunks may be missing, in which case they will be retransmitted later. As writing to the EEPROM at random is not a good idea, the chunks are simply stored linearly in the order in which they eventually arrive. This also means that the operation of rendering an image must be able to display individual chunks independently based on their numbers.

If the chunks do not fit all on one page, they are continued on subsequent pages whose numbers are listed in an initial fragment of the first page (as shown in Figure 8). A continuation page will start with a chunk number, which can never be larger than 730. Thus, a continuation page cannot accidentally pose for an empty page or the first page of an image.

The chunk numbered zero is the first chunk following the opening sequence of the image, i.e., bytes 0-55 of the first page. Those bytes are not sent as a chunk (so they formally don't count to the chunk list). Instead, that information is conveyed in the RTS packet sent in response to the WTR request for the image.

Note that while the format of a WTR packet is fixed regardless of the object type, the RTS packet that arrives in response to it carries type-specific information and its layout may vary depending on what kind of object is requested. For an image, the ODESC field of RTS packet (see Figure 3) has the layout shown in Figure 9, with the respective fields copied from the image description in EEPROM. The portion of the image's label field stored in the descriptor extends up to and including the first NULL byte occurring the label field in EEPROM. Then, if the total length of this sequence is odd, one (dummy) extra byte is inserted to make sure that one descriptor takes an even number of bytes. If no NULL byte is found within the label field (bytes 22-55 in Figure 8), the entire label field (with no NULL byte) is included in the descriptor.

Figure 9: ODESC field layout of an image RTS packet.

Image lists

The structure of an image list is shown in Figure 10. When exchanged, this list is split into chunks and sent/received in a similar way as an image. The first two bytes of the list object contain the Link Identifier of its owner. This is followed by as many image descriptors as many images the node has stored in its EEPROM. Each descriptor begins with a two-byte number indicating its size (the descriptor itself doesn't count to the size).

Figure 10: Image list layout.

The minimum possible length of an image list is 2 bytes. Such a list consists solely of the owner LID and says that the owner has no images. The rules regarding the label field are the same as for an RTS packet pertaining to an image object (see above).

The ODESC field of an RTS packet for an image list object contains a single 2-byte value specifying the total (accurate) length of the list (in bytes). Note that number of chunks is a standard component of an RTS packet (see Figure 3), however, that number does not convey the exact size of the object (only that size rounded up to a multiple of 54 bytes). For images, this is OK: they are stored in EEPROM and it makes sense to round up their size to a multiple of chunks (it must be rounded up to a multiple of EEPROM pages anyway). On the other hand, image/neighbor lists are smaller objects (stored in RAM), and the recipient may prefer to know their precise length before it decides to fetch the object.

Neighbor lists

The structure of a neighbor list is similar to that of an image list, but simpler (see Figure 11). The 2-byte owner LID field (which is the required component of any neighbor list, including an empty one) is followed by the sequence of full ESN numbers of the node's neighbors stored as 4-byte little-endian integer numbers.

Figure 11: Neighbor list layout.

The RTS packet for a neighbor list has the same layout as that for an image list, i.e., the single 2-byte component of the ODESC field specifies the exact length of the neighbor list in bytes.

OSS requests

Here is the list of OSS request that the praxis is prepared to handle. All those requests are implemented by the present OSS script and are available from it as commands.

PING (OSSRQ = 0)

No more payload is expected in the request packet. In response to this request, the node sends a STATUS packet.

GET (OSSRQ = 1)

With this request, the node is instructed to issue a WTR request for an object to be retrieved from the indicated neighbor. The specific elements of the payload include (in this order):

- two-byte Link ID of the node from which the object should be acquired
- two-byte object type (OTYPE)
- two-byte object ID (OID)
- one-byte interface selector (0 = RF, 1 = UART)
- one-byte request flags

Having received such a request, the node will issue on the indicated interface a WTR request for the specified object. Note that the Link ID may coincide with the Link ID of the node (or the OSSI script) issuing the request; thus, the operation can be used to “push” an object into the node. Only one value of the flags is used at present, and it applies to images only. Bit 4 (value 0x10) tells the node to display the image while it is being received. Without that flag, the received image is just stored in the EEPROM.

The node should respond to the above request with ACK 6, if it already has the indicated object, ACK 0, at the end of a successful reception, or ACK 1, if the operation fails for whatever reason. This is generally not reliable, so you may want to check after a while if the requested object is present at the node.

QUERY (OSSRQ = 2)

This is an inquiry to the recipient about a specific object. The specific payload contains two 2-byte values: OTYPE and OID. The recipient will respond with ACK 0 (OK) if it has the indicated object, and with ACK 1 (failure), otherwise.

CLEAN (OSSRQ = 3)

This is a request to remove an object (or a set of objects) from the node. The specific payload starts with a 2-byte OTYPE field. Then:

If OTYPE = 0, i.e., the request refers to images, the remaining part of the payload consists of image OIDs (2-bytes per one identifier). If that list is empty, then ALL images at the node will be deleted.

If OTYPE = 1, the remaining payload is ignored and the node erases its received image list.

If OTYPE = 2, the remaining payload is ignored and the node erases its received neighbor list.

Having completed the operation, the node sends an ACK 0. This also happens if the operation was void, e.g., the node didn't have the object(s) to be deleted. The ACK simply indicates that the request has been recognized and accepted.

SHOW (OSSRQ = 4)

The single specific payload item is an image OID. The node is requested to display the specified image (if present in its EEPROM) on the LCD. The response is ACK 0, if the image was found in the EEPROM (and displayed), or ACK 1, otherwise.

LCDP (OSSRQ = 5)

This request can be used to issue a raw command to the node's LCD (and is primarily intended for debugging and low-level experiments). The first byte of the specific payload carries the LCD command (you have to consult the documentation to understand what you are doing), and the second byte specifies the exact length of the argument string in bytes. That many bytes are expected in the remaining portion of the packet.

Generally, an LCD command consists of a single-byte command code with an optional sequence of data bytes to which the command applies. For example, to set the contrast, you should issue command 0x25 followed by a single-byte contrast setting.

Having issued the command to the LCD, the node replies with ACK 0.

BUZZ (OSSRQ = 6)

Sound the buzzer for the specified interval described with a single two-byte value D. The amount of time is approximately equal D x 6 msec. Having executed the command, the node replies with ACK 0.

RFPARAM (OSSRQ = 7)

The request can be used to change an RF parameter. The specific payload consists of two bytes: the parameter type and its new value. The possible parameter types are:

0	turn the RF module off (value = 0) or on (any nonzero value); this applies to both the transmitter and the receiver at the same time
1	set power; the value is as for PHYSOPT_SETPOWER
2	set channel; the value is as for PHYSOPT_SETCHANNEL
3	set rate; the value is as for PHYSOPT_SETRATE
5	reset the module (value ignored)

Having executed the operation, the node responds with ACK 0. If the parameter type is not one the above, the node will respond with ACK 7 (unimplemented).

These two OSS packet types:

DUMP (OSSRQ = 8) and EE (OSSRQ = 9)

are intended for debugging. With the first one, the OSS script can request a dump DEBUG packet showing the contents of the specified RAM/ROM or EEPROM locations. The specific payload consists of:

- single-byte memory designator (0 = RAM/ROM, 1 = EEPROM)
- single-byte dump size in bytes, which must be between 1 and 56
- four-byte starting address

For a RAM/ROM dump, the specified address is truncated to 16-bits.

With EE, the OSS script can request the node to erase its EEPROM. The specific payload consists of two four-byte numbers specifying the starting and ending EEPROM addresses, as for the standard PicOS operation ee_erase.

Note:

Any OSS request will be immediately rejected by the node with ACK 2 (busy), if the node is currently involved in an object exchange. It makes sense to PING such a node periodically for its status until the STATUS response is produced, which will mean that node is available.

# The OSS script

Before running the script, determine the COM number of the port interfacing the PC to the node. Execute

./oss.tcl N

where N is the COM number. Read README.txt in the praxis directory and go through the exercise.

Here is the list of commands you can execute from the script. Arbitrary unique abbreviations can be used instead of full keywords.

verbose n

This command sets the level of feedback you will be receiving from the script. The default is 1, minimum is 0, maximum is 3 (in that case, the script will be dumping all packets received or sent out).

retrieve otype oid

This command carries out the receiving end of the object exchange protocol. It issues to the node a WTR request for the specified object and then receives the object as prescribed by the protocol. For example:

retrieve 1 0

will let you see the node's image list.

Note that while images can be received this way by the script, they are not saved, but discarded after reception. The script doesn't know what to do with a received image. This can be easily fixed, if needed.

getobject lid otype oid flags

The command tells the node to retrieve an object from the indicated source. It issues a GET OSS packet with parameters determined from the arguments of the command. If the specified Link ID (lid) is 1, the interface selector of the GET packet will be 1 as to select the UART interface. This means that the node will issue a WTR request to the OSS script itself. Otherwise, the interface selector will be zero assuming that the Link ID refers to one of the node's neighbors.

In order to upload an image into the node, you should include an extra argument, which is the file name of a properly encoded image. This extra argument is required if the first two arguments are 1 and 0, i.e., the command asks the node to retrieve an image from the OSS script itself, e.g.,

getobject 1 0 12 16 PICTURES/wlodek.nok

You can assign any OID value to the uploaded image, as long as there is no image with that OID already at the node (in which case, the node will respond with ACK 6). The value of flags (16) in the above example will tell the node to display the image as it is being received.

ping

Ping the node. You should see the STATUS or ACK 2 (busy) in response.

clean otype oid ... oid

The command issues a CLEAN OSS packet to the node. The list of OIDs is only relevant for images OTYPE = 0. Note that when it is empty, the node will remove all images from its EEPROM.

query otype oid

Issues a QUERY OSS packet. For example,

query 1 1

asks the node where it has an acquired image list. Note that this query:

query 1 0

will always succeed (response ACK 0), as any node always has its own image list (even though its collection of images may be empty).

show oid

Request the node to display the indicated image (sends a SHOW OSS packet).

lcd cmd n ... n

Issues an LCD command (sends and LCDP OSS packet). All arguments are integers that will be converted to bytes. They can be specified in any form that looks like an absolute Tcl expression, e.g., this request issues the set contrast command (0x25) with a single numerical argument (34):

lcd 0x25 1+2+33-16/7

Note: this useless feature applies to any numerical argument of any command.

buzz dur

Sends to the node a BUZZ OSS packet with the specified duration parameter.

rfparam par value

Sends to the node an RFPARAM OSS packet with the specified parameter code and value.

dump addr n

Asks the node to send back the contents of n bytes of RAM (or ROM), which must be between 1 and 56, starting at address addr. The response will arrive as a dump-type DEBUG packet (which the script will present in a decent form). If you put the letter 'e' in front of addr, e.g.,

dump e 8192 40

then the command will apply to the EEPROM.

erase from upto

Sends an EE OSS packet to the node requesting it to erase the indicated area in EEPROM. Note that this command:

erase 0 0

will completely erase everything. The meaning of the two parameters is as for the standard PicOS operation ee_erase.