VUE2

Version 0.52

March 2007

Note: relevant changes with respect to version 0.51 are in blue

© Copyright 2007, Olsonet Communications Corporation.
All Rights Reserved.
# Introduction

VUE2 or (VUEE) which stands for Virtual Underlay Emulation Engine, is an emulator for PicOS applications and their underlying networks. VUE2 is facilitated by the fact that PicOS is a relatively straightforward descendant of a powerful simulator named SMURPH. Thus, the Emulation Engine comprising VUE2 is built around SMURPH, with a natural mapping of many PicOS operations to their SMURPH counterparts.

This document is a preliminary draft of VUE2 description, including its interfaces needed by a PicOS developer to maintain compatibility with VUE2 (such that the PicOS praxis can be directly run under VUE2). As the system is being developed, it is likely to change, not only in the course of its natural evolution, but also in response to new features being added to PicOS (which will be mirrored in VUE2). At present, VUE2 captures a significant subset of all PicOS features, including drivers for RF modules, PIN interface, external memories and UARTs. Most importantly, it provides for an easy expression of network models and their virtual deployment. This means that PicOS praxes[1] can be run under VUE2 on a multitude of virtual nodes behaving as if they were interconnected via realistic wireless links. Those virtual nodes can interface to real-life OSS agents in exactly the same manner as real nodes would. Thus, in addition to providing insights into the behavior of a PicOS praxis in the real world (performance assessment, network planning), VUE2 also facilitates the development of various agents that have to be interfaced to that praxis to make the overall system complete.
[1] PicOS term for “applications.”

This document will not be comprehended without the following accompanying documents by Olsonet Communications: PicOS, version 2.01 [or higher], VNETI: Virtual NETwork Interface, version 2.01 [or higher], SIDE/SMURPH: a Modeling Environment for Reactive Telecommunication Systems, version 2.8 [or higher].

# Similarities and differences with respect to SMURPH

The striking similarity between PicOS and SMURPH is in the thread model. In both environments, a thread describes a finite state machine with the state transition function specified in terms of event wait operations. The rules for aggregating such operations and waking up the threads based on the occurrence of the awaited events are practically identical. In SMURPH, viewed as a simulator, the awaited events are delivered by abstract objects called Activity Interpreters, while in PicOS they are triggered by actual physical phenomena (e.g, a packet reception, a character arrival from the UART, and so on).

The first significant difference between the two systems is in the interpretation of time flow. In SMURH, time is purely virtual, which means that formally nobody cares about the actual execution time of the simulation program but only about the proper marking of the relevant events with virtual time tags. As in all event-driven simulators, the virtual time tags have nothing to do with real time. For example, a significant amount of calculations may be needed to advance the virtual time by a few microseconds, and no computation at all may be required to bypass several hours of idleness caused by no events in the system model. In the first case, the tiny advancement of the virtual time may take several hours of calculations, in the second case, the system may immediately jump several hours into the future in no time at all.

Consequently, the formal useful semantics of SMURPH and PicOS threads are intentionally different. The actual execution time of a SMURPH thread is essentially irrelevant (unless it renders the model execution too long to wait for the results) and all that matters is the virtual delays separating the artificially triggered events. For example, two threads in SMURPH may be semantically equivalent, even though one of them may exhibit a drastically shorter execution time than the other (due to more careful programming and/or optimization). In PicOS, however, the threads are not (just) models but they run the actual thing. Consequently, the execution time of a thread may directly influence the perceived behavior of the PicOS node.

In this context, the following two assumptions make our endeavor worthwhile:

1. PicOS programs are reactive, i.e., they are practically never CPU bound. In other words, the primary reason why a PicOS thread is making no progress is that it is waiting for a peripheral event rather than the completion of a lengthy calculation.
2. If needed (from the viewpoint of model fidelity), an extensive period of CPU activities can be modeled in SMURPH by appropriately (and explicitly) delaying certain state transitions.[2]
  [2] We are contemplating adding tools to VUE2 that would make it possible to specify the timing of state execution time in a PicOS thread. Such a specification could indicate that the amount of CPU time needed to run through the state is not trivial. At the moment, the prospective usefulness of such a feature is unclear.

Consequently, in most cases, we can safely ignore the fact that the execution of a PicOS program takes time at all and only focus on reflecting the accurate behavior of the external events. With this approximation, the job of porting a PicOS praxis to its VUE2 model becomes reasonably simple. To further increase the practical value of such a model, SMURPH provides for the so-called visualization mode of its execution. In that mode, SMURPH tries to map the virtual time of modeled events to real time, such that the user has an impression of talking to a real application. This is only possible if the network size and complexity allow the simulator to catch up with the model execution to real time. If not, a suitable slow motion factor can be employed. These issues are described in detail in the SMURPH manual.

While the syntax of PicOS threads is close to that of SMURPH processes, there are some differences. First of all, the language of SMURPH is C++, while PicOS is plain C. Second, a PicOS praxis is a one-node program, while the SMURPH model of that praxis must consist of multiple nodes running the same or possibly different programs. Additionally, the praxis code must be supplemented by the models of all those components of reality that are needed by the praxis to run. This brings about three issues:

1. Transforming the syntax of PicOS programs to that acceptable by SMURPH.
2. Putting multiple nodes, possibly with different PicOS praxes, under the umbrella of a single SMURPH program (model).
3. Modeling the peripheral equipment needed by the praxis; also interfacing and parameterizing such models.

The third part is provided as a library of models whose interiors need not be interesting to the developer. This is to say, the third issue does not overly affect the operation of rendering a PicOS praxis executable under VUE2, as long as the necessary peripherals have their models in the library. This is because the interface (API) to those models looks exactly as the PicOS API to the real equipment. On the other hand, the first two issues come into play when the praxis is (re)organized for execution under VUE2. Notably, with the right structure (explained in the next section), the praxis may exist in a single version, which is shared between PicOS and VUE2. Most of the code is directly shared. There is no need to convert it from PicOS to VUE2 or vice versa. Thus, the emulated execution deals with the real code!

# The structure of VUE2 compiler

The VUE2 compiler, i.e., the program that turns a collection of PicOS praxes into an executable model of the network, is in fact the mks program of SMURPH, i.e., the compiler of SMURPH models into executable programs. Here is the list of components needed to set up the complete platform. These components can be configured under Cygwin (Windows) or directly under a UNIX system, e.g., Linux.

1. The standard (vanilla) SMURPH/SIDE package constituting the emulation kernel of the system.
2. PicOS, which in addition to its current collection of VUE2-compatible praxes provides certain files that are directly used by VUE2.
3. VUE2 specific environment consisting of libraries and other files that in combination with PicOS sources and praxes contribute to VUE2 models.

One special item included with the VUE2 environment (point 3) is udaemon. This is a Tk script implementing an interface (GUI) to VUE2 models.

The exact way of setting up SMURPH and PicOS is described elsewhere. Here we shall focus on the VUE2-specific aspects. For illustration, suppose that the three components have been unpacked at the same level (e.g., in the user's home directory). They fill three separate source trees rooted at directories VUEE, PICOS and SIDE.

## Notes on configuring SMURPH/SIDE with VUE2

When setting up SMURPH/SIDE (according to the instructions in the manual), you have to specify, when requested by maker, the proper location of the include libraries needed by VUE2. This location is VUEE/PICOS. Thus, the relevant fragment of your conversation with maker when installing the package should look something like this:

Now, please enter the list of paths to 'include' libraries (which can be absolute or relative to your home directory), each path in a separate line. Enter an empty line when done. This path:

        /home/pawel/SIDE/Examples/IncLib

is standard and need not be specified. If you want to exclude the standard path, enter '-' as the only character of an input line.
VUEE/PICOS

where the last line (in italics) is your response (it assumes that VUE2 has been unpacked in the home directory). Note that the default suggested by maker is retained, and one more (VUE2-specific) include library is added. The standard (default library) is also needed as it provides the models of wireless channels used by VUE2.

Defaults can be selected for the remaining installation parameters. The monitor, needed for the Java DSD applet is optional. The monitor connection of SMURPH is not required for interfacing VUE2 models to external daemons, and its only practical advantage is for internal monitoring of models under intricate debugging.

It makes sense to use a non-default name for the mks program generated by maker, i.e., the actual compiler of VUE2 models. The recommended name is vuee or vue2. When called under one of these names, the compiler automatically forces –L and –W, i.e., selects the visualization mode of SMURPH and disables the (redundant) models of wired channels.[3] Note that all VUE2 models require –W to compile.
[3] Wireless and wired channel models can coexists if needed. The system is capable of modeling hybrid networks.

It is possible to have a single installation of SIDE to be used for VUE2 as well as for other purposes, i.e., simulation of network protocols. Having run maker once to create the vuee compiler, you can run it again possibly selecting another configuration of include libraries and assigning the standard (or different) name to the mks compiler. Depending on which compiler version is invoked, the corresponding include libraries will be referenced and the respective set of options will be applied.

## Notes on setting up VUE2

The VUE2-specific components unpack into directory VUEE. It is convenient if this directory occurs at the same level as PICOS. Having unpacked the directory, move to VUEE/PICOS and execute ./mklinks in that directory. That will set up a few links to PicOS files needed by VUE2 and will only work if that directory occurs at the same level as VUEE. If this is unsuitable for whatever reason, you can edit the mklinks script specifying the correct path to PICOS.

Certain files in the PICOS tree (those linked to from VUEE/PICOS) are directly compiled as components of VUE2 models. In particular, tcv.c (VNETI) is one of those files. This greatly simplifies the compatibility issues for networked praxes.

Formally, the proper order of unpacking and installing the three systems is PICOS, VUEE, SIDE/SMURPH. This is because VUEE needs links to PICOS and SMURPH needs VUEE/PICOS as the include library. Having installed everything, you can compile those PICOS praxes that have been made VUE2 compliant by moving to the praxis directory and executing vuee (or whatever name you assigned to the VUE2 SMURPH compiler). The outcome of this compilation will be an executable file named side (side.exe under Cygwin). By running this file (with a suitable data file), you will execute the model.

A VUE2 compliant praxis can be compiled by both the VUE2 compiler as well as the PicOS compiler. In the latter case, you simply execute mkmk boardname in the praxis directory followed by make. An extension has been added to the PicOS compiler[4] to accommodate multiple praxes in the same directory. This is needed in situations when a single VUE2 model must accommodate multiple praxes (different node types). Such praxes being related, it makes sense to keep them in the same directory – also for PicOS.
[4] As of CVS commit R061216C.

Traditionally, in the single-praxis-per-directory case, mkmk seeks a file named app.c, which it treats as the root file of the praxis. The configuration of its include files + the board options + the possible extra options specified in options.sys in the praxis directory determine the constituents of the target Image file to be loaded into the microcontroller. If there is no file named app.c, but there is another file whose name looks like app_xxx.c, mkmk assumes that this is the praxis root and compiles it instead. The resulting image files will be called Image_xxx (the ELF version) and Image_xxx.a43 (the Intel hex version). If multiple files named app_... are present, e.g., app_one.c and app_two.c, mkmk will assume that there are multiple praxes in the directory and generate a Makefile to compile them all into separate images (Image_one and Image_two in this case). A VUE2 compliant configuration of multiple praxes will follow this convention to make those praxes discernible by mkmk (PicOS), while keeping them unified for the purpose of their combined model in VUE2.

One more feature of new mkmk is the treatment of those source files whose names end with the suffix .cc. As we shall see later (step 7 on page 16), this suffix is needed for a file to be compilable by SMURPH. If a file with this suffix becomes needed by the praxis when compiled under PicOS, the compiler copies it to a similarly named file with the suffix .c and compiles it from there. This also applies to praxis roots, i.e.,files named app_xxx.cc.

# Converting PicOS praxes to a VUE2 compliant format

We start from the list of general guidelines. On top of those guidelines are some further restrictions mostly resulting from the fact that not all PicOS operations are currently modeled in VUE2. However, the ones that are modeled are sufficient for practically all our present praxes. Besides, the list of deficiencies will shrink as the modeled components are extended to accommodate new praxes. It is postulated that all new praxes be programmed in the VUE2 compliant style from the beginning. Should a need arise to extend the assortment of VUE2 tools, we will be quick to respond to such requests.

## General guidelines and comments

These guidelines can be viewed as prerequisites for an easy (mostly automatic) conversion of an existing praxis that was programmed with no VUE2 compatibility in mind. This is to say, the first step in such a conversion would be to make sure that the praxis code follows these guidelines.

1. Construct your threads using these operations: thread, strand, endthread, endstrand, instead of process and endprocess. Similarly, use runthread, runstrand instead of fork.
2. Do not use static declarations within a process function. Such declarations are intended to express “permanent' local variables of processes. Instead, move them all to the global scope and use differentiating prefixes or suffixes in case of conflicts. Note that keeping all de facto global variables in one place helps avoid memory fragmentation on misalignment in a PicOS incarnation of the praxis.
3. Do not use entry constructs with numerals or expressions, e.g.,
  entry (RS_CMND+1)
  entry (0)
  Make sure that all state arguments in those operations that accept state arguments are simple constants representing state names. This means that all states must be assigned distinct symbolic constants.
4. Identify those global variables that must be statically initialized and separate them from those that need not. It may make sense to group the two classes into two contiguous chunks. There is no penalty for initializing some of the latter (say with zero), other that such an initialization will have to become explicit at some point.

The primary source of some rather ugly complications related to points 2 and 4 is the fact that all de facto global variables in the PicOS praxis must be turned into attributes of a Node object in the VUE2 model. This is because what looks like a complete program from the viewpoint of PicOS becomes merely a set of attributes and methods run by one node in the VUE2 program.

Conceptually, the idea behind the PicOS to VUE2 conversion is straightforward: PicOS threads are directly transformed into SMURPH processes run at stations representing network nodes. There are two types of variables referenced by such a process: local (automatic) variables of the process (i.e., ones allocated on the stack that do not survive state transitions) and global (permanent) variables. The automatic variables can be mostly left alone, as they appeared in the original PicOS code. The global variables must be turned into attributes of a SMURPH station representing the particular node. It makes no difference whether they are static in a thread or explicitly global. C++ cannot tell the difference between the two kinds. Moreover, as the code of a PicOS thread will (quite mechanically) become the code method of a SMURPH process, all static declaration must be removed from it, as their interpretation would be quite different from that intended.

Let us consider a sample praxis that has been written with no regard for VUE2. We shall use it to illustrate the conversion process. You can find it in PICOS/Apps/VUE/ILLUSTRATION. Here is the complete code of this praxis as it once appeared in the app.c file (see app.c_original in ILLUSTRATION):

#include "sysio.h"
#include "tcvphys.h"
#include "ser.h"
#include "serf.h"
#include "form.h"
#include "phys_dm2200.h"
#include "plug_null.h"

#define	MAX_PACKET_LENGTH	60
#define	IBUF_LENGTH	82

int	sfd;
word	Count;

void show (word st, address pkt) {

ser_outf (st, "RCV: %d [%s] pow = %d qua = %d\r\n",
Count++,
(char*)(pkt + 1),
((byte*)pkt) [tcv_left (pkt) - 1],
((byte*)pkt) [tcv_left (pkt) - 2]
);
}

#define	RC_TRY	0
#define	RC_SHOW	1

thread (receiver)
  static address packet;
  entry (RC_TRY)
packet = tcv_rnp (RC_TRY, sfd);
  entry (RC_SHOW)
show (RC_SHOW, packet);
tcv_endp (packet);
proceed (RC_TRY);
endthread

word plen (char *str) {

word k;
if ((k = strlen (str)) > MAX_PACKET_LENGTH - 5) {
str [MAX_PACKET_LENGTH - 4] = '\0';
k = MAX_PACKET_LENGTH – 5;
}

return (k + 6) & 0xfe;
}

#define	SN_SEND	0

strand (sender, char)
  address packet;
  entry (SN_SEND)
packet = tcv_wnp (SN_SEND, sfd, plen (data));
packet [0] = 0;
strcpy ((char*)(packet + 1), data);
tcv_endp (packet);
finish;
endstrand

#define	RS_INIT	0
#define	RS_RCMD_M	1
#define	RS_RCMD	2
#define	RS_RCMD_E	3
#define	RS_XMIT	4

thread (root)
  static char *ibuf;
  entry (RS_INIT)
ibuf = (char*) umalloc (IBUF_LENGTH);
phys_dm2200 (0, MAX_PACKET_LENGTH);
tcv_plug (0, &plug_null);
sfd = tcv_open (NONE, 0, 0);
tcv_control (sfd, PHYSOPT_TXON, NULL);
tcv_control (sfd, PHYSOPT_RXON, NULL);
if (sfd < 0) {
diag ("Cannot open tcv interface");
halt ();
}
runthread (receiver);
  entry (RS_RCMD_M)
ser_out (RS_RCMD_M,
"\r\nRF S-R example\r\n"
"Command:\r\n"
"s string -> send the string in a packet\r\n"
);
  entry (RS_RCMD)
ser_in (RS_RCMD, ibuf, IBUF_LENGTH-1);
if (ibuf [0] == 's')
proceed (RS_XMIT);
  entry (RS_RCMD_E)
ser_out (RS_RCMD_E, "Illegal command\r\n");
proceed (RS_RCMD_M);
  entry (RS_XMIT)
runstrand (sender, ibuf + 1);
proceed (RS_RCMD);
endthread

Illustration 1: A sample PicOS praxis.

Note that certain steps to improve its VUE2 compliance have already been taken (operations thread, strand, and so on). In the first step, we should make sure that there are no implicitly global variables declared in the threads, like the ones highlighted in the above code. Consequently, we shall remove them from the threads and put them in front, together with other global declarations:

...
int	sfd;
word	Count;
...
address r_packet;	// Used to be static at receiver
char *ibuf;	// Used to be static at root
...
thread (receiver)
  entry (RC_TRY)
r_packet = tcv_rnp (RC_TRY, sfd);
  entry (RC_SHOW)
show (RC_SHOW, r_packet);
tcv_endp (r_packet);
proceed (RC_TRY);
endthread
...
thread (root)
  entry (RS_INIT)
...

Illustration 2: Eliminating static declarations from threads.

In some cases, a static variable removed from a thread header may have to be renamed to avoid overlaps with similar variables declared in other threads. As packet seems to be a rather popular name for a variable, we have done so in the above example. Note that the automatic declaration of packet in the sender strand is left as it was.

## Beginning the conversion

In essence, a praxis looking like the one in Illustration 1, with the modifications shown in Illustration 2, can be converted to VUE2 mechanically. Here is one way to do it described step-by-step. While presenting those steps, we will be digressing into detailed explanations of the underlying issues and their solutions. Note that what truly matters is the “spirit” of the conversion, i.e., once you realize what needs to be done, your favorite way of rendering a praxis VUE2 compliant may differ in details. In particular, the exact names and structure of the files introduced in this process need not strictly follow our prescription.

Step 1: Create a file named threadhdrs.h in the praxis directory. The role of this file will be to assure the formal compatibility of threads for each of the two platforms. It will be included from app.c (and possibly other praxis files that define threads). In our case, this file may look like this:

#ifndef __praxis_threadhdrs_h__
#define __praxis_threadhdrs_h__

#ifdef	__SMURPH__

process THREADNAME (receiver) (Node) {
address r_packet;
states { RC_TRY, RC_SHOW };
perform;
};

process THREADNAME (sender) (Node) {
char *data;
states { SN_SEND };
void setup (char *d) { data = d; };
perform;
};

process THREADNAME (root) (Node) {
char *ibuf;
states { RS_INIT, RS_RCMD_M, RS_RCMD, RS_RCMD_E,RS_XMIT };
perform;
};

#else /* PicOS */

// ======================================
#define	RC_TRY	0
#define	RC_SHOW	1
address r_packet;
// ======================================
#define	SN_SEND	0
// ======================================
#define	RS_INIT	0
#define	RS_RCMD_M	1
#define	RS_RCMD	2
#define	RS_RCMD_E	3
#define	RS_XMIT	4
char *ibuf;

#endif /* SMURPH or PICOS */
#endif

Illustration 3: The contents of threadhdrs.h.

The idea is that with this file in front of a thread code, that code will be interpreted correctly by PicOS as well as SMURPH. The constant __SMURPH__ can be used as a general and authoritative way of telling whether a piece of code is being compiled by VUE2 or by the PicOS compiler.

The sequence of process statements turns the praxis threads into SMURPH processes. The actual name of the process (as seen by SMURPH), may slightly differ from the PicOS name. The responsibility of the THREADNAME macro is to properly adjust this name in those circumstances when an adjustment is required. To see the problem, suppose that different PicOS praxes are combined into a single VUE2 model. When those praxes are handled by the PicOS compiler, they are completely independent, in the sense that the name spaces of their threads are disjoint and do not interfere. However, when the same praxes are combined into a single SMURPH program, we have to eliminate potential name overlaps. For example, two praxes may use the name sender for their private variants of some thread.[5] This issue only becomes relevant when the model consists of multiple praxes (we shall return to it later). In the present case, we could simply remove the macro and, instead of:
[5] Note that processes in SMURPH are not station methods, and the names of their types are global.
process THREADNAME (receiver) (Node) {

simply say:

process receiver (Node) {

However, obeying this convention in all praxes makes their VUE2 incarnations independent and easily re-combinable into compound models.

Those variables that, according to the PicOS view, are local to threads but permanent (i.e., were declared as static within a thread scope in the very first version of the praxis code) can be safely turned into process attributes in the SMURPH version (as shown in Illustration 3). This is not the only solution: they can also be treated as straightforward global variables, as they de facto are in the PicOS incarnation of the code. From the viewpoint of SMURPH, their interpretation as process attributes may be more methodologically correct. Whatever variables you decide to view this way, their global declarations must appear in the PicOS part of threadhdrs.h (the highlighted lines). The idea is that the file takes care of those things that are formally specific to the threads. Thus, for example, as r_packet is a process attribute in the SMURPH incarnation of the receiver thread, it should be mentioned as global in the PicOS section of the file.

Note that, as the sender process is a strand, i.e., it takes a private data object, its SMURPH variant must define the data attribute, whose pointer type must agree with the type specified as the second argument of the respective strand declaration (page 8). This attribute must be initialized from the setup argument when the process is created.

Step 2: Create two files named node.h and node.cc. The first of them should look like this:

#ifndef __praxis_node_h__
#define __praxis_node_h__

#include "board.h"
#include "plug_null.h"

station Node : NNode {

#include "attribs.h"
#include "starter.h"

void setup (data_no_t*);
void _da (reset) ();
void init ();
};

Illustration 4: The contents of node.h.
#endif

Its role is to establish a link between the praxis and the SMURPH station (node) that will be running it. This file is only used by VUE2 (the PicOS compiler never looks at it). Its contents are pretty much praxis-independent and can be viewed as a standard incantation, except for the parent type for Node (NNode in the above variant). VUE2 provides a collection of standard node types equipped with some predefined features. For example, NNode stands for a node running the NULL plugin for VNETI (NULL Node). Other parent node types are TNode (for TARP Node) and PicOSNode, which is the most generic node type acting as the base type for all other nodes.

The two files included within the Node station specify the node contents (its attributes). The first of them, attribs.h, must be present in the praxis directory. It links the global variables and functions of the praxis to the node, such that they become its attributes instead of being global, as in the PicOS incarnation. The second file, starter.h, comes from the VUE2 library. It introduces a single method, named appStart, which is needed to start up the node (corresponding to powering on a physical node).

The three methods of Node announced in node.h are defined in node.cc, which in our case may look as follows:

#include "node.h"

void Node::setup (data_no_t *nddata) {
PicOSNode::setup (nddata);
NNode::setup ();
init ();
}
void Node::init () {

#include "attribs_init.h"
appStart ();
}
__PUBLF (Node, void, reset) () {
NNode::reset ();
init ();

Illustration 5: The contents of node.cc.
}

Again, the contents of this file are directly applicable “as-is” to many praxes. The setup method of Node is called by SMURPH when the node is created, and formally its role is that of a constructor. Its argument represents a standard package of data describing a PicOS node, which will be discussed later. This package is passed to the setup method of PicOSNode. This method is called only once during the virtual life of the node. Any praxis-specific initialization should be put into the init method, which is also called on every (virtual) reset. The file attribs_init.h (which should be present in the praxis directory) will provide the initialization code for those praxis-specific attributes of Node that must be initialized on every reset.

The file also defines (somewhat cryptically) the reset method for Node. The method says that upon reset, the NNode component should be reset (that component will make sure to reset any lower level components in the inheritance chain), and then Node's init should be called to restart the praxis. The way the reset method is defined is characteristic of those Node methods that must be directly accessible from the praxis threads. As this problem is general, and it affects a large portion of the overall thread interface to VUE2, it calls for a detailed explanation.

## Referencing PicOS functions and variables in VUE2 models

Suppose that a PicoS thread calls some function, e.g., the receiver thread calling tcv_rnp in Illustration 1. In the PicOS incarnation of the program, this is a global C function provided by the VNETI module. All (or at least the vast majority of) such functions must be turned into Node methods when the praxis is transformed into a VUE2 model. However, a SMURPH thread cannot reference Node methods directly: it must use a remote reference in the form of S–>tcv_rnp (...), where S points to the current Node at which the thread is run. Thus, if the PicOS functions were directly mapped into Node methods, the thread code would have to be modified in a way that would render it unusable to the PicOS compiler.

The trick played here consists in renaming those functions upon their conversion to Node methods and using the original names as macros that expand into the proper remote references. For example, the VUE2 incarnation of tcv_rnp (defined as a method of PicOSNode) is named _na_tcv_rnp. Then, there is a macro defined somewhat like this:

#define tcv_rnp(a,b) (((PicOSNode*)TheStation)->_na_tcv_rnp (a,b))

which converts the original reference to tcv_rnp to the new method. For all standard functions of PicOS modeled by VUE2 this scheme is already implemented. Unfortunately, any functions defined by the praxis (which cannot be truly global)[6] must be transformed manually for this trick.
[6] Some functions may actually be safe when left as global. This happens when they do not reference any non-automatic variables.

Thus, it is recommended that praxis functions be declared using one of these two macros (available in PicOS as well as VUE2):

__PUBLS(ot,tp,nam)
__PUBLF(ot,tp,nam)

The first argument is the node type to which the function belongs. Note that generally a VUE2 model may have to deal with multiple node types. The second argument is the function type, and the last one is the function name). Under VUE2, both macros expand in exactly the same way. For example, both:

__PUBLF (Node, void, myfun) (int a, word b) {
__PUBLS (Node, void, myfun) (int a, word b) {

are turned into

void Node::_na_myfun (int a, word b) {

while under PicOS, the expansions are:

void myfun (int a, word b) {
static void myfun (int a, word b) {

respectively. Note that static in front of a method declaration in C++ has a completely different meaning from a static function declaration in C.

By using the above macros for declaring all functions, the praxis will make itself independent of these issues and become VUE2 compliant while retaining its PicOS compatibility. Admittedly, this does require some effort. Note that not all functions need to be subjected to this transformation. A function that does not reference external variables (meaning Node attributes in its VUE2 incarnation) can be left alone. This in fact applies to both functions in Illustration 1, which can be simply left as global in the model.

To return to Illustration 5, the reason why reset is declared in the VUE2 compliant manner is that the praxis may want to call it explicitly. Indeed, reset is a legitimate standard operation in PicOS and the method in Illustration 5 plays exactly that role. Thus, when a thread executes reset ( ), it will reference that method.

The macros transforming standard PicOS operations into the respective methods (including the requisite remote access operator) are defined in file stdattr.h in VUEE/PICOS. Praxis program files must include that file (directly or indirectly) to have transparent access to those operations.

Note that the same problem concerns global variables. While under PicOS every thread can reference such variables directly, they must be accessed remotely as Node attributes in the VUE2 model. The only difference with respect to functions is that there are virtually no “standard” (predefined) variables in PicOS that a praxis thread would want to access,[7] and the problem is practically confined to the variables declared by the praxis.
[7] One exception is entropy (perhaps it should be replaced by a function). Also RF drivers reference some standard attributes like statid or backoff, but from the viewpoint of VUE2, these attributes are not part of the platform-independent praxis code.

Nonetheless, global variables cannot be referenced directly from a VUE2 compliant thread, and essentially the same trick must be applied here as in the case of functions. Let us have a look at the following macros:

#define _da(a)	_na_ ## a
#define _dac(a,b)	(((a*)TheStation)-> _na_ ## b)

The above definitions apply to VUE2. Here is how the same macros are defined in PicOS:

#define _da(a)	a
#define _dac(a,b)	b

The VUE2 compliant way to declare a global variable is to use the _da macro, e.g.,

int _da (sfd);

This encapsulation has no effect under PicOS, but under VUE2 the declaration will expand into:

int _na_sfd;

which obfuscates the original name of the variable with a prefix. The idea is that the prefixed declarations will be inserted as part of the Node class declaration, and the prefixed variables will become Node attributes. To reference them, a (PicOS) process will use their original names, which become replaced with macros. Formally, the proper way to reference variable sfd in the above example is:

 ((Node*)TheStation)->_na_sfd)

and this is what sfd should expand into. The role of _dac is to provide a shortcut for such macro declarations. Thus, with this defintion:

#define sfd	_dac (Node, sfd)

sfd will expand into

((Node*)TheStation)->_na_sfd)

The first argument of the macro is useful in situations when the network model consist of nodes of multiple types.

Owing to the initialization problems, the declaration parts for global variables usually require separate code chunks for PicOS and VUE2, which renders the two macros (i.e., _da and _dac) rather useless under PicOS (see below).

Step 4: Create the file globals.h, which in our case may look like this:

#ifndef __praxis_globals_h__
#define __praxis_globals_h__

#ifdef	__SMURPH__

#define THREADNAME(a) a
#include "node.h"
#include "stdattr.h"

#define sfd _dac (Node, sfd)
#define Count _dac (Node, Count)
#define show _dac (Node, show)
#define plen _dac (Node, plen)

#else	/* PICOS */

#include "sysio.h"
#include "tcvphys.h"
#include "ser.h"
#include "serf.h"
#include "form.h"
#include "phys_dm2200.h"
#include "plug_null.h"

int	sfd;
word	Count;
heapmem {10, 90};

#endif	/* SMURPH or PICOS */
#endif

Illustration 6: The contents of globals.h.

In a sense, this file is complementary to threadshdr.h because it accounts for the global objects, i.e., ones to be visible by all threads. Again, it has two parts depending on whether it is being compiled under PicOS or VUE2. First, note the trivial definition of THREADNAME. As we said earlier, there is no need to “adjust” thread names in this case as our VUE2 model consist of a single praxis.

The SMURPH section of globals.h includes two files: node.h (which we saw before) and stdattr.h. The latter comes from the VUE2 library (directory VUEE/PICOS) and contains definitions of macros for referencing standard functions and attributes from praxis threads (see Section 4.2). That part is followed by a series of macros that play the same role as stdattr.h but for the global variables and methods defined by the praxis. Even though, as we noticed earlier, the two functions show and plen need not be turned into Node methods, let us do it anyway (it will do no harm) for the sake of illustration.

Note that the same macro _dac is applied to variables and functions. This may occasionally lead to a confusion because, for example, any occurrence of show as a token in the praxis code will be replaced by:

((Node*)TheStation)->_na_show)

not only when the token actually looks like a function call. There is a more foolproof, albeit also more complex, way to define such macros, i.e.,

#define show(a,b) (((Node*)TheStation)->_na_show (a,b))

(see macro tcv_rnp on page 12), which, as long as there are no conflicts, is an overkill.

The PicOS section of globals.h specifies the same include files as the original praxis code. It also explicitly declares those global variables from the original code that were not classified as process attributes in threadhdrs.h. Also, if there are any other items required by the PicOS incarnations of the praxis, but useless for the VUE2 model, that part of globals.h provides a placeholder for them.[8]
[8] In particular, the present version of VUE2 implements a single malloc memory pool (which is sufficient for all our present MSP430 praxes). Consequently, the heapmem declaration is not understood by VUE2 (yet).

Note that globals.h does not declare the global variables (or Node attributes) for the VUE2 model – it only makes them accessible to the threads. It does so, however, for PicOS. At first sight, it would seem natural to put all global declarations into a separate file, e.g.,

int	_da (sfd);
word	_da (Count);

and use the same file to describe Node attributes for the VUE2 model as well as the truly global declarations for PicOS. Unfortunately, we cannot really do it this way because of static initializations. The truly global declarations in PicOS may be statically initialized, e.g.,

int	sfd = -1;
word	Count = 0;

and even if they are not explicitly initialized, they still are initialized implicitly to zero. C++ does not allow us to insert variable declarations like this directly into class declarations. Moreover, there is no implicit initialization (to zero) of not explicitly initialized attributes. This means that there is no way to avoid a separation of the two parts: completely different statements are required in the two cases. Additionally, any truly required initialization (even the implicit initialization to zero) must be handled explicitly in the VUE2 case.

Step 5: Create two files: attribs.h and attribs_init.h to take care of the C++ declarations for global variables (page 11 shows where these files are inserted). They will only be read by the VUE2 compiler. The first file may look like this:

#ifndef __praxis_attribs_h__
int	_da (sfd);
word	_da (Count);
void	_da (show) (word, address);
word	_da (plen) (char*);
#endif

It will be directly inserted into the Node class. Note that the two global functions show and plen become Node methods. The second file contains the trivial code to initialize those attributes that must be initialized:

_da (Count) = 0;

As no initial value is assumed by the praxis for sfd, there is no need to initialize that attribute (but we have to know that).

Step 7: Perform some cosmetics with app.c. First, rename the file to app.cc to make it available to the VUE2 compiler. This suffix will be OK for PicOS: the compiler will first copy the file to app.c, compile it from there, and then discard the copy. Then remove from app.cc all includes and replace them with these two lines:

#include "globals.h"
#include "threadhdrs.h"

Note that for PicOS, globals.h now provides the previous headers. Also, remove from app.cc everything that has been put into the PicOS section of globals.h, i.e., the global declarations including heapmem.

Modify the headers of all those functions that become Node methods under VUE2. Use the macros introduced on page 12. Thus,

void show (word st, address pkt) { ...
word plen (char *str) { ...

become

__PUBLF (Node, void, show) (word st, address pkt) { ...
__PUBLF (Node, word, plen) (char *str) { ...

Remove the declarations of symbolic states (they have been moved to threadhdrs.h – see page 10). Finally, add this statement:

praxis_starter (Node);

as the last line of app.cc, following the closing endthread of the root process. This is an empty statement under PicOS, and under VUE2, it expands into:

void Node::appStart () { create THREADNAME (root); }

providing the appStart method (page  11) which is called upon reset to start the praxis model.

Step 8: Create one more file, named root.cc, to provide the SMURPH program with a Root process. Do not confuse it with the praxis root thread. That file may look like this:

#include "node.h"
#include "board.cc"

process Root : BoardRoot {
void buildNode (const char *tp, data_no_t *nddata) {
create Node (nddata);
};
};

Illustration 7: The standard contents of root.cc.

This is the place where the execution of the entire model will commence. The actual code of the Root process comes from the VUE2 library (type BoardRoot) and the present declaration only specifies one (virtual) method needed to instantiate a single node of the model. The first argument of buildNode is used to identify the node type (through a textual name) in those scenarios when the model consists of several different node types. This argument is ignored in our case. The second argument points to a standard data structure containing the node parameters extracted from the data file. There is no need to interpret these parameters: they are simply passed to Node's setup method (page 11), which in turn will convey them to PicOSNode constructor.

To see how the conversion has worked, move to PICOS/Apps/VUEE/ILLUSTRATION and execute mkmk VERSA2 followed by make. This will compile a PicOS version of the praxis creating two image files Image and Image.a43. Then execute vuee in the same directory. This will create an executable VUE2 model of the praxis in the file named side.[9]
[9] It is side.exe under Cygwin.

# Models involving multiple praxes
See PICOS/Apps/VUEE/TNP, which is a combination of two PicOS praxes called Tags and Pegs. In a nutshell, the idea is to have two separate sets of the files described in Section 4. The names of those files are tagged with suffixes _tag and _peg, depending to which praxis they belong. The separation is in fact perfect (such that except for renaming the files, the conversion can be carried out exactly as for a single-praxis model) up to the rather trivial place where the two praxes are linked together to constitute a single SMURPH program. This part consists of two files: common.h and root.cc.

The first file (Illustration 8) announces two functions that are to be called to set up a node from a given praxis. In particular, buildTagNode is the Tag's equivalent of Root's method buildNode from page 17. This time, to keep the praxes separated (and to minimize the amount of shared code), we prefer to have a transparent function (rather than a method) for each praxis, such that the Root process need not be aware of the layouts (types) of their nodes. This way, we can separate the two praxes completely. In the single place where they meet, there is no need to mention anything about the types of their objects, and they are referenced solely by global functions. The trivial contents of such a function (see node_tag.cc) are of course:

void buildTagNode (data_no_t* nddata) {
/*
* The purpose of this is to isolate the two applications, such that
* their specific "type" files don't have to be used together in any
* module.
 */
create NodeTag (nddata);
}

which is essentially what we saw in the single praxis case (Illustration 7). The root.cc file is shown in Illustration 9. The file provides a definition for the same virtual method of BoardRoot as the single-praxis file in Illustration 7. This time we take advantage of the type argument to decide which node type is being created. As we shall see, boardRoot is called internally (by the Root process) as many times as many nodes belong to the modeled network. Node specifications in the data file can use textual identifiers to differentiate among multiple node types.

#ifndef	__tnp_common_h__
#define	__tnp_common_h__

#include "sysio.h"
#include "board.h"

void buildTagNode (data_no_t*);
void buildPegNode (data_no_t*);

#endif

Illustration 8: The connecting header file for Tags and Pegs.

#include "common.h"
#include "board.cc"

process Root : BoardRoot {
void buildNode (const char *tp,	data_no_t *nddata) {
if (strcmp (tp, "tag") == 0)
buildTagNode (nddata);
else if (strcmp (tp, "peg") == 0)
buildPegNode (nddata);
else
excptn ("Root: illegal node type: %s", tp);
};
};

Illustration 9: The SMURPH root program for Tags and Pegs.

The Tags and Pegs (TNP) model is considerably more complicated than the simple ILLUSTRATION discussed in Section 4, as it implements two complete and fully functional praxes involving TARP and VNETI. Each of them consists of multiple source files. Note that the source code of TARP (PicOS/Libs/LibComms) has been rendered VUE2 compliant, such that it is effectively shared between PicOS and VUE2.

# Input data

The input data file parameterizing a VUE2 model follows an XML format. Below is a complete sample data file describing a three-node network:

<network nodes="3">
    <grid>0.1m</grid>
    <channel>
        <shadowing bn="-110.0dBm" syncbits="8">
RP(d) = received power at distance d
XP = transmitted power
X = lognormal random Gaussian component
 =======================================================
RP(d)/XP [dB] = -10 x 3.0 x log(d/1.0m) + X(1.0) - 38.0
 =======================================================
</shadowing>
<cutoff>-120.0dBm</cutoff>
<ber>
Interpolated ber table:
======================
 SIR	BER
50.0dB	1.0E-6
40.0dB	2.0E-6
30.0dB	5.0E-6
20.0dB	1.0E-5
10.0dB	1.0E-4
5.0dB	1.0E-3
2.0dB	1.0E-1
0.0dB	2.0E-1
-2.0dB	5.0E-1
-5.0dB	9.9E-1
</ber>
<frame>9600 12 0</frame>
<rssi mode="log,transform">-202.0 0 53.0 255</rssi>
<power mode="log,interp">
-30.0dBm	0
-15.0dBm	1
-10.0dBm	2
-5.0dBm	3
 0.0dBm	4
 5.0dBm	5
 7.0dBm	6
10.0dBm	7
</power>
    </channel>
    <nodes>
<defaults>
   <memory>1124 bytes</memory>
   <power>
transmitter power	10.0dBm
receiver boost	0.0dB
   </power>
   <preamble>32 bits</preamble>
   <lbt>
delay	8msec
threshold	-109.0dBm
   </lbt>
   <backoff>
min	8msec
max	303msec
   </backoff>
   <uart rate="9600" bsize="12">
<input source="socket"></input>
<output target="socket" type="held"></output>
   </uart>
</defaults>
<node number="0">
   <location>1.0 4.0</location>
    <preinit tag="ESN" type="lword">0x8000ff01</preinit>
</node>
<node number="1">
   <location>1.0 10.0</location>
</node>
<node number="2">
   <location>1.0 10.0</location>
</node>
    </nodes>
    <roamer>
<input source=”string”>
R 2 [1.0 1.0 21.0 24.0] [0.5 1.8] [1.0 6.0] -1
</input>
    </roamer>
</network>

Illustration 10: A sample data file.

Each data file describes a single <network>. The mandatory attribute of the <network> element specifies the total number of nodes (of all types). This number remains fixed during the execution, but the nodes may exhibit highly dynamic behavior including mobility.

One more (optional) attribute of <network> is port, which can be used to assign a non-standard port number to the socket opened by the program for connections from agents (see Section 8).

Some input elements include numbers. Typically, besides numbers, such an element may include non-numeric text, which is ignored (treated as a comment). For example, the only relevant items from the <shadowing> element in <channel> are the numbers -10, 3.0 ,1.0, 1.0, 38.0. Also, any non-numerical characters in the otherwise numerical arguments of elements (like the letters dBm in "-110.0dBm") are ignored. Thus, the equivalent comment-free specification of <shadowing> is:

<shadowing bn="-110.0" syncbits="8">-10 3.0 1.0 1.0 38.0</shadowing>

Note that the minus sign apparently preceding 38.0 has been ignored: this is because of the space separating it from the first digit.

In the subsequent sections, we shall discuss the sub-elements of <network>.

## Grid

This optional element has no arguments, and its text must include a single (floating point) number. This number specifies the granularity (in meters) of the coordinate grid for node deployment and movement. By default, the value of grid is 1.0, which means that node location will be rounded to full meters. This parameter directly determines the discrete granularity of virtual time in SMURPH (the ITU), which is equal to the amount of time required for a radio signal (propagating at 299,792,458 m/s) to cross the grid unit.

## Channel

This element describes a radio channel. It is mandatory, which means that a VUE2 model requires a radio channel (and at least two nodes). It is anticipated that the population and format of sub-elements of <channel> will expand as new types of channel models are added to the library. The element itself takes no arguments, and the exact characteristics of the channel are described by the sub-elements. The only channel model available at present is shadowing, whose propagation properties are described by two numerical arguments of the <shadowing> element and five numbers that must occur in its body. Argument bn specifies the assumed level of background noise in dBm, and syncbits is the minimum number of correctly received preamble bits that a receiver must perceive in front of a recognizable packet. Both arguments are required (they have no defaults).

Signal attenuation in the shadowing channel model is described by the following formula:

left[ {P_r(d)}over{P_r(d_0)} right]_{dB} = -10 %beta log left( d over {d_0} right) + X (%sigma_dB)

where P_r(x) is the received signal level at distance x , d_0 is a (intentionally small) reference distance, %beta is the loss exponent and X is a Gaussian random variable with zero mean and standard deviation of %sigma_{dB} . For our purpose, we transform the formula to give us signal attenuation at distance d, which we can directly plug into the respective assessment method in SMURPH:

left[ {P_r(d)}over{P_x} right]_{dB} = -10 %beta log left( d over {d_0} right) + X (%sigma_dB) - L(d_0)

where P_x is the transmission power and L(d_0) is the calibrated loss at the reference distance d_0 . This formula is is only meaningful when d > d_0 . It is tacitly assumed that transmission at a shorter distance incurs the same attenuation as a transmission at the reference distance d_0 . This is exactly the formula from the <shadowing> element on page 19, i.e.,

RP(d)/XP [dB] = -10 x 3.0 x log(d/1.0m) + X(1.0) – 38.0

with the parameter values: %beta = 3.0 , d_0 = 1.0m , %sigma_{dB} = 1.0 and L(1m) = 38dB . This formula is used do determine the signal level at a receiving node N_r .

The <cutoff> element specifies a single floating point number interpreted as the so-called cut-off signal level in dBm. This is a threshold for the received signal level below which it can be safely assumed that there is no signal at all. This value is used to calculate the cut-off distance restricting the population of neighborhoods in the model, which may impact the execution speed. This element is mandatory.

All signals arriving from multiple transmitters within the cut-off range of N_r combine additively. The SIR of a single signal perceived by N_r is equal to the value of that signal level at N_r divided by the sum of all the other signals arriving at N_r augmented by the ubiquitous background noise (the bn argument of <shadowing>). Then, the table from the <ber> element is consulted to determine the probability of a bit error. That table is an array of numbers occurring in pairs. The numbers in the first column must be decreasing, while those in the second column must be non-decreasing (normally they are increasing). This is a discrete specification of a function that translates the signal to interference ratio (SIR) at the receiver into a bit error rate (BER), i.e., the probability that a single bit is received in error. The smooth BER function for all possible values of SIR is obtained by interpolating the table. If the SIR is greater than or equal to the first value in the table, then the bit error rate is determined by the first entry (for example, it never decreases below 10^{-6} in the channel described in Illustration 10). If it less than the last value, then the bit error rate is 1, i.e., reception is impossible.

The bit error rate applies to the so-called “physical bits,” which are also used in determining the effective transmission rate. The three numbers within the <frame> element stand for the bit rate, bits per byte, and the number of extra bits needed to frame a complete packet. The rate parameter determines the number of physical bits transmitted per second. The second parameter of that element translates physical bits into logical bits by indicating the number of physical bits in one byte (octet). This mapping accounts for the encoding, e.g., 6-bit symbols encoding 4-bit nibbles. The last parameter (also expressed in physical bits) covers any special (non-preamble) components of the frame that are invisible to the receiver software but contribute to the overall length of a transmitted and received packet, e.g., a start symbol.

Refer to the SMURPH manual for an explanation of the dynamics of the interference model. The assessment method responsible for detecting the beginning of a packet at a receiver (RFC_bot) checks if at least syncbits (physical) bits of the preamble (see page 19) immediately preceding the first bit of the actual packet have been received without an error, according to the bit error rate calculated as explained above. The second assessment method (RFC_eot), determining the final success of a packet reception, is not used in the channel model. Instead, the receiver invokes RFC_erd to await the first bit-error event in the packet. The (reasonable) simplification assumed in the model is that the first error bit will render its symbol invalid, which will interrupt the reception. This is warranted by the fact that all the legitimate symbols used by DM2200 (and most other RF modules) have the property that flipping a single bit renders the symbol invalid.

Clearly, the <channel> element describes a bit more than just the radio channel. Some of the parameters there are related to the characteristic of the RF modules used by the nodes. Although, arguably, it might make sense to associate those attributes with individual transceivers (and this may happen in the future), the present description favors networks based on the same (or similar) equipment used by all nodes (at least within the realm of a single “channel”). It is possible to have multiple channels possibly interfaced by nodes acting as gateways.

Owing to the fact that all RF drivers in PicOS share practically the same logical structure, it makes sense to encapsulate their hardware-specific properties into parameters that can be set in the input data file. This way, functions like phys_cc1100, phys_dm2200 point to essentially the same driver model, while the proper setting of the channel parameters in the input data should bring that model close to the intended hardware.

Two sub-elements of <channel>, <rssi> and <power>, describe the way of transforming the received signal strength into RSSI indications (appended at the end of a received packet), and the correspondence between the power level set by the praxis (via PHYSOPT_SETPOWER) and the actual transmitter power level resulting from that setting. Note that not all RF modules have the requisite capabilities. Thus, if no <rssi> element occurs within <channel>, no RSSI indications will be returned to the praxis (the corresponding packet byte will be always zero). Similarly, if there is no <power> element, PHYSOPT_SETPOWER will be ineffective.

The two elements have similar definitions. Let us start with <rssi>. The optional mode attribute consists of up to two strings separated with a comma. These strings can be independently: logarithmic or linear and transform or interpolate, with possible abbreviations down to log versus lin and tra versus int. With transform (as opposed to interpolate), the element body must contain four numbers, which are interpreted as:

- the lowest received signal level L_min to be convertible to an RSSI indication
- the indication value V_min corresponding to that lowest signal level
- the highest received signal level L_max to be convertible to an RSSI indication
- the indication value V_max corresponding to that highest signal level

For an arbitrary value L of the received signal level between the minimum and maximum, i.e., (L_min <= L <= L_max) , the presented RSSI will be calculated as:

 V(L) = V_min + ( L-L_min ) times {{V_max – V_min} over {L_max – L_min }} ,

i.e., through a straightforward linear transformation. If the received signal level ever happens to be lower than L_min , the indication will be V_min ; if it is higher than L_max , the indication will be V_max .

The role of the second attribute (logarithmic versus linear) is to tell whether the specified signal levels are linear (in milliwatts) or logarithmic (in dBm). For example, the specification

<rssi mode="log,transform">-202.0 0 53.0 255</rssi>

from Illustration 10 assigns the value 0 to the signal level –202.0 dBm and 255 to the signal level of 53.0 dBm. These description corresponds to the actual RSSI calculation for CC1100, where the logarithmic received signal level is linearly transformed into values between 0 and 255.

With interpolate instead of transform, the element body is expected to provide an interpolation table, similar to <ber>, consisting of an even number of values. The first value of every pair is the floating point signal level, and the second value is the corresponding integer RSSI value. Both sequences of values must be monotonically increasing, e.g.,

<rssi mode="log,int">
-202.0 0
-150.0 30
-100.0 50
-50.0 70
  0.0 128
 40.0 167
 50.0 180
 70.0 222
</rssi>

The indication for a signal level not explicitly mentioned in the table is determined by (linear) interpolation, assuming that anything less than the minimum (or greater than the maximum) maps to the minimum (or to the maximum). Again, with int instead of log, the specified signal values are interpreted as being linear.

If the mode attribute is missing, the two strings default to logarithmic and transform. These are also their independent defaults assumed in the case when only one string is present.

For <power>, the interpretation of the mode attribute and the numbers occurring within the element body is similar. This time, the conversion is carried out in the opposite direction, i.e., integer specifications of power level are converted to floating point transmit power levels assigned to the transceiver. For example, the specification from Illustration 10:

<power mode="log,interp">
-30.0dBm	0
-15.0dBm	1
-10.0dBm	2
-5.0dBm	3
 0.0dBm	4
 5.0dBm	5
 7.0dBm	6
10.0dBm	7
</power>

follows the CC1100 driver, with 8 discrete power levels (the interpolation is trivial in this case as all the settable levels are mentioned in the table) transformed into specific signal levels in dBm.

## Nodes

This element describes the configuration of nodes in the network. Each of its sub-elements, except <default>, provides a set of parameters for one specific node. The expected contents of <defaults> are the same as for <node> and describe the default setting of parameters for all nodes. If a given parameter is not explicitly mentioned within a <node> element, its <default> setting is assumed for the respective node.

A <node> item requires one argument, which is the node number. The node numbers are internal SMURPH identifiers of the stations implementing the nodes. The numbering of nodes must be continuous and start from zero. The total number of node definitions (<node> elements) in a data set must be equal to the nodes argument of <network> (page 19). Each node number from 0 to nodes–1 must occur exactly once among <nodes>, not necessarily in any particular order.

Here is the list of sub-elements of <node> (and also <defaults>). The nontrivial elements are discussed later in separate sections.

<memory> ... memory size in bytes ... </memory>

This element declares the amount of memory (standard RAM) available at the node for malloc. This is equal to the physical size of RAM at the microcontroller minus the combined size of global variables (with provision for alignment). PicOS reports this amount upon startup as the so-called leftover RAM.

<power> ... xmt power ... rcv boost ... </power>

The element provides two floating point numbers: the default transmitter power and the receiver sensitivity (or receiver boost). The interpretation of these numbers is up to the channel model. Generally (and in particular for the shadowing channel model) the transmitter power is in dBm and the receiver boost is in dB. The received signal is multiplied by the boost at the receiver before its assessment, thus, the boost of zero dB can be viewed as “normal”. Note that this element is different from the <power> element occurring within <channel>. It selects the default setting of the transmitter power after node reset.

<preamble> ... preamble length in physical bits ... </preamble>

This element specifies the packet preamble length in physical bits to be inserted by the node's transmitter in front of every packet.

<lbt> ... delay ... threshold ... </lbt>
<backoff> ... minimum ... maximum ... </backoff>

These parameters (four numbers) are used by the collision avoidance procedure of the node's transmitter. For <lbt> (Listen Before Transmit), the first (integer) number gives the time interval (in milliseconds) during which the transmitter will pause before a spontaneous transmission while monitoring the signal level. If the level is above the threshold (in dBm), the transmitter will back off randomly and try again. The back-off delay is between the minimum and maximum specified in the <backoff> element (both numbers are in milliseconds and must be integers).

All the above sub-elements are mandatory in the sense that each of them must appear either among the elements of <node> or, if absent there, its <default> version will be assumed. A situation when neither <node> nor <default> provide the parameter is treated as an error.

One special mandatory element is:

<location> ... x ... y ... </location>

which must be present in every <node> and makes no sense (is ignored) in <default>. It assigns an initial location to the node as a pair of coordinates in meters (floating point numbers). The coordinates can be arbitrary as long as they are non-negative. Nodes can only be deployed in the right upper quarter of the infinite Cartesian plane.

The following <node> sub-elements are optional: <uart>, <pins>, <leds>, <preinit>. They first three augment the nodes with optional components (like UARTs), which can be legitimately absent. The last one provides a way of initializing selected node attributes. All these elements are discussed below, each in a separate section.

## The UART

Each node may be optionally equipped with a UART, whose functionality, as perceived by the praxis, accurately mimics the functionality of a standard UART accessible with the io operation of PicOS. The UART description in the input data assigns a bit rate to the UART, declares the sizes of two buffers to be used by the modeled driver, and determines what happens to the output and where the input will be coming from. The first three values are provided as attributes of <uart>, e.g.,

<uart rate="9600" bsize="12,8">

with the rate attribute being mandatory and bsize being optional. The first of the two bsize numbers gives the length of the input buffer,[10] and the second one declares the size of the output buffer. The default buffer size is 0 (in both cases), which effectively corresponds to “no buffer.”[11] This is assumed for both buffers, if no bsize attribute is present in <uart>, or for the output buffer, if only one number is provided, e.g.,
[10] This corresponds to a compilation parameter for PicOS.
[11] In fact a single-byte buffer is used by the model in that case, which corresponds to the hardware UART register on the microcontroller. This has the same meaning as the buffer size of zero in PicOS. Also, the MSP430 UART driver in PicOS uses 0 for the output buffer size (there is no parameter to change that.

<uart rate="9600" bsize="12">

The UART's interface to the real world is described by the <input> and <output> elements. The options are:

Local file or device:

<input source=”device”>device or file name</input>
<output target=”device”>device or file name</output>

The body of each element is stripped of any initial and trailing white spaces and the remainder is interpreted as a file name path relative to the directory where the model (the side program) has been invoked.

If the names in fact refer to files, than they should be different to make sense. On the other hand, they may represent the same device, e.g., a TTY terminal window. In that case, the UART may directly interact with the user.

The (input) characters arriving from a file/device, as well as those written by the praxis to the UART and sent to a file/device, are not preprocessed in any way (using the UNIX terminology, we would say that the interface is “raw”). The assumed interpretation of lines in PicOS, for the ASCII-oriented UART access functions ser_out, ser_outf, ser_in, ser_inf, is that an output line ends with CR+LF, and an input line must end with at least one of those characters, with any sequence of CR and/or LF characters at the end interpreted as a single end of line.

Both <input> and output elements accept an optional coding attribute, which can be “hex” or “ascii”, with “ascii” being the default, e.g.,

<input source=”device” coding=”hex”>

With the “hex” coding, the input is assumed to be a sequence of bytes expressed as pairs of hexadecimal digits. Whenever a next byte is read from the UART, the emulator will look up in the file the next character looking like a hexadecimal digit (skipping all other characters). Then, if the following character is also a hexadecimal digit, the two will be decoded into a byte and returned as the read character. Otherwise, the program will be aborted with an error message. For output, the “hex” coding produces a sequence of 2-digit hexadecimal representations of the output bytes separated by spaces.

The <input> element accepts an optional type attribute, whose value can be “timed” or “untimed”, with the latter being the default, e.g.,

<input source=”device” type=”timed”>

For the “timed” type of input, the input file must be organized into records looking like this:

time { input data }

where time is a floating point number describing the time when the record will become available for input. If preceded by a '+' sign, the number describes the interval in seconds from the availability time of the previous record (or from 0 if the record starts the input sequence). If there is no '+', the number represents the absolute time in seconds from the beginning of run (time 0). If the time has already passed when the record is looked at by the system (i.e., the processing of previous records took more time than the record's availability time), the record becomes available immediately.

Once a record becomes available, its characters will arrive at the UART at the nominal rate specified in the <uart> element. If the praxis does not retrieve them on time, they will be lost. This is different from the “untimed” (default) operation whereby the bytes to be read by the praxis patiently await acceptance. In that case, the UART rate only determines how often they can be extracted (the minimum space between characters), but they never arrive faster than the praxis can cope with them.

Here is an example of a timed input sequence:

5.0 {s 4096\r\n} +4.0 {r\r\n} 3600 {s 0\r\n}
The string within braces may not include a closing brace unless escaped with a backslash. Generally, any character can be escaped with a backslash (including the backslash itself, which must be escaped). The escapes \r, \n and \t are treated as special characters (the last one standing for a TAB). An explicit newline also stands for itself, i.e., is equivalent to \n.

The timed mode can be combined with “hex” coding, e.g.,

5.0 {73 20 34 30 39 36 0d 0a} +4.0 {72 0d 0a} 3600 {73 20 30 0d 0a}

is equivalent to the previous sequence under “hex” coding.

Short input sequence specified directly in the data file:

The source attribute of <input> can be “string”, e.g.,

<input source=”string”>a direct sequence of bytes</input>

This specification is most useful in those circumstances when the node expects some short input from the UART at the beginning, e.g., to initialize the praxis. Generally, if the input part of the UART file is reasonably short, it can be inserted directly into the body of the <input> element, e.g.,

<input source=”string”>s 4096\r\n</input>

Note that the output may still be assigned independently to a file/device. Also, the “string” source can be combined with “hex” coding and/or “timed” mode, e.g.,
<input source=”string” type=”hex” mode=”timed”>
5.0 {73 20 34 30 39 36 0d 0a}
+4.0 {72 0d 0a}
3600 {73 20 30 0d 0a}
</input>

Defining a <default> UART whose input is mapped to a file is usually not a good idea, even if it works in principle. This is because, for a large network, the multiple instances of the file being opened for different nodes may deplete the population of allowable file descriptors and crash the model. On the other hand, having a default UART with an immediate input string (say for a default initialization of all the nodes) makes perfect sense. The output part of such an UART can be legitimately left unspecified.

Remote association through an agent:

The most flexible option is to map the UART to a socket and make it possible for external agents to claim its input and output. This is accomplished by using “socket” for the source and target, e.g.,

<input source=”socket”></input>
<output target=”socket”></output>

Once you map one end (say input) to a socket, the other end (output) also becomes mapped to a socket (there is no way to map it differently). Thus, the second line in the above sequence is redundant (although harmless). It may may be needed, if some other attribute of the element must be included, e.g., coding=”hex”. A specification like this:

<input source=”device”>/dev/tty</input>
<output target=”socket”></output>

will result in an error.

The body of an <input> or <output> element specifying “socket” is always ignored. External agents connect to such a UART following a special protocol that identifies the node (see Section 8.2). Thus, there is no need to provide any more details at this stage. A socket input can also be “hex” and/or “timed”. A socket output can be “hex”. Additionally, an <output> element specifying target=”socket” may also include type=”held” among its attributes, e.g.,

<output target=”socket” type=”held”></output>

The meaning of this setting is that the initial output written to the socket is saved and will be presented to the agent upon its (first) connection. This way you can make sure that whatever the praxis writes to the UART is never lost. This is important because before an agent can connect to the socket, the model must be started; thus, if the node writes something to the UART immediately after startup, that output might be lost.

Partially mapped UARTs

A socket UART is flexible in the sense that an agent may connect to it and disconnect many times. If anything is written to the UART while no agent is connected to it (excepting the period preceding the first connection to a “held” socket), that output is discarded and lost. Then if the node tries to read something from a disconnected socket, it will simply receive no data. This is the same as if the real UART were disconnected from the device.

For a device-mapped UART (and also for a UART whose input end is mapped to a string), it is legal to leave one end unmapped. For example, when writing to a UART whose output end is unmapped (but the UART is present), the output will be absorbed by the UART and discarded. An attempt to read from a UART with no input end will never return any data, but is formally legal. On the other hand, if no UART is defined at all, any attempt to reference it for I/O will trigger an error and abort the model.

You can indicate explicitly that the particular end is unmapped by saying something like this:

<output target=”none”></output>

This is equivalent to simply skipping the specification. Note that a socket UART always defines two ends, even if only one end is explicitly mentioned in the declaration.

If a <node> element has no <uart> sub-element, but there is such a sub-element in <default>, then the <default> specification of UART will be assumed by the node. If the node wants to say explicitly that it has no UART, default or otherwise, the following declaration should be used:

<uart></uart>

This is the only variant of the <uart> element that requires no rate specification.

## The LEDS module

For a node equipped with LEDs, you can make their status traceable or presentable to external agents. Here is a sample declaration of the LEDS module within <node>:

<leds number=”4”>
<output target=”device”>led_status.txt</output>
</leds>

It says that the updates to the LEDs will be written to file led_status.txt. Each update takes one ASCII line beginning with the letter U (capital) and terminated with the newline character. The complete line looks like this:

U T F LLLLL ... LLL

where T is the time of the status change in seconds (a floating point number), F is 1 or 0, depending on whether the fast blink option is active or not (see PicOS operation fastblink), and each of the subsequent characters stands for the status of one LED from zero up (i.e., the length of the L...L string is equal to the number of LEDs). The values are: 0 – the LED is off, 1 – the LED is on, 2 – the LED is blinking. Here is an example:

U 10.325 0 0101

To make the LEDs status perceptible by external agents, use “socket” as the output target, e.g.,
<leds number=”2”><output target=”socket”></output></leds>

Having connected to the LEDS module via the socket interface, the agent will be receiving updates in the same format as when they are written to a file.

Note that a LEDS module description can be placed in <defaults>. It may not make a lot of sense to direct LEDs status updates of all nodes to the same file, but it is perfectly legal to declare that all nodes can have their LEDs inspected by an agent (target=”socket”). If no agent is connected to the module, changes in the LEDs status trigger no external actions. Upon a connection, the agent will receive the current status of the LEDs, and then it will be receiving updates for as long as it is connected.

Similar to UART, to explicitly say that a node has no LEDs (overriding the default), you can use this declaration:

<leds></leds>

Specifying zero as the number of LEDs has the same effect. In that case, the <output> specification is ignored if present.

## The PINS module

This module provides an external interface to the node's I/O pins, including ADC and DAC. The node-inflicted changes to the (output) pins can be sent to an agent or stored in a file. Similarly, external changes to the pin voltage can be submitted by an agent or read from a file, possibly along with their timing. Here is a sample declaration:

<pins total="10" adc="8" pulse=”1,2” dac=”6,7”>
<output target="device">pins_output0.txt</output>
<input source=”device”>pins_input0.txt</input>
<status>1111111111</status>
<values>0000000000</values>
<voltage>0.0 0.0 0.0 0.0 0.0 0.0 0.0 0.0</voltage>
</pins>

which is complex enough to illustrate all sub-elements that can contribute to <pins>. Except for the trivial declaration <pins></pins>, which explicitly states that the node has no PINS module, the total attribute of <pins> is required, and it specifies the total number of I/O pins in the module. If the adc attribute is present, it declares the number of pins capable of providing input to the analog-to-digital converter. That number cannot be larger than total. The ADC-capable pins constitute an initial subset of all pins.

The conventions assumed for identification and access to the pins are strongly related to the standard pin interface offered by PicOS (functions pin_read, pin_write, pin_read_adc, pin_write_dac, etc., including pulse monitor and notifier). Some familiarity with that interface will help you understand the ideas behind the PINS model.

If the PINS module is to be equipped with the pulse monitor, which requires two pins: the counter and the notifier, the numbers of those pins must be specified with the optional pulse attribute. They can be any pins, including ones capable of ADC/DAC operation. Then, if any pins should provide DAC output, their numbers can be specified with dac. Note that only some models of MSP430 offer this functionality, which is confined to two pins.

The role of <status> is to indicate whether any of the pins in the range 0 ... total-1 are absent, i.e., the range includes holes.[12] The status of each pin is described by a single binary digit in the string, with 1 standing for “present” and 0 for “absent,” with the leftmost digit corresponding to pin 0. If no <status> element appears within <pins>, it is equivalent to “all ones,” i.e., no absent pins. If the string is shorter than the number of pins, the unaccounted for pins are all present by default.
[12] Even though the pin numbering is purely logical (defined on the per-board basis), the numbering convention assumed in PicOS makes it possible to exclude some pins from the continuous range.

The <values> element assigns initial digital values to all pins, which can be 0 or 1. Note that this assignment is only meaningful if the praxis sets the pin to input. At this stage, the declaration is equivalent to pulling the physical pin down or up via a resistor. Note, however, that it can be changed dynamically through an agent or from an input file. If the specification is absent, the pin values default to all zeros. If the string is shorter than the number of pins, the unaccounted for pins are all pulled down (initialized to 0).

Similarly, <voltages> assigns predefined analog values to the ADC-capable pins – in the natural order. When such a pin is selected by the praxis for its ADC function, this is the constant voltage that will show up on the pin for conversion. Again, that voltage should be viewed as initial as it can be changed by an agent of from an input file. If the specification is absent, the voltage defaults to all zeros. If the number of items in the list is less than the number of ADC-capable pins, the unaccounted for pins are set to voltage 0.

The <input> and <output> specifications are similar to those for UART, albeit simpler because the elements take no attributes besides “source” and “target.” The “string” source option is also available. There is a way to set up timed scripts for configurations of pin values via explicit sequences in the input data.

An input command addressed to a pins module is an ASCII line starting with one of the letters T, P, D. A T command requests a delay before reading the next command. The letter must be followed by a non-negative floating point number optionally preceded by a sign, e.g.,

T 12.5
T +0.01

In the first case, the number indicates the absolute time in seconds at which the next command should be read and interpreted. If the model is already past that time, the next command is read immediately. In the second case, the specified delay in seconds is calculated from the current moment.

A P command sets the digital value of a single pin. The letter is followed by the pin number in decimal followed in turn by 0 or 1, e.g.,

P 12 0
P 0 1
P 14 1

A D command assigns a voltage to the specified pin. The letter is followed by the pin number and the discretized voltage as a number from 0 to 32767 (0x7FFF) corresponding linearly to 0 ... 3.3V.[13]
[13] No negative voltage is implemented at present (but probably will be later).

An integer number can be specified in decimal (in the natural way) or in hexadecimal preceded with 0x. Initial spaces preceding the command letter are ignored. Thus, for example, the following sequence of commands makes sense:

T 0.5
P 0xc 1
P 0 0x0
D 0xf 0x00ff
T 1.0
D 0xf 0x0000

An immediate input string (the source=”string” option) should look like the contents of a file with a series of input commands, with the command lines separated with explicit new lines or \n sequences, e.g.,

<input source=”string”>P 1 1\nP 2 1\nT 0.01\nP 2 0</input>

is equivalent to:

<input source=”string”>
P 1 1
P 2 1
T 0.01
P 2 0
</input>

The first new line (the one preceding the first command) in the second version is stripped off by the data parser. This is not very important as empty lines in the command sequence are always ignored.

If the <output> part of the interface is configured and active, every change in the status of a pin results in a message being written to the file or sent to the agent. At the very beginning of the output sequence, there will be one special message looking like this:

N tt an

and specifying the number of pins: tt is the total number of pins and an is the number of ADC-capable pins (as specified in the attributes of the <pins> element). This line is also sent as a first message to any agent connecting to the PINS module over a socket – immediately after the connection has been established.

An actual update message starts with the letter U (capital) and consists of the following four components:

1. The time in seconds (with millisecond granularity) followed by a colon.
2. The number of the affected pin.
3. The status of this pin (a single decimal digit).
4. The pin value.

Here we have a few examples:

P 16 8
U 24.556: 4 1 0
U 3600.120: 7 3 176
U 2365.667: 2 0 0

The pin status value is interpreted as follows:

0 – digital input pin
1 – digital output pin
2 – an ADC pin
3 – DAC pin number 0
4 – DAC pin number 1
5 – pulse monitor counter pin
6 – pulse monitor notifier pin

The output value for cases 5 an 6 is always zero. For cases 2, 3, 4, the value is a number between 0 and 32767 representing the voltage (it is the output voltage for status 3 and 4, and the input voltage for status 2). For cases 0 and 1, the value can only be 0 or 1.

When the output is directed to a file, it starts with an N message followed by the complete list of initial pin values. From then on, the full status of all pins can be determined by tracking the updates reflecting changes in the individual pins. In the socket case, whenever an agent connects to the module, it immediately receives an N message followed by the initial series of “updates” for all pins reflecting their current status and values.

## Pre-initialization

By pre-initialization we understand assigning initial values to some node attributes in a way that is conceptually different from the normal (dynamic or static) initialization in the node program. Intentionally, it corresponds to burning some characteristic values into the node's flash memory, e.g., serial numbers, that make the node unconditionally distinguishable from other nodes.

Pre-initialized values are represented in the input data as <preinit> elements, which can be sub-elements of <node> or <default>. Here is an example:

<preinit tag="ESN" type="lword">0x8000ff01</preinit>

The mandatory tag attribute assigns a name to the preinit. The second (optional) type attribute determines the object type, which can be:

lword	a 32-bit long integer value (signed or unsigned)
word	a 16-bit integer value (signed or unsigned)
string	a character string

These indicators can be abbreviated down to the initial letter. If the type attribute is absent, it defaults to word.

The element's body contains the value, which should agree with the type specification. For types lword and word, the value should be a decimal number (possibly signed) or a hexadecimal value (beginning with 0x). Regardless of its actual size, it will be truncated to the respective size of the object. For the string type, the body is simply viewed as a character string.

The way to reference a preinit in the praxis code is via this function (which is a method of PicOSNode – see page 11):

IPointer preinit (const char *tag);

which returns the preinit value represented by the tag. The generic output type must be cast to the proper object type.

The most natural place to put calls to the above function is file attribs_init.h (see page 16), which contains “static” initialization of node attributes, e.g.,

_da (ESN) = (lword) preinit (“ESN”);
_da (Greeting) = (char*) preinit (“WELCOME”);

If the tag referenced by preinit is not found among the <preinit> elements associated with the current node, the function consults the preinits of <defaults>. If it is not found there, the function returns zero, i.e., the object is initialized to zero (or to a NULL string pointer). This corresponds to leaving the object uninitialized in the real world.

# Mobility drivers

The underlying SMURPH/SIDE vehicle allows the programmer to create arbitrarily elaborate mobility models as external SMURPH processes. VUE2 provides an interface to external daemons that can modify coordinates of nodes by sending commands over sockets (section 9.4). The same interface can be fed from files (or devices).

## Declaring a mobility driver

A mobility driver accepting node positioning commands[14] is not a node module (like UART, LEDS or PINS), because its domain is not restricted to a single node: it may affect the positions of multiple nodes essentially at the same time. One such driver, capable of receiving connections from remote agents over sockets, is available all the time and need not be declared in the input data file. We shall call it the external driver. It is also possible to declare local mobility drivers, which can modify node positions according to a local description, i.e., included directly in the input data or read from local files. Such a driver accepts a subset of the commands available to a remote agent connected to the external driver
[14] Strictly speaking, positioning commands apply to Transceivers rather than nodes.

A local mobility driver is declared with the <roamer> element (see Illustration 10), which is a sub-element of <network> and looks like this:

<roamer>
    <input source=”...”> ... </input>
</roamer>

where the input source specification is essentially the same as for PINS (section 6.6). A <roamer> element with <input source=”socket”> is ignored. Note that there is no <output> sub-element in <roamer>. While an external agent connected to a mobility driver over a socket can query the driver and receive feedback information (see section 8.5), this functionality is not available to a local driver.

An arbitrary number of local mobility drivers can be declared in the same data file. Each of them can affect the position of an arbitrary number of nodes. Once a driver requests to re-position a node, any active positioning request regarding that node, possibly originating from another driver, is canceled and the new request takes over.

## The commands

Essentially there are three types of commands accepted by a local mobility driver. These commands constitute a subset of requests available to external agents talking to a mobility driver over a socket. The simplest command simply assigns new coordinates to a given node and has this format:

M nn x y

where nn is a node number (according to the numeration of <node> elements), and x and y are the new planar coordinates. The operation amounts to teleporting the node to the new location. The move is instantaneous. Note that the coordinates cannot be negative.

Similar to PINS (page 30), it is possible to delay the interpretation of subsequent requests with a T command, e.g.,

T +0.01

will cause a 10 ms delay before interpreting the next request, while

T 3600

will halt the input until the model has been run for one hour since its startup.

With a sequence of appropriately timed (tiny) teleportations one can implement any movement, closely approaching smooth navigation along any curve at any (possibly variable) speed. It is tedious, however, to procure such data sets by hand. To simplify typical experiments, the mobility driver offers a standard random-way-point roaming model, which is invoked with the following command:

R nn x0 y0 x1 y1 smin smax pmin pmax duration

where all numbers except nn (the node number) are floating points. When such an request is accepted, the indicated node starts roaming an continues doing so for duration seconds according to the pattern prescribed by the remaining parameters. If duration is zero or negative, the roaming continues forever, or rather, until another repositioning request is issued to the node. In the meantime, the driver is free process other commands: the roaming is carried out in the background.

The first four floating point numbers, i.e., x0, y0, x1, y1, describe the rectangle bounding the node's roaming area. Note that x0 must not be greater than x1, and y0 must not be greater than y1. Besides, all coordinates must not be negative. The node will travel according to this algorithm:

1. A uniformly distributed random target location is generated within the bounding rectangle as well as a uniformly distributed random speed between the specified minimum (smin) and maximum (smax) in meters per second. The node moves at this speed towards the target location.
2. Upon reaching the target location, a uniformly distributed random pause time is generated between pmin and pmax seconds. The node rests for this much time and proceeds from 1.

This process continues for duration seconds, or indefinitely (if duration is zero or negative). It will be interrupted when the same or different mobility driver issues any re-positioning command to the node.

Taking advantage of the string source for a roamer, you can easily set up multiple random-way-point mobility scenarios for multiple nodes. For illustration, consider this declaration:

<roamer>
    <input source=”string”>
R 0 [0.0 200.0 0.0 200.0] [3.5 10.0] [1.0 10.0] -1
R 1 [0.0 200.0 0.0 200.0] [3.5 10.0] [1.0 10.0] -1
T 1800.0
R 5 [0.0 200.0 0.0 200.0] [3.5 10.0] [1.0 10.0] -1
R 7 [0.0 200.0 0.0 200.0] [3.5 10.0] [1.0 10.0] 7200.0
T +1800.0
M 5 40.0 50.0
    </input>
</roamer>

Nodes 0 and 1 start roaming immediately at the beginning of the experiment. After 30 minutes, nodes 5 and 7 join them. Node 5 stops roaming after another 30 minutes when it is teleported to location (40.0, 50.0) and becomes stationary. Node 7 keeps moving for two hours before stopping (at some random location), while nodes 0 and 1 roam forever.

The above example suggests that the command syntax allows for non-numerical characters to be interspersed among the numbers (we used square braces for clarity). This only applies before floating point numbers and should be viewed as an undocumented feature that may be removed without warning. The maximum length of a single request line is 112 characters, which means that extravagance is not encouraged.

# The agent protocol

A running VUE2 model makes a socket available for connections from agents. Such agents may implement GUI to various station components (UART, LEDS, PINS, ROAMER) or provide an interface to OSS programs for the target praxis (executed on a real network). For example, an agent may implement an open ended UART driver (like a COM port under Windows) connected to a node running under VUE2.

The standard port number of the socket opened by a VUE2 model is 4443. It can be changed via the port attribute of <network> (see Section 6), e.g.,

<network nodes=”48” port=”5590”>

which can be useful, e.g., if multiple VUE2 models are run on the same system.

At present, VUE2 implements five functions (i.e., connection types) for agents. They are:

UART	for connecting to a node's UART
LEDS	for connecting to a node's LEDs module
PINS	for connecting to a node's pins module
CLOCK	for reading the virtual clock of the model
ROAMER	to affect the locations of nodes

Except for ROAMER, there can be multiple active instances of any connection type at any given moment. For example, several UARTs belonging to different nodes can be interfaced to agents simultaneously. The above list is likely to grow and new functions to the existing connection types are likely to implemented. The present interface should be viewed as preliminary.

In all cases, the interface is session-oriented, meaning that an agent does not connect to the model for a single inquiry, but sets up a session during which it will be involved in an exchange of potentially unlimited length. The connection can be broken by the agent at any time by simply disconnecting.

## The handshake

A connection is initiated by the agent (client) connecting to the agent port of the VUE2 model for a TCP (stream) session. Immediately after receiving a connection, the agent should send a polling sequence shown in Illustration 1.

It consists of 8 bytes interpreted as two short numbers and one long number in the network format, i.e., MSB first. The first number is a magic sequence used for a quick assessment of the request's sanity. The second short number, code, describes the requested service type. For a request related to a specific node (e.g., connection to a UART), the last four bytes specify the node number, according to the numeration of <node> elements in the input file (Section 6.3).

Illustration 11: Connection polling sequence
Having received a polling sequence, the VUE2 program responds with a single byte. If its value is 129 (decimal), it means that the request has been accepted. The remainder of the exchange depends on the request type. If the value is different, it means an error. Having sent the error byte, the VUE2 program immediately closes its end of the connection. Here is the list of error values:

0	wrong magic sequence
1	node number out of range
2	illegal (unimplemented) request code
3	the node has no UART (for a UART connection request)
4	some agent is already connected to this particular module
6	timeout; this is only sent if a complete 8-byte polling sequence does not	arrive within 30 seconds from the moment of connection
7	the module (UART, PINS, LEDS) is present at the node, but it has no socket	interface
8	the node has no LEDS module (for a LEDS connection request)
9	this code is sent when the program discovers that the other side	has closed	the connection, before closing its end; thus, it is unlikely to be ever received
11	this and the next code are sent within a session, to indicate a protocol error;	code 11 means that the request sequence is too long
12	illegal request (sent within a session in response to an illegal request/query)

Code 10 is intentionally not used as it could be mistaken for a newline character, which terminates messages sent by the VUE2 program in course of normal sessions. A protocol error detected by the program in the middle of a session causes immediate disconnection (EOF) preceded by a single byte (11 or 12).

## UART protocol (request code 1)

This kind of request requires a valid node number. If the number is OK, and the indicated node is equipped with a UART module with socket interface, and no other agent is connected to that UART at the time, the request is accepted. Then, following the acknowledgment byte sent by the VUE2 program, the connection becomes entirely dedicated to the UART. This means that whatever the agent sends over the socket will appear as input on the UART, and whatever the praxis writes to the UART will be sent to the agent over the socket. This will continue until the session is torn down (closed) by the agent (or until the VUE2 program terminates).

The format of the data sent/received by the UART conforms to the coding and type attributes associated with the UART in the input data (Section 6.4). In particular, if the input is “timed”, the data must be organized into packages preceded by the playback time. Normally, this kind of operation is not very useful for a socket connection, but it is available. Note that when the playback time is in the future, the input will be blocked until that time. Similarly, with “hex” encoding of the respective end, the data follows the hexadecimal format described in Section 6.4.

## PINS protocol (request code 2)

This request requires a valid node number. If the number is OK, and the indicated node is equipped with a PINS module with socket interface, and no other agent is currently connected to the module, then the request is accepted. Following the acknowledgment byte, the VUE2 program immediately (without polling by the agent) sends an N message (indicating the number of pins – see page 31) followed by the full list of updates reflecting the current status of all pins. Each such a message takes a complete ASCII line of text, as described in Section 6.6, terminated with a single newline character. The agent may assume that the messages arrive in the order of pin numbers from zero up. Note that the total number of pins and the number of ADC-capable pins are included with every message.

No other message types ever arrive from the VUE2 end. Whenever the status of a pin is changed by the praxis, a pertinent message is queued for transmission. Such a message always refers to a single pin.

The agent is able to affect the status of pins by sending messages over its end of the socket that look exactly like those described in Section 6.6. Such a message should be an ASCII string ending with a single newline character. With an on-line agent connection (as opposed to reading the pin status from a file), there is little demand on T requests, although they are not prohibited. Note that if such a message specifies a moment in the future, the input will be blocked until that time.

## LEDS protocol (request code 3)

This kind of connection works one way, i.e., following the initial 8-byte polling sequence, the agent never sends anything to the VUE2 program. Immediately after the confirmation byte, the VUE2 program sends to the agent the initial configuration of LEDs as a message described in Section 6.5. This is an ASCII message terminated with a single newline character. Then, a similar message is sent whenever the status of a LED changes.

Additionally, to be able to detect the disappearance of the agent, the program sends a dummy NOP message, which is simply a single newline character, every 10 seconds, unless there is a LED status change to report. Note that no NOP messages are sent when the LEDS module is interfaced to a file.

## ROAMER protocol (request code 4)

This type of connection requires no node number (which is ignored, but must be present in the polling sequence). By following this protocol, the agent is able to carry out the operations described in section 7.2, as well as receive feedback from VUE2 regarding node positions. Only one remote ROAMER connection can be active at any time. Following the confirmation byte sent by the VUE2 program to the agent, the rest of the conversation is in ASCII, with lines terminated by (single) newline characters.

Immediately following the confirmation byte, the VUE2 program awaits requests from the agent. The agent may query the program for the position of a given node with a command that consists of the letter Q followed by a single nonnegative node number, e.g.,

Q 49

In response, the program will send the following line:

P nn total x y name

starting with the letter P and consisting of two integer numbers in hexadecimal (nn, total), two floating point numbers (x, y) and a string (name). The first number is the node number and should be the same as the number sent in the query. The second number gives the total number of nodes in the network. The two floating point numbers are the node coordinates in meters. The string is the node's type name, i.e., the name of the SMURPH class representing the node. The latter is useful when the model consists of nodes of several types, as it allows the agent (with an appropriate set of queries) to recognize the complete configuration of the network. If the agent knows nothing, it can always safely issue a query for node 0. Then, having learned the total number of nodes, it can poll them all for position and type.

The agent may issue at will the commands described in section 7.2. Also, it will receive an update whenever the position of a node changes, including changes incurred by the agent itself. Note that local mobility drivers may be changing things behind the scenes. VUE2 tries to reduce the number of unnecessarily updates to avoid overflowing the connection with traffic under heavy mobility scenarios.

An update message begins with the letter U and looks like this:

U nn x y

where nn is the node number and x and y are its new coordinates.

Remember that node coordinates cannot be negative. Having received an invalid request, i.e., one specifying an illegal node number or a negative coordinate, the program sends error code 12 to the agent (a single byte) and closes the connection.

## CLOCK protocol (request code 5)

With this simple protocol, the agent can receive time information from the VUE2 program. Following the confirmation byte, the program will be sending at second intervals the number of virtual seconds from the beginning of execution. This number arrives as a four-byte binary integer in the network format. Every message consists of exactly four bytes.

# UDAEMON

Here we briefly describe the functionality of udaemon, which is a Tk program implementing a rudimentary GUI agent for conversing with a VUE2 model in execution. The program is started with an optional argument, which indicates the port number used by VUE2 program. By default, this number is 4443 and agrees with the VUE2 default (Section 8).

When started, the program opens a window that looks as shown in Illustration 12. This window is the launcher of five different interfaces, corresponding to the five protocols described in Section 8.

The text area labeled “Node Id” is used to insert the (decimal) node number, for those interfaces that require it. The “select” button, initially showing “UART (ascii),” offers the menu shown in Illustration 13. Having selected a given interface (and, if required, inserted a node number in the text area), you can click the Connect button to bring up the respective interface window.

The area below the buttons displays various textual messages (the log), which, in particular may include error messages. The area is scrollable and stores the last 1024 lines of the log (which practically always means everything).

Illustration 12: The root window of udaemon.

## The UART interface

Note that the UART interface occurs in two versions on the menu: “ascii” and “hex.” These versions are independent of the “ascii/hex” coding discussed in Section 6.4. In this place, “hex” means hexadecimal display of the data arriving from the UART, as well as hexadecimal entry of the data to be sent to the UART, and is useful in those cases when that data are non-ASCII (e.g., the praxis is meant to communicate with some program using binary data, and we want to manually emulate the behavior of that program). A similar effect will be achieved when the UART coding is “hex” (and the interface mode at udaemon is “ascii”); however, in that case, the hexadecimal coding/decoding will be done by the VUE2 program. Note that double “hex,” i.e., on both sides, will have a rather confusing effect of displaying in hexadecimal the character codes of hexadecimal digits (the input will be even more confusing).

A UART connection produces a window shown in Illustration 14. It looks like a straightforward terminal emulator, with the text area at the bottom used for input. The upper area is resizeable and scrollable. It stores the last 1024 lines written to the UART.

By checking the “hex” box at the bottom, you can switch the terminal from “ascii” to “hex” and vice versa without reconnecting. The reason why, in addition to this box, the mode can also be selected from the root window is that when the UART window is open, some text may already be displayed on it (see the held option on page 28). The mode switch only affects the data to be displayed, not that already present on the screen.

Illustration 13: The interface menu.
A line typed into the bottom text area is sent to the VUE2 program when you hit the Enter key. For “hex” mode of the UART terminal, this data should consist of pairs of hexadecimal digits optionally separated by spaces. Only the binary data represented by those digits will be sent to the VUE2 program.

Illustration 14: A UART window.

## The PINS interface

Similar to UART, this interface requires a valid node number. Following a successful connection, a window like the one shown in Illustration 15 pops up on the screen.

The three rows of boxes at the top reflect the current status of the pins, with one column corresponding to one pin. Only the bottom row is clickable, and only if the letter in the upmost box of the column is I, which means that the pin has been set by the praxis to “input.” For such a pin, clicking on the box in the bottom row toggles the binary value of the pin. In Illustration 15, pins 0, 1, 3, 6, 8, 9 are input, pins 2 and 7 are output (letter O), and pins 4 and 5 are set for analog input (letter A). The full collection of characters that can appear in a bottom-row box is:

I	the pin is set for digital input
O	the pin is set for digital output
A	the pin is set for analog input
P	the pin is a pulse counter
N	the pin is a notifier
D	the pin is a DAC output
–	the pin is unused (its status field in the input data set is 0, see page 29)

The middle row shows the output value of those pins that have been set by the praxis as “output.” For any other pin type, the corresponding square contains a dash. Those squares in the bottom row that do not represent input pins are disabled, i.e., clicking on them triggers no action.

Each ADC-capable pin has a slide widget that can be used to set the voltage on that pin. Only those pins that have been currently selected for the ADC function have their slides enabled (pins 4 and 5 in Illustration 15). The value above the slide knob tells the current voltage on the pin. Finally, the DAC-capable pins have voltage display areas at the bottom. No such pins appear to be available in Illustration 15.

Illustration 15: A PINS window.
Note that the praxis can dynamically redefine pins, and, for those that are output or DAC, set their values. All such changes are immediately reflected in the window. You can trigger changes in those pin values that are currently available for digital input or ADC – by clicking on a box in the bottom row or adjusting the respective slide. Such changes are immediately conveyed to the VUE2 program. Slide adjustments are sent incrementally, meaning that a slow movement of the slide knob will result in several updates sent to the VUE2 program, reflecting the progress in adjustment.

## The LEDS interface

This interface is very simple as it involves no user input. The displayed window shows one circle for each of the LEDs defined in the module, with the LEDs numbered from left to right. Color gray means that the LED is off, otherwise, it is on. The first five LEDs show the colors: red, green, yellow, orange and blue when lit. If there are more than five LEDs, the ones numbered 5 and up are all red.

Illustration 16: A LEDS window.
## The ROAMER interface

This interface takes no node number. Illustration 17 shows a sample window displayed in response to a ROAMER connection, for a network consisting of 6 nodes of the same type. The numbers in the lower right corner show the dimensions of the area covered by the window.

If the window is resized, udaemon will re-fit the nodes to the new size, i.e., by extending the window, you do not necessarily make it cover a larger area, but simply magnify the picture. It isn't difficult to guess that by dragging a node, you will move it to a new location. If the dragging is smooth, multiple requests will be sent to the VUE2 program, such that the movement will appear incremental to the model. Note that the present version of udaemon has no interface for specifying random-way-point mobility patterns (see page 34). This feature will be added shortly.

Moving to the right and up is unrestricted. If you move a node beyond the window boundary, the window will be renormalized to the new network geometry. This renormalization does not affect the window's size or shape on the screen, but the assumed dimensions of the edges. Moving to the left and down is limited by the coordinates <0,0>. Udaemon will not let you move a node below these coordinates.

To see the exact position of a node, just move the mouse over it. The coordinates will be displayed in the lower left corner of the window along with the node's type name, which coincides with the name of the node's class. If there are multiple node types in the model, they will receive different colors on the screen – up to six colors: yellow, blue, orange, red, green, gray. If there are more than six node types, all the remaining types will be gray.

There is a way to see the distance between a selected pair of nodes. Click on the first node without dragging it, then move the mouse over the second node and click. A dashed line connecting the nodes will show up for 2 seconds with a number in the middle showing the distance between the nodes in meters.

## TIMER interface

This is a very simple interface that needs no node number. It opens a window that shows the emulated time of the model in seconds, assuming that the execution started at time 0.

Illustration 17: A MOVER window.