# RFTEST 23/10/04
# Preamble
The role of this program is to test transmission/reception capabilities of nodes operating in a group. The present version is just something to start with (this sentence was written a long time ago, for the first version, and I am still reluctant to remove it). I will be adding more capabilities as needs arise.
# Preparation
Compile and download. All nodes in the test setup run the same code (accounting for the fact that different node types need that code to be properly configured and recompiled, as per the pertinent board type). They tell their IDs (which should be all different) based on the flashed HOST_ID, whose interpretation is similar to our standard blueprints, e.g., T&P. Use genimage (image customization in PIP) to create downloadable images from the generic compilation output.
The Node ID, via which a node can be referenced, is the lower half of HOST_ID, which corresponds to the "Node number” as inserted by genimage. The prefix part, i.e., the upper half of HOST_ID (known to genimage as “NetId”) encodes a few startup parameters as follows:
15	8 7 0
===============================
D A R Z Z P P P C C C C C C C C
The lower byte encodes the RF channel, which can be any number from 0 to 255.[1] Bits 8-10 (PPP) encode the initial setting of transmitter power (0-7), bits 11-12 (ZZ) are the two least significant bits of the Network ID (and can be used to differentiate among multiple test setups operating in the same neighbourhood), bit 13 (R), if set, indicates that the module should start with the radio receiver on, bit 14 (A), if set, indicates that the node should start "active", i.e., it will be transmitting measurement packets at the default interval of 1 second, as explained below), bit 15 (the most significant bit D) indicates power-down mode of the CPU (if set, the node begins in power-down mode).
[1] For CC1350, there are only 8 channels; any value larger than 7 translates into 7.
When a node starts in the off state, then, obviously, it cannot be controlled by wireless commands arriving from other nodes. It can be started (controlled) from the UART or by pressing a button (if the node happens to be so equipped). A UART-less device devoid of buttons starting with the receiver off (the R bit set to zero) will never be able to do anything.
For example, the standard prefix BACA (supposing you leave it as is), expands into:
======= ======= ======= =======
1 0 1 1 1 0 1 0 1 1 0 0 1 0 1 0
which means: channel 202 (0xCA),[2] transmission power 2, Network ID 0xF617 (0xF614 is the prefix applied to the two bits amounting to 3), sender initially inactive with the receiver on, starting in power-down mode. On the other hand, to select the “natural” default, i.e., the maximum transmission power, channel 0, and power-up mode with active transmitter/receiver, use this prefix:
[2] It is channel 7 for CC1350.
0 1 1 0 0 1 1 1 0 0 0 0 0 0 0 0
i.e., 0x6700. The Network ID field can be arbitrary, but it must be the same for all nodes of the same setup. Note that nodes can be rendered active/inactive remotely. Also, their transmission power levels can be changed, as well as their power-down/power-up status, and even the channel number. There is no way, however, to change the Network ID remotely.
# Operation
Any node can be used to orchestrate an experiment. Nodes equipment with buttons can be started and stopped by pushing a button, but a UART interface is needed if we want to see numbers and/or change parameters. The default UART rate is 9600 bps (it can be changed from options.sys).
The simplest way to discuss the operation of a node is to introduce the commands, as they can be entered from the UART, so this is where we start.
When a node resets, it produces a message that looks like this:
    Node: 19, NetId: F610, Channel: 6, XPower: 7, Powerup, TxOn, RxOn
    Ready:
where your actual indications may vary depending on the initial settings (see the previous section). All numbers except Network ID are in decimal.
Command l [el] (set packet parameters):
l [mindel [maxdel [minpl [maxpl [ackto]]]]]
All parameters (five unsigned numbers) are optional (the command with no arguments sets nothing and shows the current settings). The command describes the parameters of measurement packets to be transmitted at prescribed intervals. There is a separate command to start the actual transmission (see below). Nodes receiving such measurement packets are expected to count them and report (upon request) the received counts. The arguments have the following meaning:
mindel	the minimum inter-packet interval in (PicOS) milliseconds (the default is 1024)
maxdel	the maximum inter-packet interval (defaults to 1024)
minpl	the minimum packet length (see below)
maxpl	the maximum packet length (defaults to 60)
ackto	the Id of the node to receive ACKs for the measurement packets
A value that is not specified retains its previous (last or default) setting with the sanitizing procedure described below. If mindel < maxdel, the actual inter-packet interval will be randomized between the two values. The lowest limit is zero (not recommended except for limited series of packets to be sent at the maximum possible rate). Whatever values you specify, the program will try to sanitize them, i.e., if the specified maximum is less than the minimum, it will be set to the minimum. This also applies to the case when only the minimum is specified and the previous setting of the maximum turns out to be less than the new minimum. The limit on the maximum interval is 65535. The command always lists all the actual settings.
The absolute minimum packet length is determined by the compiled-in configuration of sensors (whose values are reported in every measurement packet). Whatever you specify for the packet length, the program will make sure that the actually assumed minimum is not less than the absolute minimum and that the assumed maximum is not less than the assumed minimum.
The layout of a measurement packet, which you don't have to know to run tests, is this (in words, in order, starting from the beginning):
NID	Network ID
DRI	filled by the driver with the packet's LBT backoff in PicOS milliseconds
RCV	zero (this is used to tell measurement packets from other packets)
SND	Node ID of the sender
SER	serial number of the packet (inserted by the sender)
FLG	node flags associated with the sender (xmit power level + power-down state)
ACT	the ID of the node to receive the ACK for the packet
SEN	first sensor value
...
SEN	last sensor value
RND	random contents
...
RND	random contents
CRC	CRC (as required by the driver)

The DRI field is only filled by the driver, if it has been compiled with RADIO_OPTION_RBKF added to RADIO_OPTIONS (see options.sys); otherwise, the field is going to be zero.
The number of sensor values equals the declared number of sensors and can be changed at compilation. Thus, the minimum length of a measurement packet, in bytes, including the CRC, is 16 + 2 x N, where N is the number of sensors. If the specified value of minpl is less than that, it will be bumped to the required minimum. Also, if the specified (or previous) maximum (maxpl) is less than the new minimum, it will be set to the new minimum. If the maximum is greater than 60, it will be truncated to 60. In other words, whatever you specify, the program will make (some) sense of it.
If the effective minimum packet length is strictly less than the maximum, the program will randomize the actual packet length. Note that the specified minimum can be more than the absolute minimum. In any case, when a packet's length is more than needed to accommodate the sensor values, the unused words are filled with random contents.
Something to fix: at present, the program assumes that each sensor value takes one word, which is not very convenient. This should be done differently. Besides, some sensors must be initialized, turned on and off.
Command s (send measurement packets):
s [count [urgent [rxofftime [predelay]]]]
The first argument specifies the number of packets to be sent. Zero (or absent) means keep sending indefinitely (until stopped explicitly). The second argument is the urgent flag. If nonzero, the packets will be sent with the urgent tag, which (assuming that the WOR option has been compiled in) will cause them to be preceded by extra long preambles to wake up the receivers sleeping on WOR.[3]
[3] If the WOR option is not compiled in, the urgent flag is ignored, except for the standard treatment by VNETI consisting in pushing the packet to the front of the transmit queue.
If the third argument is nonzero, the receiver will be switched off for the specified number of PicOS milliseconds (which must be less that 65536) and then switched back on again. This way you can send a bunch of packets in the OFF mode (testing the node's operation in this mode) without permanently removing the node from the network (important if the node can only be reached by radio).
If the fourth argument is nonzero, it specifies the initial delay (in PicOS milliseconds) before sending the first packet (this may be useful when the command is issued remotely, see below). Normally the first packet is sent immediately: the delay specification from the l command only applies to spacing in front of the subsequent packets.
The first thing a node does when it receives a measurement packet is tallying it. If this is the first time the node ever hears from the packet's sender, it will create an entry for the sender with the initial count of 1. A node can accommodate up to 8 different senders. This can be increased in principle, but the format of reports (that you can request from nodes remotely) restricts that population to whatever can fit into one packet.
Having counted the packet, the node checks if the ACT field in the packet is nonzero. If this is the case, the node sends an ACK to the node indicated in the field. The ACK includes:
- the identity of the sender and the recipient
- the packet's serial number (SER) as inserted by the sender
- the packet's length
- the power level setting at the packet's sender
- the RSSI at which the packet was received
- the LQI (link quality indication) at which the packet was received
A node receiving an ACK for a measurement packet will report it on the UART in a line of text looking like this:
MAK F:19, T:16, N:45, L:58, P:7, R:101, Q:0
where F and T are the packet's sender and recipient (from and to), respectively, N is the serial number, L is the length, P is the transmission power, R is the RSSI, and Q is the LQI.
If the ACT field of a received measurement packet specifies the recipient node, i.e., the node receiving the original packet, the recipient will show the contents of the ACK directly on its UART, rather than sending an ACK packet to itself.
Command q (stopping transmission):
The node's transmitter can be stopped with this command:
q
The same command can be used to stop (abort) a collection of PATABLE statistics in progress (see the t command below).
Command r (measurement report):
By executing this command, you can obtain a report from the current node (this report will be written to the UART):
r c
The argument is an optional number interpreted as a Boolean value. If nonzero, the command will clear the counters after presenting their contents. For example, you may see something this:
Stats (local, ch = 0):
Mem: 4130 4051 78
Sent: 3576
Received from: 19: 2491
Received from: 20: 3387
Received from: 22: 831
Driver stats: 576, 573, 1311, 0, 0, 83
Ready:
The header lists the current channel number followed by memory information: the current amount of free memory on the heap, the smallest amount registered so far, and the minimum unused portion of the stack (all values in words).
The Sent value is the number of measurement packets sent so far by the node itself. This is followed by the list of entries for all nodes from which the node has received measurement packets, along with the number of packets received. At the end we see the "driver statistics", i.e., a collection of numbers produced by querying the PHY with PHYSOPT_ERROR. For CC1100, they stand for, in this order:
1. The total number of activations of the receiver. This happens whenever the device thinks it perceives something looking like a packet. The counter wraps around at 64K. When that happens, the next counter is automatically zeroed out as well.
2. The total number of packets that have been correctly received and passed to VNETI. Note that this can never be more than the previous value. Also note that with hardware CRC and the AUTOFLUSH option on, the two values will always be the same.
3. The total number of packets submitted for transmission.
4. The total number of packets that were submitted for transmission and exceeded the limit on the number of transmission attempts on LBT failures. [Note: such packets are not dropped in the present version, but rather resubmitted for transmission resetting the LBT procedure.]
5. The exponential moving average of the transmitter's waiting time for channel access maxed at 4095 (PicOS) milliseconds. The formula, which is evaluated at every attempt at a channel grab, is W_{n} = W_{n-1} times 0.75 + b times 0.25 , where W_n is the new calculated average, W_{n-1} is the previous average, and b is the current backoff (in PicOS milliseconds). If the transmitter gets the channel immediately, the backoff is assumed to be zero. Note that the reported value never grows above 4095 (which is considered an alarm condition).
6. The maximum backoff experienced so far by a single packet in PicOS milliseconds. This is maxed at 64K (i.e., word size).
For CC1350, there are seven numbers (collected automatically by the internal firmware):
1. The number of packets that have been correctly received and not ignored.
2. The number of packets that have been received with CRC errors. This is zero, because our driver never receives packets with erroneous CRC.[4]
  [4] An option to this end can be made available if needed.
3. The number of packets that have been correctly received and ignored, because of address mismatch. This is zero, because our driver doesn't use the built-in addressing scheme.
4. The number of packets that were not received because of illegal length.
5. The number of packets that have been received and discarded because of the lack of buffer space.
6. The RSSI of the last-received packet.
7. The internal time stamp of the last-received packet (mostly useless).
Note that the driver statistics may include overheard packets belonging to other setups. They also include non-measurement packets of the present setup (see below). Thus, tallying them up with measurement reports may be difficult, depending on how (un)clean the setup is.
Command c (clearing measurement statistics):
Here is a command to clear all the numbers shown with r:
c
It zeroes out all packet counters, as well as the driver statistics. Note that, e.g.,
r 1
also zeroes the counters (having shown their last values).
Command v (viewing measurement packets):
v [f]
will switch on (or off) reports on measurement packets. The argument is an unsigned integer whose only bits 0 and 1 are interpreted (i.e., the value is taken modulo 4). The meaning is:
0 – switch off the reports
1 – show all outgoing measurement packets
2 – show all incoming (received) measurement packets
3 – show both outgoing as well as incoming measurement packets
The absence of an argument is equivalent to 2.
An outgoing packet is shown as:
->N:45, L:58, P:7, M:U, V:2365,234,0,1
and an incoming one is shown as
<-S:19, B:127, N:45, L:58, P:7, R:101, Q:0, M:U, V:2365,234,0,1
S is the Node ID of the sender, B is the backoff experienced by the packet in PicOS milliseconds,[5] N is the serial number of the packet (incremented by 1 for each subsequent packet transmitted in a series), L is the total length of the packet, including the CRC. P is the transmission power applied by the sender, R is the RSSI reading at the receiver, and Q is the LQI. M tells the power-down/power-up status of the sender (U means up, D means down). The remaining values show the sensor readings, if any. All values are in decimal. Note that stuffed words filled with random contents are not displayed.
[5] This is going to be zero, if the RF driver is not compiled with RADIO_OPTION_RBKF.
Command n (cancelling packet viewing):
This command:
n
is equivalent to v 0.
Command d (putting the node into power-down mode):
This command:
d
puts the node into power-down mode. Note that for CC1350 there are two (active) power down modes: 1 (IDLE) and 2 (STANDBY). The selection of the effective power down mode (one to be actually applied when the node is put into the power down mode) is done in options.sys. Typically, for a node equipped with a UART, the effective power down mode is IDLE (for CC1350 the UART doesn't work in STANDBY), while for a UART-less node, the effective mode is STANDBY.
Recall that the mode in which the node starts is determined by the formal NetId parameter (see above).
Command u (undoing the power-down mode):
u
puts the node into the power-up mode.
Command p (selecting the transmission power):
This command:
p val
where val is between 0 and 7 inclusively, sets the node's transmission power.
Command m (modifying the parameters of the RF module):
CC1100 (setting registers):
When compiled properly [with the 0x40 flag included in RADIO_OPTIONS], the CC1100 driver allows you to specify an argument to PHYSOPT_RESET viewed as a list of pairs: register number, new value. With this command, the program can modify (in principle any) writable registers of the chip:
m reg1 val1 ... regn val4
The arguments are byte-sized hexadecimal values. Their total number must be even. The first value specifies the register number, the second its new content. Note that individual entries in the PATABLE can be set one-by-one (the register number of entry 0 is 0x3e).
CC1350 (redefining power levels [aka PATABLE]):
On CC1350, the command modifies the settings of the eight standard power levels (for tradition, we refer to those settings as PATABLE). The settings are described by word-sized bit patterns. The command accepts up to 8 hex arguments representing the initial PATABLE entries. The unspecified (trailing) entries, if any, are left intact. The command only works, if the driver has been compiled with an option allowing multiple (switchable) power levels (RADIO_DEFAULT_POWER < 8).
Command P (repeating a command periodically):
This command:
P interval cmnd
where interval is a number of seconds, will periodically issue command cmnd at the specified intervals. For example,
P 60 r 1
will produce a report every minute and zero out the counters. At most one P can be active at a time. This command:
Q
revokes the last P command.
Commands f and g (switching the receiver off and on):
This command:
f [wor]
when issued without an argument or with zero, switches off the node's receiver (rendering the node dumb to measurement packets and remote commands, see below). The node can still transmit. If the argument is nonzero, the command puts the node into WOR mode, if the node admits that mode (the mode has been enabled in options.sys with #define RADIO_WOR_MODE 1).
The f command cannot be issued remotely (see below).
The receiver can be switched back on (also exiting the WOR mode) with:
g
Command w (modifying WOR parameters):
The syntax is different for CC1100 and CC1350. For CC1100 the command looks like this:
w [idle [pre [evt0 [rxtime [pqt [rssit [evt1]]]]]]]
It is applicable when the program has been compiled with the WOR option included [#define RADIO_WOR_MODE 1]. The CC1100 driver then accepts a PHYSOPT_SETPARAMS request to modify WOR parameters (see the driver's document for details).
The arguments of w are interpreted as (in this order):
RADIO_WOR_IDLE_TIMEOUT in PicOS milliseconds
RADIO_WOR_PREAMBLE_TIME in PicOS milliseconds
WOR_EVT0_TIME
WOR_RX_TIME
WOR_PQ_THR
WOR_RSSI_THR
WOR_EVT1_TIME
The last five arguments are only interpreted when the program has been compiled with the test option for WOR [#define RADIO_OPTIONS ( ... + 0x20 ...)] on top of WOR being compiled in [#define RADIO_WOR_MODE 1].
For CC1350, the command accepts four arguments:
w [idle [interval [rssit [pqt]]]]
which stand for (respectively):
1. the idle timeout after which the WOR mode is automatically resumed following a packet reception (equivalent to RADIO_WOR_IDLE_TIMEOUT for CC1100)
2. the wakeup interval (in PicOS milliseconds), i.e., the WOR cycle length
3. the RSSI threshold expressed as a standardized PicOS RSS reading (nonnegative byte)
4. the PQT flag (zero/nonzero) indicating whether the packet quality assessment is incorporated into the scheme
Missing arguments (from the end) receive standard values (see cc1350.h).
Command t (collecting PATABLE statistics):
With this command you can start an experiment whereby the node scans through a sequence of possible power settings corresponding to a PATABLE entry and exchanges packets with a selected neighbour to determine the perceived RSSI reading corresponding to the particular setting. The command takes four arguments:
t nid cavg start nvals
where nid is the node ID of the selected neighbor, cavg is the number of samples per one PATABLE setting (to average the readings), start is the initial value to try, and nvals is the number of values. The initial value (start) is specified as a hex number (the remaining parameters are decimal).
The initiating node will set its formal power level to 0 (selecting the first PATABLE entry) and enter a loop in which it will reset the first entry to start. Then, the setting will be incremented by 1 on every turn, until nvals settings have been scanned. For each setting, the node will poll the selected neighbour, which will subsequently respond with the RSSI at which the polling packet has been received. The node will try to receive cavg responses for every setting, re-trying every poll up to 16 times. For each setting, the node will write to the UART a line like this:
xxxx, rrr, cc, lqc, maxlq
where xxxx is the PATABLE setting in hexadecimal, rrr is the averaged RSSI reading, and cc is the number of samples used to calculate the average. Normally, cc is equal to the cavg argument of the t command, however, it can be less if some responses haven't made it (despite the 16 retries per sample). The last two values in the output line refer to the link quality indication (which is a reception parameter returned along with the RSSI). Thus lqc is the number of cases (samples) where LQI was found to be nonzero (it is a number between 0 and 127) and maxlq is the maximum LQI value among the samples that have contributed to the reading.
For CC1100, a PATABLE setting is one byte, so the specified (and incremented) settings are truncated to the less significant byte. For example, with this command:
t 23 16 0 256
you can scan through all possible PATABLE settings, using node 23 as the responder, with 16 samples per setting, starting from zero.
For CC1350, the setting is 2 bytes. No LQI values are produced (lqc and maxlq are always zero).
To interpret the results, it is recommended to direct the terminal output to a file and then read that file (as a comma-separated list of values) into a spreadsheet program and sort the lines by the second column.
A collection in progress can be interrupted (prematurely) with q. At the end of collection, the node resets the power setting to its value before the collection.
Remote commands (S):
You can issue practically any of the above commands addressing it to a remote node (akin to Wlodek's old “remote command execution” patent) by executing this:
S n command
where n is the Node ID of the node on which the command should be executed. For example, you can do something like this:
S 19 s
which will activate the transmitter of node 19 with the standard (or last-configured) parameters. The following examples should all work (assuming the nodes are reachable):
S 19 l 512 4096 44 58
S 19 s 1000
S 23 d	[putting node 23 into power-down mode]
S 19 q
S 25 p 6
S 21 m 1C 01 24 1F
S 24 v
The last one may make little sense, as the reports about received packets will be shown on the target node's UART, but is legit. You can also say something like this:
S 19 S 24 s 8000 1
It may not be very useful, but comes for free.
Remote commands (as well as responses to them) are sent in packets that are not considered measurement packets, so they are not "officially" counted by their recipients (although they do contribute to driver statistics). A packet carrying a remote command is characterized by nonzero in the RCV field, which identifies the single recipient of the command. The full format of a command packet is this:
NID	Network ID
DRI	the packet's backoff inserted by the driver (if the option is compiled in)
RCV	Node ID of the recipient
SND	Node ID of the sender
SER	serial number (used to match responses to commands)
FLG	unused
CMD	command text
...
CMD	command text
CHK	CRC
The command text is represented as a straightforward string terminated with a NULL byte. Note that there is a limit on how much of the command string can fit into a packet. Excluding the NULL byte, this limit is 45 characters. BTW: the maximum length of a line entered from UART is 80 characters (excluding CR/LF).
Having received a command, the recipient responds with an ACK, which, gives the sender some indication of success/failure. For example, you may see something like this:
Ready:
S 19 d
Ready:
OK from 19
The last line indicates that the command has been accepted by the recipient and, apparently, executed fine.
The sender will retry the command up to five times at 1 second intervals. If it receives no reply from the recipient, you will see this:
Ready:
S 233 d
Ready:
Timeout reaching 233
A reply looks like the original command packet up to and including the SER field, with the command text replaced with the response. In the simplest case, the response is a single word with 0 meaning OK, and nonzero indicating a failure. For example, instead of OK, you may see:
Error 6 from 23
I may make this message more friendly later. Here is the list of numerical error codes:
1. formal error (probably cannot happen)
2. no memory to acquire packet
3. node busy with a previous command
4. command syntax error
5. node out of memory (umalloc failure)
6. no room to run more threads
7. no such command
In the present version, only one (remote) command, r, triggers a non-trivial response. Having received it, the node will not send the count report to its UART (as per normal), but rather to the sender of the command packet. For example:
S 19 r
Ready:
OK from 19:
Stats of node 19:
Sent: 2108
Received from 17: 3908
Received from 18: 2201
Driver stats: 6001, 4, 2, 1
This way you can conveniently collect all reports in one place.
Please note that the range of packet counters is 65535. This may matter, e.g., if you leave an experiment overnight when a single node can transmit more than 64K packets (but you should be fine with, say, 12 hours, 1 packet per second).
Command C (changing the channel):
With this command you can change the RF channel of the node:
C ch nsec
where ch is the channel number (0 – 255)[6] and nsec is a timeout interpreted as the number of seconds. The timeout argument is only interpreted when the command is received over the radio (it is ignored if the command has arrived from the UART). The node will switch to the indicated channel. If the command has been received remotely, the node will reset (interrupting any activity and effectively reverting to the default channel) if it receives no packet for the specified number of seconds. Use a large value for a semi-permanent switchover. The maximum timeout is 65536 seconds.
[6] 0-7 for CC1350.
When sent remotely, the command will receive no acknowledgement (the sender will signal a timeout), which should be considered normal.
Debugging commands
There is a single command, z, whose purpose is to cover auxiliary commands, e.g., useful for debugging, whose population may grow as needed. This is what we have at present:S
ztm d n
ztu d n
The command times the spin delay loop for the CPU verifying the operations mdelay and udelay, respectively. The first argument is passed to mdelay/udelay, the second argument (defaulting to 1) is the number of times the operation should be repeated (in a loop). When completed, the command produces the number of seconds it took to execute it, e.g., the output from:
ztm 1000 3
may look like this:
ZTM: 1000, 3 -> 3
The letter m can be dropped, i.e., zt is equivalent to ztm.
zrb a
zrw a
The command reads a byte or word, respectively, from the memory location a, which must be specified in hex, and prints its content (both in hex and in decimal).
zwb a v
zww a v
The command writes the specified byte or word v to memory location a. Both values must be specified in hex. The letter b is optional, i.e., zr is equivalent to zrb, and zw is equivalent to zwb.
A sample experiment:
From PIP, compile the program for, say, the WARSAW board. Run genimage (Customize image). Leave the Cookie fields as they are, and enter 4700 into the NetId field. This selects channel 0, power 7, and makes the nodes start in an active state (with their transmitters and receivers active, the transmitters sending packets at 1 second intervals. Create images for, say, six nodes. Enter 1 into the From field and 6 into How many. Press Generate. Load the files into the nodes and power them up.
Connect a terminal (piter) to the UART of node 1. Execute:
v 3
on that node. This will let you see the packets transmitted and received by the node. After a while enter
q
f
to stop the transmitter and the receiver. Then see the report:
r
and retrieve reports from the remaining nodes, e.g.,
S 2 r
S 3 r
...
and so on. Compare the numbers.
# Buttons and LEDs
For field (e.g., range) tests, it is convenient to be able to control the nodes by buttons, operating them without the UART interface. If a node is outfitted with at least one button (formally configured as a BUTTON in the BOARD definition), then the button number 0 is configured as the start/stop button for the radio. This makes more sense when there is at least one LED configured into the BOARD, because then the simple actions triggered by the button can be visualized by the LED. If the symbol SIGNALING_LED is defined (e.g., in options.sys), its value is interpreted as the number of the LED to be used for indicating button actions and packet reception events.
By pressing the button (the action is in fact triggered on the button's release), you will toggle the on/off status of the radio, where by “on” we mean both the transmitter and the receiver being on (as after the pair of commands s and g issued consecutively), and by “off” we mean both components being off (as after q and f). When the radio is turned on, the signaling LED blinks quickly 4 times, when the radio is turned off, the LED blinks twice. The initial status of the radio is determined by the second most significant bit of the NetId field.
On devices capable of a soft shut down (considered the deepest power down mode), like CC1350, pressing the button continuously for slightly over 5 seconds, until the signaling LED starts to blink rapidly (at twice the frequency of the on/off blink), will shut the device down, leaving it in a semi-off, restartable state with the absolutely minimum current drain. The device will wake up in its initial reset configuration when the same button is ever pressed again.
When the signaling LED is configured, it will blink on reset, when the device is powered on: 8 times, if the device is UART-capable, and 4 times, if no UART is configured into the device. The LED will also blink (staying lit for a slightly longer time) on every packet reception. The longer on period makes packet receptions relatively easy to spot, which may be useful in field tests.
With two LEDs available, one of them can be dedicated to showing the on/off status of the device in a (sort of) persistent fashion. If the symbol STATUS_LED is defined (e.g., in options.sys), its value is interpreted as the number of the LED to indicate the on/off status of the radio. When the device is running (i.e., it is not in the shutdown state), the status LED will blink (briefly): every 4 seconds, if the radio is off, and every second, if it is on. It possible to set STATUS_LED to the same value as SIGNALING_LED, thus combining the two functions into a single LED. This will make it a bit more confusing, but just a little bit, because the status blinks are quite perceptibly shorter than reception blinks.
# CHRONOS
The praxis can also be used with CHRONOS (in a UART-less mode) with some commands mapped to the CHRONOS buttons. When compiling for CHRONOS, keep in mind that the values of CHRONOS's sensors cannot be directly dumped in measurement packets, because they are compound (take more than one word), so make sure to set NUMBER_OF_SENSORS to 0 (options.sys in the application's directory does that by default).
All the standard configuration options derived from the NetId also apply to CHRONOS. When started, the praxis says RFTS READY (in the display), or as close as it can possibly get.
The buttons are assigned these functions:
Button 0 (upper left) toggles between “send” (the argument-less s command) and “quit” (q). Button 1 (lower left) toggles between commands v and n. With v, the lower line of the LCD will be showing the serial numbers of received packets. Button 2 (upper right) toggles between d and u (switching between the power-down and power-up modes of the CPU). Button 3 (down right) circulates the RF state through: RXOFF, RXOFF+WOR, and RXON. Button 4 (middle right) toggles LCD OFF and ON.
Except for button 4 (whose effects are directly visible), the outcome of a button press is displayed in the upper line of the LCD.