# DecaWave DW1000
# driver

August 19, 2015

© Copyright 2015, Olsonet Communications Corporation.
All Rights Reserved.

# Preamble

DecaWave DW1000 is a UWB radio module with built in precise timing capabilities, intended for indoor positioning. The module is described in detail in these documents:

DW1000 User Manual
DW1000 Data Sheet, version 2.04
DWM1000 Data Sheet, version 1.01

available from DecaWave's web site at: http://www.decawave.com/

This document sketches the practical functionality (interface) of the present PicOS driver for the module. There is no need to refer to the above documents, unless you want to understand in depth what is going on inside the module (or in the driver). Needless to say, the present driver is preliminary and intended solely for experiments (and this document is intended as a starting point for discussion). We don't know yet whether the module is going to be useful for us at all.

# The assumptions

At present, we focus solely on the location tracking capabilities of the module. While the device can be used for straightforward RF communication (say as a replacement for CC1100), and the present driver can be quite easily extended in that direction, the option doesn't immediately appear attractive to me, because the device's power consumption is one order of magnitude (in fact almost exactly 10 times) higher than for CC1100 (say with the receiver on). On the other hand, DW1000 has a number of interesting features reducing the length of duty cycles in some communication scenarios (plus some lower power listening modes similar to WOR). Those scenarios are related to IEEE 802.15.4 (ZigBee) and (sort of) assume point-to-point communication, so it is not immediately clear how attractive the module can be for our applications.
Consequently, the present driver does not make the device available as a PicOS PHY. Instead, it implements a sensor-actuator pair. To see how the two conceptually simple interfaces can represent the device for our purpose, we have to learn a bit about location tracking with DW1000.
# Ranging

The extra features of DW1000 (compared to other radios, e.g., CC1100) boil down to a configuration of precise timers that can be used to estimate the Time of Arrival (TOA) of a packet together with its Time of Departure (TOD). Consequently, we can estimate the packet's Time of Flight (TOF), which can be translated into the distance between the sender and the receiver. Having three or more distances between a Tag and a number of Pegs (whose locations are known) will let us estimate the location of the Tag.
Suppose that some two nodes want to determine the distance between them. They have to carry out a handshake of sorts with one node going first. The initiating node (call it A) sends the first packet of the handshake which I call POLL. The packet needs no particular structure or content. The only important thing is that the other node (call it B) should recognize it as a POLL packet and should also learn the identity of the initiating node. Any packet exchanged within the handshake is a ranging packet, which means that:
- the sending device can precisely determine the time of its departure
- the receiving device can precisely determine the time of its arrival
Specifically, there is a special marker symbol within the packet's header whose transmission is used as the relatively sharp reference point for the timing. Needless to say, the timers are local, so the scheme does not assume that nodes synchronize their clocks. The TOF estimation is based on differences in the indications of local timers only.
When the initiating node A sends the POLL packet, it marks the time of its departure (using its local clock) as TSP. The other node, B, receiving the POLL packet, marks its arrival time as TRP.
Having received the POLL packet, B responds with a RESP packet addressed to A. Again, the packet needs no special content other than being identifiable as a RESP packet sent by B and addressed to A. B marks the departure time of the RESP packet as TSR, and A marks its reception time as TRR.
Having received the RESP packet, A sends the final packet of the handshake to B. I call this packet FIN. A inserts into the FIN packet (the packet does have a payload) three timer values: TSP, TRR, and TSF, where TSF is the departure time of FIN. The tricky bit is that A has to know that time, i.e., the exact time of departure of FIN, before sending the packet. To make this possible, the device has a feature whereby it can be instructed to dispatch the next outgoing packet in such a way that the packet's marker symbol is transmitted precisely at a preset timer value. Thus, the driver calculates a safe (delayed) transmission time of FIN, based on current time + some processing interval, sets TSF to that time, inserts TSF into FIN (along with the other two timers) and tells the device to transmit the packet exactly at TSF. The actual action is a bit more complicated, but it pretty much amounts to this.
When the FIN packet gets to B, the node has enough information to try to estimate the distance between the two nodes (note that it is B that does the estimation). The node has these six timers:
TSP – departure time of POLL at A
TRP – arrival time of POLL at B
TSR – departure time of RESP at B
TRR – arrival time of RESP at A
TSF – departure time of FIN at A
TRF – arrival time of FIN at B
Now, the TOF can be calculated as:
TOA1 = ((TRR – TSP) – (TSR – TRP)) / 2
and also as
TOA2 = ((TRF – TSR) – (TSF – TRR)) / 2
so the node can take the average of the two values. Note that all the differentials refer to timers from the same side.
The timers are in fact 40-bit values and the arithmetic is a bit involved for MSP430, so it makes sense to pass the timers to the OSS. This makes even more sense considering that (probably) some Tag/Peg-specific adjustments (calibrations) will have to be applied to them. Thus, the last leg of the handshake (i.e., the FIN packet) should arrive at a Peg to be forwarded to the OSS. Consequently, POLL packets should be sent by Tags. It can hardly be any other way, because keeping the receiver open in a Tag for any nontrivial amount of time is out of the question. The module facilitates some low power listening modes (akin to WOR) which have to be studied, if the preliminary tests turn out promising.
The timer resolution is formally about 1/63897600000s which roughly translates into about 5 mm at the speed of light (yeah, right). There is a healthy bit of guessing involved in the timing of those marker symbols. Moreover, some signals can get reflected, and so on. They suggest procedures and heuristics to detect and discard such signals (basically by looking into the very reach set of various quality indicators). There is no RSSI, but they say how it can be computed from those indicators in a rather messy sort of way.
# The interface

The device is started (initialized) with the following operation:
void dw1000_start (byte mode, byte role, word pan);
where:
mode	is one of 8 RF configurations (frequency, preamble, channel, etc.) which I have copied from the reference driver by DecaWave; so far I have only tried mode = 0
role	determines the node's role, i.e., which end of the handshake the node wants to play; 0 means Tag, 1 means Peg (also called anchor)
pan	is basically the network Id (the so-called PAN); nodes belonging to different networks will not talk to each other (similar to our Network Id)

Note: I could use our Network Id for the PAN, but the driver cannot assume that another radio (like CC1100, where the Network Id is prominent) is configured into the system. On the other hand, I am using our standard Node Id (the lower word of host_id, which is always known for every node) as the node's (short) address.
To switch the device off execute this:
void dw1000_stop ();
When the device is started with role 1 (Peg), the receiver is immediately switched on (note that it drains about 150mA) and the device begins to listen for POLL packets. Completed handshakes are communicated to the praxis as (compound) values arriving on a sensor (see BOARDS/OLIMEX_CCRF_DW1000 for the way that sensor is configured). A single value is described by this data structure (defined in dw1000.h):
 typedef struct {
word tag;	// Source
byte tst [6*DW1000_TSTAMP_LEN];	// Six time stamps
byte seq;	// Sequence number
} dw1000_locdata_t;
where:
tag	is the Tag Id of the handshake (the node sending the initial POLL packet)
tst	is a byte array storing the six time stamps produced by the handshake and consisting of 6*5 = 30 bytes (DW1000_TSTAMP_LEN is defined as 5); the byte offsets to the respective timers are represented by these constants (defined in dw1000.h): / #define DW1000_TSOFF_TSP (DW1000_TSTAMP_LEN * 0) / #define DW1000_TSOFF_TRR (DW1000_TSTAMP_LEN * 1) / #define DW1000_TSOFF_TSF (DW1000_TSTAMP_LEN * 2) / #define DW1000_TSOFF_TRP (DW1000_TSTAMP_LEN * 3) / #define DW1000_TSOFF_TSR (DW1000_TSTAMP_LEN * 4) / #define DW1000_TSOFF_TRF (DW1000_TSTAMP_LEN * 5) / The above ordering of the time stamps is forced by some driver implementation issues.
seq	is the handshake's sequence number (a single-byte value) arriving in the initial POLL packet (see below)

To retrieve the handshakes, the praxis should run an FSM with a state organized like this:
...
dw1000_locdata_t	location;
…
fsm … {
...
state EVENT:

read_sensor (EVENT, SENSOR_RANGE, (address)&location);
if (location.tag == 0) {
wait_sensor (SENSOR_RANGE, EVENT);
release;
}
...
If the tag attribute of the sensor value is zero, it means that there is no new handshake value to see. The sensor generates an event whenever a new handshake is received. Then, the tag attribute of the returned structure is set to the originating Tag Id.
When the node's role is 0 (Tag), the device is put to sleep after startup (the current drain is of order nanoamps). To start a handshake, the praxis has to store a value in an actuator (see BOARDS/OLIMEX_CCRF_DW1000 for the way that actuator is configured). The value consists of a single byte specifying the sequence number of the POLL packet, e.g.,
…
byte seq;
...
state POLL:
write_actuator (POLL, ACTUATOR_RANGE, (address)&seq);
...
If the driver is busy doing the previous handshake, the operation will block and auto-restart when ready.
A handshake is retried up to 4 times, if the RESP packet fails to arrive within 10 milliseconds after POLL. The Tag doesn't verify whether its FIN packet makes it to the Peg. Its end of the handshake completes with the departure of the FIN packet.