Pawel Gburzynski

# P i c O S
LCD-G interface

Version 0.91
May 2009

© Copyright 2008-2009, Olsonet Communications Corporation.
All Rights Reserved.
# Preamble

This note describes the praxis interface to graphic LCD under PicOS. At the moment, the only LCD with this interface is Nokia 6100 equipped with Philips (PCF8833) or Epson (S1D15G10) controller.

Note: the controller version is Philips by default. To select the Epson controller, include this setting:

#define LCDG_N6100P_EPSON 1

in board_lcd.h or in options.sys. This setting only affects the low-level driver (file lcdg_n6100p.c).

The present praxis interface consists of two parts: basic operations provided by the driver and a library of functions implementing simple stacking of displayable objects on the screen (including menus).
# Basic operations

The LCD offers raw access to individual pixels with no built-in text functionality. A single pixel can be in at least two states, possibly more. The pixels are organized into a rectangular display area, with each pixel being (in principle) addressable and settable independently of other pixels. In particular, Nokia 6100 has 132x132 pixels. Each pixel can be set to an arbitrary 12-bit value representing a color. Boundary pixels are deemed unusable, i.e., for all practical purposes the display consists of 130x130 pixels. The driver ignores the boundary lines of pixels (never touches them) assuming that the display is organized into 130 rows and 130 columns addressed from 0 to 129 (up to down and left to right. Other modes regarding the representation of colors are theoretically available (e.g., 8-bit colors). Those modes have been tried and discarded as not very useful.

Text operations are optional depending on the availability of fonts. To avoid overtaxing the code flash, fonts are stored in EEPROM. Thus, EEPROM is a required configuration option for text operations. The EEPROM must be preloaded with fonts, and the starting address of the font file in EEPROM must be made available to the driver. This is accomplished by setting the constant LCDG_FONT_BASE (typically in board_pins.h) to the respective EEPROM address. If this constant is not defined, text operations are not available.

void lcdg_on (byte con)

The operation switches on the display, i.e., the display will actually show its contents. When the display is off (see below), it will accept content-rendering commands, but the image will not show. For example, if the rendering operation is messy (and you would prefer not to show to the user how the individual pixels are being processed), you may switch the display off, render the image, and then switch the device on when everything is ready and nice.

The argument gives the contrast, with zero standing for the default value of 55. Feel free to try other values.

void lcdg_off ()

The operation switches the display off (see above). The display is off by default.

void lcdg_set (byte xl, byte yl, byte xh, byte yh)

The operations sets a bounding rectangle, which is typically intended as a container for some object to be displayed. For example, in order to render a picture or a text area, you have to set its bounding rectangle first. The arguments are coordinates of two points: xl and yl stand for the coordinates of the left upper corner, and xh, yh are the coordinates of the lower right corner. Note that the x coordinate grows left to right, and the y coordinate grows top to bottom. This assumption is consistently followed in the rest of this document.

For example,

lcdg_set (0, 0, 129, 129);

sets the maximum possible bounding rectangle for Nokia 6100.

Two symbolic constants: LCDG_MAXX and LCDG_MAXY describe the maximum x and y coordinates allowed for the particular LCD device. They are 129/129 for Nokia 6100.

void lcdg_get (byte *xl, byte *yl, byte *xh, byte *yh)

The function returns via the arguments the current setting of the bounding rectangle. Any of the four pointers can be NULL, in which case the corresponding value will not be returned.

void lcdg_setc (byte bgr, byte fgr)

The operation sets the background and foreground colors, e.g., for text rendering. This is the list of colors (color numbers) that are currently available:

#define COLOR_WHITE	0
#define COLOR_BLACK	1
#define COLOR_RED	2
#define COLOR_GREEN	3
#define COLOR_BLUE	4
#define COLOR_CYAN	5
#define COLOR_MAGENTA	6
#define COLOR_YELLOW	7
#define COLOR_BROWN	8
#define COLOR_ORANGE	9
#define COLOR_PINK	10

If an argument to lcd_setc is not one of the above numbers, then it will be ignored, i.e., the corresponding setting will not change. The default colors are background = COLOR_BLACK, foreground = COLOR_WHITE.

void lcdg_clear ()

The function erases the current bounding rectangle by filling it with the background color.

void lcdg_render (byte c, byte r, const byte *pix, word n)

The function is normally called in the course of rendering a picture. It fills n pixels in the current bounding rectangle starting from the pixel with coordinates c, r relative to the left upper corner of the rectangle. The values to which those pixels are set are taken from pix, which should contain at least n values of the proper size. For Nokia 6100, two pixels take three bytes (two packed 12-bit values). If n is odd, the lower nibble of the last byte in pix is ignored.

Note that the operation automatically wraps around when attempting to cross the right edge of the bounding rectangle.

In the Seawolf project (for which the present interface has been implemented) pictures are stored (in EEPROM) as sequences of 56-byte “chunks” that need not occur in any particular order.[1] Each chunk contains its number, which implicitly specifies a pair of coordinates (describing the location of the starting pixel) and 54 packed bytes representing the values of up to 36 pixels. Such a chunk is naturally displayed by a simple call to lcdg_render.
[1] This is described in a separate document.

word lcdg_font (byte f)

The function sets the font for a subsequent text rendering operation. The argument represents the font index, and its range corresponds to the number of fonts available in the font file in EEPROM. The operation fails when the specified font index is out of range, or if the font file doesn't exist. There are three fonts at present (or, rather, one font with three different sizes [sort of] labeled 0, 1, 2).

The present implementation only allows fixed-size fonts.

Note: there is no default font. If you want to render text, you have to issue lcdg_font beforehand, at least once.

The function returns zero on success and nonzero on failure.

byte lcdg_cwidth ()
byte lcdg_cheight ()

The functions return the width and height (in pixels) of the current font (note that all characters are the same width and height). The size includes spacing.

word lcdg_sett (byte x, byte y, byte nc, byte nl)

The operation can be viewed as a variant of lcdg_set to set up a bounding rectangle for a text. It requires a current font definition, so it must be preceded by a call to lcdg_font. As for lcdg_set, the first two arguments are the coordinates of the left upper corner of the bounding rectangle. The remaining two arguments specify the number of characters in one line (nc) and the number of lines (nl). Based on the character size for the current font, the function calculates the pixel coordinates of the right lower corner and issues a pertinent call to lcdg_set. If needed, those coordinates can be then obtained by a call to lcdg_get (see above).

The function returns zero on success. It fails (returning nonzero) if the rectangle cannot be determined (because there is no font definition), or if the rectangle is too large (i.e., it doesn't entirely fit on the screen).

void lcdg_wl (const char *s, word sh, byte cx, byte cy)

The operation displays one line of text (described by string s) in the current bounding rectangle (e.g., created with a preceding call to lcdg_sett). The second argument is the shift count indicating the number of characters in s to be skipped from the left. The last two arguments are the character coordinates of the first displayed character, e.g., cx = 3, cy = 5 means that the first character will appear in the fourth character position counting from the left edge of the bounding rectangle, and in the sixth row (line) of the rectangle. Any characters that fall outside the rectangle are clipped out.

If sh is greater than or equal to the number of characters in s, the operation is void. The role of this argument is to provide for horizontal scrolling whereby some initial portion of the line has been shifted out off the left edge of the bounding rectangle.

The displayed characters are rendered in the current foreground color (as defined by lcdg_setc) against the current background color.

Note that the function returns no value. If the text cannot be rendered (because no font is defined), its action is void.

void lcdg_ec (byte cx, byte cy, byte nc)

The function erases (i.e., fills with the background color) nc characters in the current bounding rectangle starting at character position cx, cy (coordinates as for lcdg_wl). The operation only affects one line of the area, i.e., it doesn't wrap past the right edge of the bounding rectangle. Similar to lcdg_wl, it fails silently and does nothing if no font is defined.

void lcdg_el (byte cy, byte nl)

The function erases (i.e., fills with the background color) nl entire lines in the current bounding rectangle starting at line number cy. The operation never affects any pixels below the lower edge of the bounding rectangle, e.g., if nl happens to be larger than the rectangle's capacity. Similar to lcdg_wl, it fails silently and does nothing if no font is defined.

# Display manager

The functions discussed in this section (defined in files lcdg_dispman.c and lcdg_dispman.h in PicOS/Libs/LibLCDG) allow you to represent a simple hierarchy of displayable objects, including pictures, text areas, as well as scrollable and selectable menus. You have to insert:

#include “lcdg_dispman.h”

in the header section of your program to make them available to the praxis.

A displayable object is described by one of these types (declared in lcdg_dispman.h).

lcdg_dm_img_t	a picture
lcdg_dm_tex_t	a piece of text
lcdg_dm_men_t	a menu

These types are structures sharing a common initial chunk of data represented by type lcdg_dm_obj_t. This means that it makes sense to cast any of the three specific object types to type lcdg_dm_obj_t as long as you are only interested in the shared attributes of all displayable objects. Those shared attributes are:

byte	XL, YL, XH, YH;
lcdg_dm_obj_t	*next;
address	Extras;
byte	Type;

The first four numbers describe the bounding rectangle of the object, attribute next is needed to organize multiple objects into a list, and Type describes the actual object type (and determines the layout of the remaining portion of the object structure). Its two least significant bits (which can be extracted by and-ing Type with the constant LCDG_DMTYPE_MASK) can store one of these values LCDG_DMTYPE_IMAGE (0), LCDG_DMTYPE_MENU (1), LCDG_DMTYPE_TEXT (2). The remaining bits of Type are available for storing flags. One such flag, 0x80 (LCDG_DMTYPE_FDATA) is used internally in the present version. When set, it means that when the object is freed (by lcdg_dm_free – see below), the data structures pointed from it should be freed as well. This applies to menus and text objects, which contain pointers to lines (those lines can be allocated by umalloc and may thus have to be deallocated when the object is destroyed). The Extras attribute is reserved for the praxis and can be used to store a pointer to some auxiliary data related to the object. I am not sure if it is really needed.

At any time, the display manager knows the current hierarchy of objects to be shown on the screen. Those objects are described by a list (we shall call it the display list) headed at LCDG_DM_HEAD (a global variable of type lcdg_dm_obj_t*). This list can be empty, in which case LCDG_DM_HEAD contains NULL. Another global variable of the same type, LCDG_DM_TOP, points to the last object on the display list, which is called the top (or current) object. LCDG_DM_TOP is NULL if the display list happens to be empty.

The following six functions can be used to create objects of the specific types. All of them assume that the positions of those objects are specified at the moment of creation. Note that a created object is not automatically displayed. Typically, lcdg_dm_newtop (see below) is called after an object creation to show the object on the screen and make it the current (top) object.

The first three functions, i.e., lcdg_dm_newimage, lcdg_dm_newtext, and lcdg_dm_newmenu, are made available (i.e., are compiled in) if the constant LCDG_DM_SOFT_CREATORS is defined as nonzero. The default setting of this constant is 2. It can be overridden by including an explicit definition, e.g.,

#define LCDG_DM_SOFT_CREATORS	0

in the praxis's options file. The constant also selects between two header formats for the functions: long (2) and short (1). With the long format, the respective function takes more arguments, which all have to be mentioned explicitly when the function is called. With the short format, the sequence of byte arguments is passed in an array, which may be a more convenient choice when those arguments are read from some place as a contiguous chunk. The advantage is most visible for lcdg_dm_newtext, and lcdg_dm_newmenu, which functions take many arguments.

Long format:

lcdg_dm_obj_t *lcdg_dm_newimage (	word ihandle,
            byte x,
            byte y);

Short format:

lcdg_dm_obj_t *lcdg_dm_newimage (word ihandle, byte *args);

The function creates an image (picture) object. The first argument is the image handle, which can be returned, e.g., by a call to lcdg_im_find (as described further in this document). The last two arguments (in the long format) specify the left top corner of the picture's bounding rectangle. The coordinates of the right bottom corner of the bounding rectangle are determined from the picture's dimensions. With the short format, the two coordinates are passed as the first two elements of args.

The function returns the new object or, possibly, NULL indicating a failure. In the latter case, the reason for the failure is stored in global variable LCDG_DM_STATUS of type byte. Generally, this variable can take the following values (not all of them are applicable to pictures):

0	no problem (last operation has succeeded)
LCDG_DMERR_NOMEM	memory allocation (umalloc) failure
LCDG_DMERR_GARBAGE	format error (bad image handle)
LCDG_DMERR_NOFONT	font unavailable
LCDG_DMERR_RECT	bounding rectangle out of screen

For example, if the sum of one of the corner coordinates (x or y) and the respective dimension of the picture (as stored in EEPROM) turns out to be greater than the screen size, the function will return NULL, and LCDG_DM_STATUS will be set to LCDG_DMERR_RECT.

Note that umalloc failures (LCDG_DMERR_NOMEM), if they happen at all, can be intermittent, which means that it may make sense to retry the same operation later. Other failures are fatal and indicative of more fundamental problems.

Long format:

lcdg_dm_obj_t *lcdg_dm_newtext (char *str, byte x, byte y,
  byte font, byte bgr, byte fgr, byte w);
Short format:

lcdg_dm_obj_t *lcdg_dm_newtext (char *str, byte *args);

The function creates a text object. The first argument is the character string to be shown on the screen. Newlines, as well as any non-printable characters, are converted to blanks, i.e., the string is effectively treated as a single line.

The next two arguments (in the long format) provide the coordinates of the left upper corner of the bounding rectangle for the text object. The width of that rectangle in characters is w, and its height accounts for the number of lines resulting from wrapping the specified string (as many times as needed) at the rectangle's right edge. The remaining arguments (font, bgr, and fgr) identify the font and two colors: background and foreground.

For example, assuming that w is 12, this string “a quick brown fox jumps over the lazy dog” will produce 4 lines rendered like this:

a quick brown
fox jumps ove
r the lazy do
g

The possible failure codes for this operation are LCDG_DMERR_NOMEM, LCDG_DMERR_NOFONT (the specified font is not available), and LCDG_DMERR_RECT (the resultant bounding rectangle does not entirely fit on the screen).

The string passed to lcdg_dm_newtext must not be deallocated for as long as the text object is supposed to live (the object will point to the original rather than creating its private copy). The function sets the LCDG_DMTYPE_FDATA flag in the object's Type attribute, which will instruct lcdg_dm_free (see below) to deallocate (by calling ufree) the line of text passed as the argument to lcdg_dm_newtext. Thus the function “guesses” that the string has been allocated dynamically and it is the praxis's intention to deallocate it when the object ceases to exist. If this is not the case, the praxis has two options: 1) clear the flag before calling lcdg_dm_free for the object, 2) deallocate the object by calling ufree rather than lcdg_dm_free (i.e., to do the cleanups by hand).

In the short format, all the byte arguments are passed in the consecutive elements of the args array.

Long format:

lcdg_dm_obj_t *lcdg_dm_newmenu (	char *lines,
            word nl,
            byte x, y,
            byte font,
byte bgr, byte fgr,
            byte w, byte h);
Short format:

lcdg_dm_obj_t *lcdg_dm_newmenu (	char *lines,
            word nl,
            byte *args);
The function creates a menu. The first argument is an array of NULL-terminated character strings constituting the list of menu entries. The number of strings (lines) in this array should be equal to nl. This array will not be replicated, i.e., it should remain untouched for as long as the menu object exists. The next six arguments (in the long format) have the same meaning as for lcdg_m_newtext. Note that the first character position (column) of a menu is reserved for the pointer to current selection; thus, the actual entries will be displayed starting from position 1. The width specification (w) stands for the total character width of the object's bounding rectangle. Also, h specifies the rectangle's height in characters.

In contrast to a text object, a menu line is never wrapped at the end of the bounding rectangle, but scrolled out (truncated). Also, it is quite common for a menu to contain more lines than can simultaneously fit into the rectangle (nl > h). Scrolling operations are available (see below) to make different portions of the menu visible within the rectangle.

Similar to lcdg_dm_newtext, he function sets the LCDG_DMTYPE_FDATA flag in the object's Type attribute – to notify lcdg_dm_free that the lines (together with the array of pointers to them) should be deallocated along with the object.

With the short variant, the byte arguments are passed in the args array, in the same order as with the long version.

These three functions are made available (i.e., are compiled in) when the constant LCDG_DM_EE_CREATORS is set to nonzero. The default setting of the constant (which can be overridden from the praxis's options file) is 1.

lcdg_dm_obj_t *lcdg_dm_newimage_e (lword ep);
lcdg_dm_obj_t *lcdg_dm_newtext_e (lword ep);
lcdg_dm_obj_t *lcdg_dm_newmenu_e (lword ep);
The functions create new displayable objects by reading their layouts from EEPROM starting at address ep. They can be used in the situation when the EEPROM contains pre-compiled objects in the format readily acceptable by the display manager (i.e., direct memory images of the object structures). The objects are loaded from the EEPROM using the EEPROM object loader (the ee_ol module) described in a separate document. Each function returns the object pointer upon success and NULL on failure. The latter case can happen in two circumstances: 1) there is no memory to accommodate the object (LCDG_DM_STATUS returns EE_LOADER_NOMEM), 2) the EEPROM area pointed to by ep does not contain something that looks like a legitimate object of the corresponding type (LCDG_DM_STATUS returns EE_LOADER_GARBAGE).

An object prepared for storage in EEPROM, should have the LCDG_DMTYPE_FDATA flag cleared in its Type attribute. This is because an object whose complete layout is read from EEPROM is always allocated and deallocated as a single memory structure. For example, the recommended way of organizing a complete menu object as a chunk of EEPROM storage to be read by lcdg_dm_newmenu_e is to put the Lines array behind the object structure, and follow that array by the strings representing the lines. See the EPPROM Object Loader document for details.

This operation deallocates a displayable object (of any of the three types);

   void lcdg_dm_free (lcdg_dm_obj_t *o);

Basically, it executes ufree on the pointer, but, if the object happens to be a text or a menu, it also examines the LCDG_DMTYPE_FDATA flag. If this flag is set, the function will also deallocate the line (or lines, for a menu object). In the latter case, the function will first deallocate all the individual lines pointed to by the Lines array, and then deallocate the array itself. This is accomplished by calling lcdg_dm_csa (see below).

Here are the operations that render objects on the screen.

byte lcdg_dm_newtop (lcdg_dm_obj_t *o);

The function displays the object pointed to by the argument and makes it the new top object. If the object already happens to be the top object, its image is just refreshed. If the object is not present on the display list, it is added as a new object (the list grows). If the object occurs somewhere on the list (but it isn't the top object), it is moved to the top.

The operation invokes this function, which is also available for general use:

word lcdg_dm_display (lcdg_dm_obj_t *o);

Its responsibility is to render a single object pointed to by its argument. That object need not be present on the display list.

The function sets LCDG_DM_STATUS to zero (upon success) or to an error code (see above). The setting of LCDG_DM_STATUS is also returned as the function value.

Theoretically, once an object has been successfully created, its subsequent display attempts can only fail with code LCDG_DMERR_NOMEM. Such errors are generally intermittent and they may never occur under sane circumstances. The memory requirements of lcdg_dm_display are quite modest, but the function does invoke umalloc.[2] Note, however, that if the contents of EEPROM are changed after an object has been created (e.g., a font is removed, a picture is replaced), then lcdg_dm_display may fail in a confusing way, e.g., signaling LCDG_DMERR_NOFONT or LCDG_DMERR_GARBAGE.
[2] Perhaps it doesn't have to. A small buffer area is needed for rendering a picture, which could be declared statically in RAM.

A failure to display an object means that not even a fragment of the object has appeared on the screen. Thus, such a failure will not mess up the display.

The value returned by lcdg_dm_newtop (as well as its setting of LCDG_DM_STATUS) are those of lcdg_dm_display invoked to do the actual rendering.

Note that, by using lcdg_dm_display directly, you can display an object from outside the display list. If you subsequently want to revert to the top object from the list, you should invoke lcdg_dm_dtop (see below) which will bring the top object back to the front. While any object can be easily brought to the front, there is no automatic and efficient way to remove a displayed object, such that it disappears from the screen and uncovers the objects that it was obscuring. The only way to clear the screen of garbage is to call this function:

byte lcdg_dm_refresh ();

which scans through all objects from the display list, starting from LCDG_DM_DHEAD, and renders them in turn (by calling lcdg_dm_display). If no object from the display list covers the entire screen, then the screen is cleared (to COLOR_BLACK) before this action is started. If the display list is empty, the screen is just cleared. Thus, it makes sense to call lcdg_dm_refresh upon initialization.

Note that lcdg_dm_refresh returns a value. The function assumes that it has failed (and stops scanning the display list) upon the first failure of lcdg_dm_display invoked in its course. Then, the value returned by lcdg_dm_refresh, as well as the setting of LCDG_DM_STATUS, are those of the failing lcdg_dm_display. If all invocations of lcdg_dm_display have succeed, the function returns zero.

lcdg_dm_obj_t *lcdg_dm_remove (lcdg_dm_obj_t *o);

The function deletes the indicated object from the list and returns its pointer. Normally, the returned value is the same as the argument, except when the argument is NULL, in which case the function deletes from the list the top object (and returns its pointer). Note that this object can also be NULL (in that case nothing happens, and the function returns NULL).

If the specified object does not occur on the list, the function does nothing and returns the argument.

If the top object from the display list is deleted, then the preceding object moves to the top. That new top object is then displayed (refreshed with lcdg_dm_display) overwriting any possible objects obscuring it. If the list becomes empty (there is no new top object), the screen is cleared to COLOR_BLACK. The error status of lcdg_dm_display implicitly invoked by lcdg_dm_remove to bring the new top object to the front can be verified by reading LCDG_DM_STATUS.

Note that the object deleted from the list by lcdg_dm_remove is not deallocated (freed), which is left up to the praxis.

byte lcdg_dm_update (lcdg_dm_men_t *m, word ln);

The function re-displays the ln-th line of the menu pointed to by m, but only if the menu happens to be the current top object; otherwise, it does nothing. Intended as a more efficient tool to update the current menu, instead of redisplaying it completely.

Boolean lcdg_dm_shown (const lcdg_dm_obj_t *o);

The function returns YES if the specified object is present on the display list and NO otherwise.

byte lcdg_dm_dtop ();

The function refreshes (re-displays) the top object. If there is no top object (i.e., the display list is empty), the screen is cleared to COLOR_BLACK. For example, it may make sense to call it after lcdg_dm_display, if the object displayed by the latter function is not on the display list (and lcdg_dm_remove will not automatically revert to the previous top object).

The function returns the status of lcdg_dm_display invoked to render the top object.

Four special operations are available for menu objects. Initially, when a menu object is created, its selection pointer points to the first entry, i.e., line number zero. This pointer is available as attribute SE of type word declared in lcdg_dm_men_t (see lcdg_dispman.h). Its value can be read, but it should not be set directly. For purists, this function (macro) can be used to reference the SE attribute in a less explicit way:

   #define	lcdg_dm_menu_c(m)	(((lcdg_dm_men_t*)(m))->SE)

The value of SE is interpreted as the index of currently selected line between zero and N-1, where N is the total number of entries in the menu.

The following functions are provided to be called in response to events triggered by pressing buttons or moving a joystick. They assume that the menu object specified as the argument is active, i.e., it is the frontmost object on the screen.

void lcdg_dm_menu_d (lcdg_dm_men_t *m)
void lcdg_dm_menu_u (lcdg_dm_men_t *m)
void lcdg_dm_menu_l (lcdg_dm_men_t *m)
void lcdg_dm_menu_r (lcdg_dm_men_t *m)

The first two functions move the selection pointer one position down and up, respectively. Nothing happens if the pointer is already at the boundary (at entry zero for lcdg_dm_menu_u, or at the last entry for lcdg_dm_menu_d). When the cursor crosses the boundary of the menu's rectangle, and scrolled out entries are present in its direction, new entries are automatically scrolled in. The SE attribute is updated to reflect the new selection.

The last two functions are used for horizontal scrolling, which is useful if the current set of entries displayed within the bounding rectangle contains lines longer than the rectangle's width. Thus, lcdg_dm_menu_l shifts the view one position to the left, while lcdg_dm_menu_r scrolls the rectangle one position to the right. The scrolling stops if no new characters can be exposed. The functions do not affect the SE attribute.

Here are two more functions that appear generally useful in the context of menus:

char **lcdg_dm_asa (word n);

This function allocates an array to store n strings and returns its pointer or NULL, if umalloc fails. In the latter case, LCDG_DM_STATUS is set to LCDG_DMERR_NULL. If the array has been successfully allocated, it is filled with NULL pointers. Such an array can be subsequently filled with string pointers and used for a dynamically created list of menu items, i.e., the first argument of lcdg_dm_newmenu.

void lcdg_dm_csa (char **lines, word n);

This one deallocates the specified array of strings of size n, assuming that all the strings as well as the array itself were previously allocated with umalloc. Any entries in lines that are NULL are not deallocated. For many menus, the array of lines is created dynamically by the praxis, so it must be cleaned up when the menu is destroyed.

# The image handling module

The functions pertaining to image processing are contained in files lcdg_images.c and lcdg_images.h in directory PicOS/VLibs/LibLCDG. They cover image lookup in EEPROM, rendering, as well as OEP hooks for image transmission over unreliable links.

Images are stored in EEPROM in such a way that one picture occupies an entire number of 8KB pages. Note that those pages are logical, i.e., the 8KB size is not necessarily related to any physical properties of the EEPROM, although, of course, the fact that that size is a nice power of 2 is not without a significance. The pages constitute a (somewhat crude) unit of storage allocation for images, and the 8KB size of that unit reflects a tradeoff between fragmentation and the ease of lookup. The image handling module must be initialized by a call to this function:

void lcdg_im_init (word fp, word np);

where fp is the number of the first EEPROM page (8KB chunk) to be used for image storage, and np is the total number of pages used for this purpose. If np is zero or extends beyond the EEPROM size, the image area will comprise the entire trailing portion of EEPROM starting at address fp x 8KB. On the hand, if fp falls beyond the EEPROM size, the function will trigger a system error.

Normally, if the EEPROM already contains some images, the praxis should know the bounds of the image area and specify them properly with an initial call to lcdg_im_init. If the EEPROM has been physically erased, the area will be automatically recognized as containing zero images, i.e., no specific initialization is required in such a case.

word lcdg_im_find (const byte *lbl, byte len, word pn);

This function can be used to locate an image by its label. The first two arguments describe the label, which can be any string of bytes (not necessarily ASCII characters) of the specified length (len) between 0 and 38. If len is less than 38 (which is the total size of the fixed label area of an image), then the first len bytes in lbl must be identical to the first len bytes in the image's label for a match. This also means that if len is zero (in which case lbl is irrelevant and can be NULL), any image matches the search. The last argument (pn) can be used to start the search from a particular place (e.g., where previously stopped), which makes it possible to scan through all the images currently stored in EEPROM.

The function returns either WNONE (0xFFFF) or the so-called image handle, which is simply the pointer (number) to the image's first page. If the last argument is WNONE, the search will begin from the very first page of the image area in EEPROM. Otherwise, the search will start at page pn+1. This way, by setting pn to the previously located handle (other than WNONE), you can start effectively continue the previous search. In particular, here is a loop that scans through all the images:

   pn = WNONE;
   while ((pn = lcdg_im_find (NULL, 0, pn)) != WNONE) {
      ... process the image pointed to by handle pn ...
   }

The simplicity of the search scheme consists in the fact that it is easy to identify the first page of an image by looking at its first two bytes (the magic code). That first page, among other things, contains pointers to the remaining pages (if any) representing the complete image.

byte lcdg_im_hdr (word pn, lcdg_im_hdr_t *hdr);

Given a valid image handle (pn), the function returns (via hdr) the image header, which is a structure with the following layout (declared in lcdg_images.h):

   typedef struct {
byte X, Y;
byte Label [38];
   } lcdg_im_hdr_t;

where X and Y are the image dimensions in pixels, and Label is the complete label.

The value returned by the function indicates success or failure in a manner similar to the functions described earlier. Thus, zero means success, i.e., the handle was valid, and the structure pointed to by hdr has been filled with the image's header. Otherwise, in this case, the value can only be LCDG_IMGERR_HANDLE, which means that the handle doesn't seem to point to the first page of a valid image.

byte lcdg_im_disp (word pn, byte x, byte y);

Given a valid image handle (pn), the function renders the image on the display, with x and y standing for the left top corner coordinates. In particular, the lcdg_dm_display function of the display manager (see the previous section) invokes lcdg_im_disp in the course of its action.

The function returns zero on success. The possible error codes are:

   LCDG_IMGERR_HANDLE	the specified handle doesn't point to a valid image
   LCDG_IMGERR_NOMEM	memory allocation failed
   LCDG_IMGERR_GRBAGE	the image structure in EEPROM appears damaged

The amount of dynamically allocated memory needed by the function to do its job is about 70 bytes.

Some of the error codes returned by the image-related functions coincide with those returned by functions in related modules. For example LCDG_IMGERR_NOMEM and LCDG_DMERR_NOMEM translate into the same value (17), which is the same as OEP_STATUS_NOMEM. Also, LCDG_IMGERR_GARBAGE and LCDG_DMERR_GARBAGE are identical (33).

Note that the image rendered by lcdg_im_disp will only show up on the screen if the display is turned on (see lcdg_on above).

word lcdg_im_free ();

This function returns the number of free pages available in the declared image area of EEPROM.

byte lcdg_im_purge (word pn);

This function removes the image pointed to by the specified handle reclaiming its pages (marking them as free). The values returned are the same as for lcdg_dm_disp.

If the set of images stored in the EEPROM includes one with the label “wallpaper” (the first 10 bytes of the label looking like the NULL-terminated ASCII string “wallpaper”), that image will be used by the display manager as the background (instead of the default blank screen). The background is drawn, e.g., by lcdg_dm_refresh; in particular, if the list of objects to be displayed is empty, lcdg_dm_refresh will simply clear the screen.

The first time the display manager has to draw the background, it tries to locate an image whose label is “wallpaper”. If such an image is found, then its handle is stored to be used for subsequent renderings of the background without the need to scan the image area for a matching label. If there is no such image, the display manager will not try to look it up again. Thus, the wallpaper image must be present in the EEPROM before the first background rendering to be effective.

## OEP functions for exchanging images

The following functions implement image transfer over OEP. Please consult the OEP document before reading this part.

As explained in the OEP document, the praxis should first negotiate the exchange of an image in its private way. On the sender side, the image (which must be stored in local EEPROM) is represented by its handle, e.g., obtained by invoking lcdg_im_find (see above). The sender will also learn from the receiver the requisite values of LID (link ID) and RQN (the request number). The sender must in turn communicate to the receiver the parameters of the image, which come as the contents of the header structure (lcdg_im_hdr_t). The receiver will calculate the number of chunks comprising the image from the X, Y dimensions stored in the header.

Thus, in order to receive an image, the receiver calls this function:

byte oep_im_rcv (const lcdg_im_hdr_t *hdr, byte xd, byte yd);

where hdr points to the image header, and the remaining two parameters are optional. They indicate the coordinates of the left upper corner on the screen for rendering the image simultaneously with its reception (and storage in EEPROM). If the image is just to be received and stored (without being displayed at the same time), xd should be BNONE (0xFF). The value of yd is then irrelevant.

For its end, the sender should invoke:

byte oep_im_snd (word ylid, byte yrqn, word pn);

where ylid and yrqn are link ID and request number obtained from the receiver, and pn is the image handle.

Each of the two functions will build some data structures needed by the chunk handlers during the exchange and invoke oep_rcv/oep_snd to do the job. The value returned by oep_im_rcv or oep_im_snd should be interpreted in the same way as the status value returned by oep_rcv or oep_snd. In particular, zero means that the operation has been successfully started and the praxis should now await is completion with oep_wait. Any nonzero value means failure. In addition to the OEP failure codes, the above functions can also return these values: LCDG_IMGERR_HANDLE (the handle for oep_im_snd is not valid), LCDG_IMGERR_NOMEM (failed memory allocation, both functions), LCDG_IMGERR_GARBAGE (corrupted image file for oep_im_snd, or illegal X, Y values in the header for oep_im_rcv), LCDG_IMGERR_NOSPACE (insufficient number of free pages to accommodate the image for oep_im_rcv).

Once the given end of the transfer has been successfully started (the corresponding function has returned zero), the praxis should use oep_wait (see above) to await its (successful or failed) completion. When that happen, the praxis should call this function:

void oep_im_cleanup ();

which will clean up after the exchange, i.e., deallocate the dynamic structures used by the respective chunk handler. Note that the cleanup function should only be called after a successful initialization of the exchange. There is nothing to clean up if the initialization has failed (i.e., oep_im_snd or oep_im_rcv has returned a nonzero status).

## Appendix: Image formats

Images acquired are stored in EEPROM in such a way that one image occupies an entire number of 8KB (logical) pages. The image module identifies a contiguous range of 8KB pages to be used for storing images. A page falling within that range can be of one of three kinds:

- Free, if its first two bytes look like 0xFFFF. In particular, immediately after the EEPROM is erased, all pages are free.
- The first page of an image. Such a page has 0x7F00 (little endian) in the first two bytes. When looking for a specific image, or counting images stored in the EEPROM, the praxis only looks at such pages.
- Other. Normally, such a page belongs to an image as one of its subsequent (non-first) pages. It is theoretically conceivable that the image area stores objects other than images. In such a case, the pages of those object must not start with 0xFFFF or 0x7F00. Then, they will never be used for storing images or interpreted as parts of images.

Figure 1: The first page of an image stored in EEPROM.

Any page belonging to an image consists of an entire number (up to 146) of 56-byte chunks. As 8192 is not divisible by 56, the last 16 bytes of every page are unused. Their contents are irrelevant, but it makes sense to keep them all ones (0xFF).

All chunks except for the first chunk of the first page (see Error: Reference source not found) contain descriptions of image pixels. One pixel is described with 12 bits packed in such a way that three consecutive bytes represent two consecutive pixels of the image. The first word of a chunk stores the chunk number between 0 and the total number of chunks in the image – 1. The chunk number is required, as the chunks need not be stored in order. As their reception may not be reliable, the received chunks are simply written to the flash in whatever order they arrive (some of them being missing and retransmitted later). This way the access to EEPROM is simpler and faster.

The first chunk of the first page of an image has a special purpose. Its fields are interpreted as follows:

Bytes 0-1	0x7F00 (this is the magic code identifying the first page of an image).
Bytes 2-3	The total number of pages in the image, including the first page.
Bytes 4-13	This is a 5-word array containing the numbers of all pages occupied by	the image, starting with this page number. Only the number of entries	indicated in bytes 2-3 are valid. A page number is the address of the	first byte of the page shifted by 13 bits to he right.
Bytes 14-15	The total number of chunks in the image excluding the first (header	chunk), i.e., the total number of pixel chunks.
Byte 16	The X dimension, i.e., the row size (or the image width) in pixels. The	maximum legitimate width is 130.
Byte 17	The Y dimension, i.e., the column size (or the image height) in pixels.	The maximum legitimate height is 130.
Bytes 18-55	The image label, i.e., an arbitrary sequence of 38 bytes.

The maximum number of pages that a single image may occupy is 5. Note that a continuation (non-first) page will begin with a chunk number, which can never be larger than 4 x 146 = 584. Thus, a continuation page cannot accidentally pose for an empty page or the first page of an image.

In addition to the EEPROM format for images, there is another format in which images can be stored in regular files before being downloaded into EEPROM (or converted to EEPROM format). The recommended procedure for creating such downloadable images is al follows:

1. Convert the original image (e.g., in JPEG format) to a 130 x 130 pixels standard Windows bitmap format with 24 bits per pixels.
2. Run the bitmap file through a conversion program (script) named cbm.tcl in the following way:

cbm.tcl -l label sourcefile.bmp targetfile.lcd

where label is the string describing the contents of the label field of the image's first chunks, sourcefile.bmp is the bitmap version of the image and targetfile.lcd represents the target file where the converted copy of the image will be written.

If the -l argument is present, label is interpreted as a character string whose initial 38 characters will be put into the label field. If the string is shorter than 38 characters, then the remaining bytes of the label will be filled with zeros.

An alternative variant of the label argument is -ln list_of_numbers, where list_of_numbers may consist of comma separated integer values, e.g.,

   cbm.tcl – ln “1,2,-10,0xfffccc,999” myphoto.bmp myphoto.lcd

Each number is interpreted as a 32-bit little endian value to be stored into four consecutive bytes of the label area. As before, any bytes in excess of 38 are ignored, while any leftover trailer of the label area is filled with zeros.

If the -l argument is absent, the image is assigned a default label obtained from the target file name by removing any directory prefix as well as the suffix and converting the remaining characters to lower case. For example, if the target file name is /home/pawel/MyImage.nok, the default label will be the string myimage. with the remaining bytes of the label field filled with zeros. If the string obtained this way is longer than 38 characters, the excess characters are ignored.

The image format created by cbm.tcl is even simpler than the EEPROM format (the file is continuous, so there is no need to deal with pages). The file starts with the 16-bit little endian word 0x77AC (used as a magic code), followed by two bytes storing the X and Y dimensions of the image, followed in turn by 38 bytes of the label. This 42-byte header is followed by the pixel codes. The total number of bytes expected in that area is at least X x Y x 12 / 8. They can be cut into 54-byte chunks numbered from zero up. The last chunk need not be full (i.e., the pixel area need not be a multiple of 54 bytes), if the total number of pixels in the image does not warrant a full chunk at the end.