# Agent message formats

(All sequences in network format)

## Handshake

Client:
0xBA 0xB4 MC MC NN NN NN NN
CC - module code
NN - node number

Server:
0x00 SV SV SC
SV - status value
SC - status code

Module codes:
1	UART
2	PINS
3	LEDS
4	ROAMER
5	PANEL
6	CLOCK
7	SENSORS
8	LCDG
9	PTRACKER
10	EMUL

Status codes:
0	wrong magic sequence
1	node number out of range
2	illegal (unimplemented) request code
3	some agent is already connected to this particular module
4	timeout (no polling sequence is 30 seconds)
5	no socket interface for the module
6	closed connection (never received)
7	request format error (too long)
8	illegal request
128	the node has no such module

Status value:
UART rate / 100 (used only for UART)

Once a connection has been started (following the handshake) the messages are textual (lines of text terminated with newlines).

## ROAMER (module code 4)

The client queries the server for a node:

Q n
n is SMURPH node number (unsigned dec)

Response to Q arriving from the server:

P n h total x y m name <leds,pins> [vcolor,vlabel]
n	SMURPH node number (corresponding to the query)
h	host node number (unsigned dec)
total	total number of nodes
x, y	node coordinates (FP)
m	movable flag (0 or 1)
name	node type name
leds	leds string (first digit = blink mode [0|1], then [0|1|2] – per LED)
pins	pins string ([0|1] per PIN)
vcolor	node color override (color index)
vlabel	message to display at the node
Note: braces and comma required in <...> and […], although each string can be absent

Update (may arrive from server spontaneously):

U n h x y <leds,pins> [vcolor,vlabel]
the arguments as for P (some are skipped)

Move node (from client to server):

M n x y
n is SMURPH node number

Roam node (from client to server):

R n x0 y0 x1 y1 smin smax pmin pmax dur
n	SMURPH node number
x0-y1	bounding rectangle
smin	minimum speed (m/s)
smax	maximum speed
pmin	min pause (sec)
pmax	max pause
dur	duration (sec)

Delay reading input (client to server):

T [+]del
+	from current time
del	delay in seconds