# Configuring Bluetooth Modules

September 16, 2012

© Copyright 2011, 2012, Olsonet Communications Corporation.
All Rights Reserved.

This note describes the procedure of pre-configuring a Bluetooth module before interfacing it to the target praxis, which need not care about the internal features of the module, but instead would like to pretend that the interface looks exactly (or almost exactly) like a straightforward UART. The configuration can be carried out from the present praxis (BlueTest) and then, for as long as no configuration commands are issued to the module, the target praxis need not bother itself with the configuration procedure.

At present, we can handle three types of BT modules: Linkmatik 2.0, BTM-182, and BC4 with BOLUTEK firmware which will be referred to hereafter as BOLUTEK. Their physical configuration into Warsaw board is described in BOARDS/WARSAW_BLUE. A specific module is selected by defining one of these constants in options.sys:

BT_MODULE_LINKMATIK
BT_MODULE_BTM182
BT_MODULE_BOLUTEK

Exactly one of the three constants must be defined in options.sys.

Note that the BOLUTEK variant of BC4 is just one (and not a very fortunate one) firmware option for BC4.

# User (OSS) interface over RF

Following the June 3, 2012 revision, the BlueTest praxis is able to handle modules connected to boards with a single UART, where the module is attached to the UART thus precluding UART communication with the user. This is possible as long as the board is equipped with an RF module (like CC110x) which can provide a link to an Access Point (AP) which, in turn, can be interfaced to a terminal emulator (piter) for user interaction. Notably, a BT module can be attached to our new board based on CC430 (codenamed CC430W). One minor nuisance with this kind of setup is that the RF link used for OSS communication limits the length of command lines/responses to 55 characters. This may cause problems with longer commands, notably S (see page 4) whose arguments may be potentially long. Again, I may be able to do something about it, should we decide that the effort is worthwhile.

Note that by default the maximum UART rate for a CC430-based board is 9600 bps. You have to put:

#define UART_FROM_SMCLK 1

into options.sys to make higher rates available. Another relevant and needed option is:

#define UART_RATE_SETTABLE 1

Both options have been already set for CC430_BLUE (in board_options.sys).

The AP praxis can be found in Apps/TESTS/AP. Compile it for the (vanilla) WARSAW board, connect the node to the PC, and start piter (or any terminal emulator) with 9600 bps, direct communication. When you reset the node, you should see the “AP” prompt. Whatever lines you enter will be sent (over RF) to the BT node, whatever lines the BT node decides to send in response will arrive (over RF) to the AP which will forward them to the UART. The two nodes will be using XRS over RF (see the Serial document). The communication is reliable, except the that first line entered from the AP after the node's reset may be lost (so it makes sense to start in such a case from some dummy command, like “h”).

When the BlueTest praxis is compiled for a board with a single UART (CC430W_BLUE is one option available at present), it will automatically configure itself for communication via the AP. If the target board is equipped with two UARTs (like WARSAW_BLUE), the praxis will be configured the old way, i.e., using UART_A for user interface and UART_B for the BT module.

# Configuring the LinkMatik module

Note: this assumes that the BT module is attached to a board with two UARTs (e.g., WARSAW_BLUE), where UART_A is used for user interface, while UART_B is occupied by the BT module. See the previous section for notes on the single-UART case.

Define the constant BT_MODULE_LINKMATIK in options.sys and then execute:

mkmk WARSAW_BLUE
make

to create the praxis. Upload it into the node and connect a terminal emulator (e.g., piter) to the standard UART (UART_A) at 9600. Note: this is now the default UART rate for the praxis. It used to be 115200 for LinkMatik and 19200 for BTM-182, but I think it is better (safer and more consistent) to stick to the same low denominator default.

Note that while the praxis uses UART_A to talk to you, UART_B is connected to the BT module. Even though the rates of the two UARTs can be changed independently,[1] they both start at the same value, i.e., 9600 bps.
[1] For a single-UART board (communicating with the user over an Access Point), the command to change the bit rate of the user-end UART is not available.

The praxis allows you to input data/commands directly to the module and see its responses. When you write:

w some text

then some text will be sent to the module (over UART_B). Any responses from the module (arriving at UART_B) will be echoed to the terminal. This will work if the UART_B rate (9600 bps) matches the rate expected by the module, which may not be the case immediately. If it is not, you can manually change the rate of UART_B this way:

r xxxx

where xxxx, which is the target rate divided by 100, i.e., 1152 corresponds to 115200 bps. Note that we mean UART_B, i.e., the module's UART, not UART_A via which you talk to the praxis from the terminal emulator. That rate need never be changed, but it can be with this command:

t xxxx

where the argument is as before.

For illustration, suppose you are talking to a LinkMatik module (its factory rate is 9600, so you should be OK when you start). When you go:

w SET

you should see the current important settings of the module, i.e., something similar to this:

SET BT BDADDR 00:07:80:81:12:8a
SET BT NAME somename
SET BT CLASS 001f00
SET BT AUTH * 1234
SET BT LAP 9e8b33
SET BT PAGEMODE 4 2000 1
SET BT ROLE 0 f 7d00
SET BT SNIFF 0 20 1 8
SET CONTROL BAUD 9600,8n1
SET CONTROL CD 04 0
SET CONTROL ECHO 4
SET CONTROL ESCAPE 0 00 1

If you want to change the module's rate, say to 115200, do this:

w SET CONTROL BAUD 115200,8n1

Following this command, you will not be able to communicate with the module any more (its rate is no longer matching the UART rate) until you do:

r 1152

The full (and intimidating) list of commands applicable to the module can be found under this link:

http://www.flexipanel.com/Docs/LinkMatik%202.0%20Reference%20DS389.pdf

You don't need to know much of it. I don't understand most of those commands. You don't want to look at this manual at all, unless something goes wrong, you are desperate, and I am not available. The above list of settings is the recommended configuration for using the module as a wireless UART. You can type those lines directly as commands (that accomplish the required settings), e.g.,

w SET BT CLASS 001f00
w SET BT NAME MyLittleDevice
w SET BT AUTH * 98765

The last two commands assign the so-called friendly name to the module, and the PIN for pairing with other devices.

The praxis provides two powerful shortcuts. If you don't know the module's rate (and don't feel like fishing for it), you can enter:

D

which will cause the program to scan through the available rates until the module responds. The rate will then be reported and assumed for the BT module's UART. Here is another shortcut, which likely provides all the functionality you will ever need from the praxis:

S rate name pin mode

where rate is the target bit rate to which the module should be set, name is the friendly name to be assigned to the module, pin is the numerical pin (up to 16 digits) for pairing, and mode can be either the letter u (for UART) or s (for scanner). The command will set up the module for one of two roles: as a wireless UART, or as a scanner/sniffer for other BT modules in the neighborhood.

Here are the remaining commands offered by the praxis:

e n

This command manipulates the status of the module's ESCAPE signal (typically used to force disconnection in the UART mode). If the argument is missing or equal -1, the command will set the ESCAPE signal (for an undetermined time) and exit; you will have to clear the signal explicitly by issuing the same command with argument 0 (zero). If the argument is 1, the signal will be set for the standard duration of 10 milliseconds and then reset. Any other value is interpreted as the number of seconds for which the signal should be set and then reset automatically.

a

The command resets the module (it pulls the reset signal for 10 msec). Note the BOLUTEK module has no RESET signal (the commands behaves as e 1 in that case).

s

The commands reports the value of the “ready” flag. Not extremely important. Normally, if the flag is set, it means that the module is “connected”.

## Connecting to the module in UART mode

Switch on the laptop and make sure that Bluetooth is on. I am assuming XP. Right click on the Bluetooth mini-icon in the bottom right corner (on the taskbar), select "Add a Bluetooth device".

When you see the device, double click on it. On my laptop, the service window shows no services, but when I cancel it, I get another window that asks me to pair the device by entering the PIN code (see above). When I do that, I get a new COM port (in the device list) labeled Bluetooth Communication Port. When the module gets paired, it says (on the node's UART):

CONNECT 0 RFCOMM ...

Now you can open a terminal emulator on the laptop's new UART. Whatever you write there, shows up on the module's UART, and vice versa.

## Using the module as a scanner

Use the INQUIRY command. It appears to work pretty much independently of the settings, except that ECHO (SET CONTROL ECHO) should be set to 7. Otherwise, the friendly names of discovered devices will not be reported.

When you say:

w INQUIRY 10 NAME

the module will scan the neighborhood for ca. 13 seconds (10 * 1.28 sec) and then report all discovered devices, e.g.,

INQUIRY_PARTIAL 00:1e:0b:03:4b:0e 3a0110 "" -58
INQUIRY 1
INQUIRY 00:1e:0b:03:4b:0e 3a0110
NAME 00:1e:0b:03:4b:0e "pawel"

# BTM-182

A board using the BTM-182 module must be compiled with the BT_MODULE_BTM182 symbol defined.

Everything is basically the same, except that the commands to set the module up are (completely) different (they resemble a conversation with an old modem). The factory rate setting of the module is 19200 (but I wouldn't bet on it).

Note: there is a convenient way to make sure that the module rate in fact is 19200. You have to hold the escape signal high for at least four seconds, which you can do, e.g., with this command:

e 5

Commands D and S work the same as for LinkMatik, so you use just them without bothering with all those details.

Here is a sample list of commands (recommended for wireless UART):

w ATC0	to disable hardware flow control
w ATP=1234	to set up a PIN for pairings
w ATN=SeawolfDongle	to set up a device identifier
w ATX0	to disable the +++ escape sequence
w ATL5	to change the UART rate to 115200
w ATE1	echo off
w ATQ1	no result codes

Here is the way to list pretty much all the relevant settings:

w ATI1

You may get something like this (spelling is not mine):

ATI1
OK
ATC=0, NONE FLOW CONTROL
ATD=0000-DR
000000, NEVER SET BLUETOOTH ADR
ATE=1, ECHO CHARACTERS
ATG=1, ENABLE ALL PAGE AND INQUIRY SCAN
ATH=1, DISCOVERABLE
ATK=0, ONE STOP BIT
ATL=5, BAUD RATE is 115200
ATM=0, NONE PARITY_BIT
ATN=SeawolfDongle, LOCAL NAME
ATO=0, ENABLE AUTO CONNECTING
ATP=1234, PIN CODE
ATQ=1, NEVER SEND RESULT CODE
ATR=1, SPP SLAVE ROLE
ATS=1, ENVRLE AUTO-POWERDOWN OF RS232 DRIVRATX=0, NEVER CHECK '+++'

This is what I get after the initialization sequence above. Following that, connections from BT devices work exactly as for LinkMatik.

Note that the rate is set with ATLx, where x is interpreted this way:

#	1200
*	2400
0	4800
1	9600
2	19200
3	38400
4	57600
5	115200
6	230400
7	460800
8	921600

The praxis never bothers with rates below 9600 (this also applies to LinkMatik). Thus, considering PicOS's selection of UART rates, only entries 1, 2, 3, and 5 from the above list are available. If the module's rate is accidentally set to something else (with ATL), you will have to use the escape command to reset the rate to 19200, as the module will not be able to respond to the D scan.

A potentially useful command is ATZ0, i.e.,

w ATZ0

which reverts the module to the factory setting (retaining the name and PIN, however).

## Using the module as a scanner

You have to enable reports (result codes):

w ATQ0

Select the master mode:

w ATR0

Disable auto connect:

w ATO1

Then do:

w ATF?

The command scans the neighborhood for ca. 60 seconds producing reports like this:

Inquiry Results:
1 pawel 001E-0B-034B0E
Inquiry End. 1 Device(s) Found. [or]

# BC4 BOLUTEK

This is the most unfriendly module of the gang, but I think I have managed to tame it for out purpose. Here is how the module should be wired:

- PIO 2 is to be treated as the ATTN signal of LinkMatik (should go to the same MCU pin)
- PIO 3 is equivalent to the ESCAPE signal of LinkMatik
- There is no RESET signal (wiring PIO 3 as RESET makes some sense)
- PIO 4 is connected to power supply
- PIO 5 is connected to ground

With the above configuration of signals, the module can be pre-configured to work in one of the two roles (similar to the other two modules) and appears to exhibit a reasonably consistent behavior.

Note: My experiments show that setting the ESCAPE signal high for >= 3 sec resets the module's baud rate to the default value of 9600 bps. Then you have to re-power the module to make it operable. This is a way out from accidentally mis-setting the baud rate to something inaccessible. Setting the ESCAPE signal high for 1 sec terminates a connection in progress (apparently without affecting any other settings).

Here is the sequence of commands to put the module into the UART mode:

w AT+DEFAULT	[makes sure we are at factory defaults]
w AT+BAUDk	[sets the target baud rate, see the table below]
w AT+ROLE0	[makes sure the module's role is UART]
w AT+RESET	[makes sure the settings have been activated]
w AT+NAMEname	[assigns a friendly name to the module]
w AT+PINxxxxx	[assigns a PIN]
w AT+INQS	[puts the module into PAIRABLE state]

The baud rate is determined by a single hex digit from 1 to C, according to this table:

1	1200
2	2400
3	4800
4	9600	[the default]
5	19200
6	38400
7	57600
8	115200
9	230400
A	460800
B	921600
C	1382400

Considering PicOS's selection of UART rates, only entries 4, 5, 6, and 8 from the above list are available.

Commands D and S work the same as for LinkMatik (or so I hope).

## Using the module as a scanner

For the “scanner” role, the above sequence of commands should be modified as follows (starting from the third command):

w AT+ROLE1	[makes sure the module's role is MASTER]
w AT+RESET	[makes sure the settings have been activated]
w AT+INQM0,9,30	[sets the “inquiry” parameters]
w AT+AUTOINQ0	[no automatic (only explicit) inquiries]
w AT+AUTOCONN1	[automatic connection attempt on discovery]

Here is the sequence to start a new scanning (inquiry) round:

w AT+CLEAR	[forget the devices scanned in the previous round]
w AT+INQC	[stop any previous round in progress]
w AT+INQ	[start a new round]

The round will continue automatically for 61.44 seconds (this is determined by the 30 in AT+INQM0,9,30) unless stopped earlier by AT+INQC. Detection of a (new) device in the neighborhood will trigger the following (sample) sequence of lines from the module:

+INQ:00:aa:70:a5:8c:ae,58020c,7fff
+CONNECTING>>00:aa:70:a5:8c:ae
+INQE
+RNAME=LG-P700
+CONNECTION FAILED
+READY

Each of the first two lines reports the MAC address of the discovered device. However, as far as I could determine, the only way to learn the “friendly name” of the device is to attempt a connection. Note that the inquiry round ends (only one device is discovered), so it must be restarted after each discovery.