# E-RTags: Interface Specifications

        n Packet Format ith value
November 2009

This document contains confidential information, which is proprietary to Olsonet Communications Corporation. No part of its contents may be used, copied, disclosed or conveyed to any party in any manner whatsoever without prior written permission from Olsonet Communication Corporation.

© Copyright 2009, Olsonet Communications Corportation.
All Rights Reserved.

TABLE OF CONTENTS

# Purpose
To provide details on UART interfaces: BaseStation <-> Host and SensorRx <-> SensorNode.

# Definitions
Base Station	In a given network, a single node connected to a single Host via UART (RS232: <rate>, 8, 1). Same as Master.
Beacon Freq	If nonzero, next (qualified) message will be constructed and resent that often (in seconds).
Binding	Process of nodes joining a network.
Bridge	See Sensor Node.
ESN	Equipment serial number, unique and constant (4 bytes).
Local Host	THIS node’s Node Identifier, unique in a given network (2 bytes).
Master Host	Master’s Node Id, stored on every node bound to a network (2 bytes).
        Network Id	Logical identifier of a network. Usually, messages are sent between nodes with the same network id. Same as Net Id.
Node Id	Logical identifier (address) of a node, unique within a network (2 bytes).
NVM	Nonvolatile memory (EEPROM or Flash Information Memory).
Sensor Node	Synonymous to Bridge: Node connected to a single SensorRx via UART (RS232: <rate>, 8, 1).
Source Node:	Where command or message is initiated.
Target Node	Command’s target node id, usually destination of
a message generated by the command.
Tarp Level	Operational functionality (0 – no TARP (flooding), 1 – no sub-optimal path detection, 2 – full TARP.
Tarp Slack	A path recovery control parameter.
Tarp Rte Rec	Another one.

The interfaces are defined with a few types of packets:
- Host to Master: instruction,
- Master to Host: response,
- Master to Host: message output,
- Master to Host: diagnostics
- SensorRx to SensorNode: sensor info.

# References
E-RTags: Operations.

# Grammar

instruction:
0x00
i_len
op_code
op_ref
node_id
op_payload
EOT (0x04)

i_len:
byte // 4..?

op_code:
byte:

CMD_GET |
CMD_SET |
CMD_MASTER |
CMD_TRACE |
CMD_BIND |
CMD_SACK |
CMD_SNACK |
CMD_SENS |
CMD_RESET |
CMD_LOCALE |
CMD_IO |
CMD_IOACK

op_ref:
byte

node_id:
word	// little endian (e.g. node_id 7 == 0x0700)

op_payload:
byte[i_len - 4]

response:
0x00
r_len
op_code
op_ref
op_rc
node_id
op_payload
EOT (0x04)

r_len:
byte // 5..?

op_rc:
byte:
RC_OK |
RC_OKRET |
RC_ERES |
RC_ENET |
RC_EMAS |
RC_ECMD |
RC_EPAR |
RC_EVAL |
RC_ELEN |
RC_EADDR |
RC_EFORK |
RC_EMEM |
RC_NONE

message output:
0x00
len
0xFF
msg_type
msg_specific
0x04

msg_type:
byte

msg_specific:
byte[len – 2]

sensor info:
0x00
0x07
0xFE
ESN
status
rssi
0x04

ESN:
byte[4]

status:
byte

rssi:
byte

diag info:
0x00
0x04
0xFD
level_area
info_val
0x04

level_area:
byte

info_val:
word

# Details

All multi-byte parameters must be input, and are output as little endian, e.g. 2-byte Node Id equal “88” is “0x58 0x00”, 4-byte ESN equal “0xBACA0001” is “0x01 0x00 0xCA 0xBA”.
## Host to Master: Instructions

Byte 0: starting byte 0x00,
Byte 1: instruction length, from the next byte to EOT, exclusive.
Byte 2: operation code (op_code)
Byte 3: operation reference (op_ref).
Bytes 4-5: node id.
Bytes to EOT: operation payload.
EOT ends the instruction.

Instruction layout:

0.	1.	2.	3.	4..5.
0x00	len	Op_code	op_ref	node_id
len – 4 bytes			len+2.
op_payload (optional)			EOT 0x04

Instruction Details:

Starting byte
Value	size	Description
0x00	1 byte

Length
	size	Description
len	1 byte (4..?)

Operation Code
	Size (1byte)
op_code	value	Description
CMD_GET	0x01	Get numerous parameters and attributes.
CMD_SET	0x02	Set numerous parameters.
CMD_MASTER	0x03	Refresh pertinent data on targeted host(s), also designates the sender as the net’s Master.
CMD_TRACE	0x04	Round trip trace
CMD_BIND	0x05	Request or perform binding
CMD_SACK	0x06	Send status ack
CMD_SNACK	0x07	Send status nack
CMD_SENS	0x08	Find, read, add, delete an ESN (sensor)
CMD_RESET	0x09	Various levels of (remote) resets.
CMD_LOCALE	0x0A	Returns local data (node id, ESN, master host)
CMD_IO	0x0B	IO operations (pins, counter, comparator)
CMD_IOACK	0x0C	Send IO ack

Operation Reference
	Size	Description
op_ref	1 byte	For reference, e.g. for OSS scripting. Also, if the MSBit is set, an ack with rc set is sent back, if it makes sense (i.e. if there is no implicit results visible in message output).

Node id
	Size	Description
node_ id	2 bytes

Operation Payload
CMD_GET
payload size	Description
1	parameter id

Operation Payload
CMD_GET
Parameters (settable) & attributes (system state)
parameter	value		Description
PAR_LH	0x01		Local Host
ATTR_ESN	0x02		Equipment serial number
ATTR_MID	0x03		Master Id
PAR_NID	0x04		Network Id
PAR_TARP_L	0x05		Tarp parameters* (level)
PAR_TARP_S	0x06		Tarp parameters (slack)
PAR_TARP_R	0x07		Tarp parameters (route recovery)
PAR_TARP_F	0x08		Tarp parameters (forwarding)
PAR_BEAC	0x09		Beacon frequency
PAR_CON	0x0A		Connectivity audit data (freq, warn, bad, missed)
PAR_RF	0x0B		Status txrx; 2 bits: tx on/off, rx on/off
PAR_ALRM_DONT	0x0C		Optional “don’t tell” entry on the sensor node
PAR_STAT_REP	0x0D		Status report param (freq, pos/neg, time to next)
PAR_RETRY	0x0E		# of tries, timeout for end to end reliability
PAR_AUTOACK	0x0F		Auto-acknowledgments (master)
ATTR_UPTIME	0x10		In seconds
ATTR_BRIDGE	0x11		# of registered ESNs, # of statuses reported
ATTR_RSSI	0x12		Read RSSI of the last message sent by Master
ATTR_MSG_COUNT_T**	0x13		Messaging counters (tarp_rcv, _snd, _fwd)
PAR_RFPWR	0x14		Power level (0-7, def. 3, only on CC1100)
ATTR_MEM1**	0x15		Memory statistics (memfree, stackfree)
ATTR_MEM1**	0x16		Memory statistics (maxfree, staticsize)
PAR_ENCR_M***	0x17		Encryption mode
PAR_ENCR_K***	0x18		Encryption key (number)
PAR_ENCR_D***	0x19		Encryption data (mode, key)
ATTR_SYSVER	0x1A		System version (0xMMmm – Majorminor)
PAR_UART	0x1B		UART speed / 100 (e.g. 384 for 38400)
PAR_CYC_CTRL*****	0x1C		Duty cycle controls (state, mode)
PAR_CYC_SLEEP	0x1D		Sleep period in seconds
PAR_CYC_M_SYNC	0x1E		Duty cycle master sync period (or spec. modes)
PAR_CYC_M_REST	0x1F		Rest period in seconds
ATTR_CYC_LEFT	0x20		Seconds left in the current state, state, mode.

Operation Payload
CMD_SET
Payload	payload parameters
Size per	parameter	value		Description
1+2 bytes	PAR_LH	0x01
1+2 bytes	PAR_NID	0x04
1+1 bytes	PAR_TARP_L*	0x05		Tarp level
1+1 bytes	PAR_TARP_S*	0x06		Tarp slack
1+1 bytes	PAR_TARP_R*	0x07		Tarp route recovery speed
1+1 bytes	PAR_TARP_F*	0x08		Tarp forwarding (on or off)
1+1 bytes	PAR_BEAC	0x09		Beacon frequency
1+2 bytes	PAR_CON****	0x0A		Connectivity data (freq, warn, bad)
1+1 bytes	PAR_RF	0x0B		Status: tx, rx
1+5 bytes	PAR_ALRM_DONT	0x0C		ESN + status byte
1+3 bytes	PAR_STAT_REP	0x0D		Freq. in minutes, negative / positive reporting
1+2 bytes	PAR_RETRY	0x0E		# of retries, timeout in seconds,
1+1 bytes	PAR_AUTOACK	0x0F		Set Master’s auto-acknowledgments
1+1 bytes	PAR_RFPWR	0x14		Set RF power level (only on CC1100)
1+1 bytes	PAR_ENCR_M***	0x17		Set encryption mode
1+1 bytes	PAR_ENCR_K***	0x18		Set (select) encryption key
1+1 bytes	PAR_ENCR_D***	0x19		Set encryption data (b2: mode, b1-b0: key#)
1+2 bytes	PAR_UART	0x1B		Set UART speed (/ 100 e.g. 12 is 1200)
1+2 bytes	PAR_CYC_CTRL*****	0x1C		Duty cycle controls (state, mode)
1+4 bytes	PAR_CYC_SLEEP	0x1D		Sleep period in seconds
1+2 bytes	PAR_CYC_M_SYNC	0x1E		Duty cycle sync period (or spec. modes)
1+4 bytes	PAR_CYC_M_REST	0x1F		Rest period in seconds

* TARP parameters: 1 byte (0 is LSBit):
Bit 0: Forwarding on/off
Bits 3-1: Tarp slack (0-7)
Bits 5-4: Tarp route recovery (0-3)
Bit 7-6: Tarp level (0-2)
All is in “get”, individual values are “set” (arguments are byte-long)

Routing on/off
Whether the node is supposed to route (default on, master off)

Tarp slack
SPD will add this when examining suboptimal path dicards

Tarp route recovery
SPD will exponentially weigh discards using this parameter (i.e. 0 means “additional hop for every discard”, 1 is “a hop for every 2 discards”, 2: 1 for 4, 3: 1 for 8.

Tarp level
Level 0:
Full flooding with the maximum hop count (defaulted to 10).
Level 1:
Duplicate Discard (DD). Duplicate (revisiting) packets are discarded.
Level 2:
DD + Suboptimal Path Discard (SPD). If the packet's destination is known, the node discards packets on suboptimal paths. Number of discarded packets per destination is kept to play a role in route recovery, together with “tarp slack” and “tarp route recovery speed”.

** For testing and troubleshooting, some may be withdrawn for resource conservation.

*** Encryption data:
Bits 1-0: key number
Bit 2: mode
All is in “get”, individual values are “set” (arguments are byte-long)

**** Connectivity Set: Byte 1: audit freq, Byte 2: bits 7-4: missed beats to warning, 3-0: missed beats to bad status.

***** Duty cycles are described in the Operations document.
States: disabled (0x00), enabled / rest (0x01), prep / sync (0x02), sleep (0x03). Only disabled, enabled, rest, sync can be set by the user.
Modes: net (0x00), priv_net (0x01), priv_on (0x02), priv_off (0x03).

PAR_CYC_SLEEP is illegal on the master, PAR_M_SYNC, PAR_M_REST are allowed only on the master. Illegal combinations return RC_EMAS.

PAR_CYC_M_SYNC max value is 0xFFF (4095 s.). It also can be set to force the network to a desired state: 0xEFFF would move all listeners to enabled, 0xDFFF to disabled states.

Operation Payload
CMD_MASTER
Size	Payload parameters
0	No payload

Operation Payload
CMD_TRACE
Size	Payload parameters
1	Number of forward hops allowed

Operation Payload
CMD_BIND
Size	Payload parameters
7 bytes	ESN (4), new node id (2), range (1)

BIND	Target node (node_id from the instruction packet) will broadcast msg_bind within “range” hops, carrying pertinent data: ESN and new node id, but also net id, master host, and connectivity and encryption data.

Operation Payload
CMD_SACK
Size	Payload parameters
4 bytes	ESN

SACK	Acknowledges msg_status being sent by the target node (presumably a reporting bridge). ESN must be the last ESN reported or 0x00000000 for msg_br acknowledgment. Note that this functionality is automatic if PAR_AUTOACK is set.

Operation Payload
CMD_SNACK
Size	Payload parameters
0 bytes

NACK	Negative ack: stop sending status report for further ESNs.

Operation Payload
CMD_SENS
Size	Payload parameters
5 bytes	ESN (4), sensor action (1)

SENS	Does ESN-related NVM operations on the target node(s):

0x00: find – if the ESN is registered with the target node id (presumably a bridge), high 4 bits will show its status, i.e. returned is the same ESN, and 0x10 if the heart beat is set, or 0x00 if it isn’t. If the node is not found, nothing is returned (unless high bit in the command ref. code is set, which is a general mechanism to request somehow redundant notifications). This command is meant for broadcasts, to find bridges where a given ESN is registered.

0x01: read – reads the ESN’s status, returns 0x11 or 0x01 (on / off), or RC_ERES if the ESN is not present on the target node.

0x02: read next any – replaces the ESN with the next one, and gives its status (0x12 or 0x02), or returns RC_ERES if there is no higher ESN on the target bridge.

0x03: read next 0 – as 0x02, but the search is after the ESN with status off.

0x04: read next 1 – as 0x03, with status on

0x05: write (add) the ESN to the NVM. RC_ERES if it’s already there.

0x06: erase. RC_ERES if it’s not there. Only on boards with EEPROM.

Operation Payload
CMD_RESET
Size	Payload parameters
1 byte	Level

RESET
Bit 0: sensor vector (RAM) reset;
Bit 1: sensor table (NVM) reset;
Bit 2: software restart;
Bit 3: cold boot (all NVM erase and software restart).

Operation Payload
CMD_LOCALE
Size	Payload parameters
0

Retrieves node id, ESN, and master host from locally connected node (via RS232).

Operation Payload
CMD_IO
Size	Payload parameters
4 bytes	operation (1), args (bytes a1, a2, a3)

Operations document details on the network context of IO operations (i.e. reliable message delivery).

Pin mapping and configuration:
GP1..7 are mapped as pins 1..7. CFG0..2 are mapped as pins 8..10.
GP1 may be configured as an interrupt driven 24-bit counter.
GP2 may be configured as an interrupt driven state change notifier.

Operations:
IO_READ (0x00): Read pin(s), including the bulk read variant.
IO_WRITE (0x01): Configure a pin, write a pin, configure & write a pin.
IO_ADC (0x02): Analog in, converted (12 bits).
IO_CNT_START (0xX3): Start interrupt driven counter on GPIO_1.
IO_CMP_START (0x04): Start comparator.
IO_NOT_START (0x05): Start interrupt driven state change notifier on GPIO_2.
IO_STOP (0x06): Stop (suspend) any of the three pulse monitoring operations.
IO_CNT_GET (0x07): Get the counter’s current value.
IO_CMP_GET (0x08): Get the comparator’s current value.
IO_STATE (0x09): Get the current state of pulse monitoring operations.
IO_CREG_GET (0x0A): Get comparator’s additional register.
IO_CREG_SET (0x0B): Set comparator’s additional register.
IO_FLAGS_GET (0x0C): Get flags of pulse monitoring operations.
IO_FLAGS_SET (0x0D): Set flags of pulse monitoring operations.

IO_READ (0x00): pin a1 is read and the value returned in a2 (bits b2-b0):
a2.b2 set: pin is analog in
a2.b1 set: pin is out
a2.b2 and a2.b1 set: pin is unavailable (used for interrupt driven operations)
a2.b0: pin value
e.g. 0x00 0x0A 0xFF 0xFF
returns 0x00 0x0A 0x03 0xFF if CFG2 is dig. out and high.

Bulk read is performed if a1 == 0xFF: All 4 bytes are used to show all 10 pins encoded as for read pin above, 3 bits per pin (operation is the LSB). The 4 bytes should be treated as a little endian long word (32 bits), e.g. reading of GP3 spans bits 6, 7 of operation and bit 0 of a1 byte.

RC_EVAL is returned for invalid pin numbers.

IO_WRITE (0x01): pin a1 is configured if necessary or written to, according to a2 (b2-b0):
a2.b2 set: configure pin a1 analog in
a2.b1 set: configure pin a1 digital in
a2.b2 = a2.b1 = 0: if necessary, pin a1 is configured digital out and a2.b0 written to it.
If GP1 or GP2 are enabled for interrupt driven functionality, attempts to write them return RC_ERES errors. RC_EVAL is returned for illegal pin numbers (note that pins > 7 are illegal for analog in).

IO_ADC (0x02):
a1: b7-b4: vref (0: 1.5V, 1: 2.5V, 2: Vcc);
    : b3-b0: pin number (only P6 may be used, i.e. GP1-7).
a2: sampling time reference (stref) in ms. Max. 64 ms, 0 defaults to 1 ms.
a2a3: returned value (little endian). Note that stref is overwritten.

RC_EVAL is returned for invalid pin numbers or wrong vref.
Note that RF receiver is switched off for ADC operations.

Interrupt driven functionality (GP1 – counter, GP2 – change notifier)

IO_CNT_START (0xX3): set counter to a1a2a3 (little endian) and start counting pulses.
X (4 high bits of operation) controls additional parameters:
X & 2: a1a2a3 are ignored and the counter starts with its value (continue)
X & 1: Count rising edges (falling edges if not set).
e.g. 0x33 0x00 0x00 0x00 continues with the counter’s value on rising edges.

RC_ERES is returned if the counter is already active.

IO_CMP_START (0x04): set comparator to a1a2a3 (little endian) and start comparing.
RC_ERES is returned if comparator is already active.

IO_NOT_START (0x05): start notifier on rising edges if a1 is non-zero, on falling otherwise.
RC_ERES is returned if notifier is already active.

IO_STOP (0x06): stop operations, according to a1, a2, a3:
a1 set: stop the counter;
a2 set: stop comparator;
a3 set: stop notifier.
RC_ERES is returned if requested functionality is already stopped, with appropriate field marked.
e.g. 0x06 0x01 0x01 0x01 attempts to stop everything, and returns 0x06 0x01 0xF1 0xF1 with RC_ERES if comparator and notifier were not active. Despite RC_ERES, the counter is stopped as requested.

IO_CNT_GET (0x07): Returns the counter’s value. In addition, operation.b4 encodes whether the counter is active or not.
e.g. 0x07 0xFF 0xFF 0xFF returns 0x17 0x0A 0x00 0x00 if the counter is 10 and active, or 0x07 0x00 0x01 0x00 if the counter is 256 and inactive.

IO_CMP_GET (0x08): Returns comparator’s value. In addition, operation.b4 encodes the status, as for the counter.

IO_STATE (0x09): Returns IO state encoded in a1:
b0 set: notifier edge is rising
b1 set: notifier is on
b2 set: notifier event is pending
b3 is 0
b4 set: counter edge is rising
b5 set: counter is active
b6 set: comparator is active
b7 set: comparator event pending

Comparator’s additional register (CREG) and IO_FLAGS allow useful operations without operator’s involvement, as they control counter or comparator updates on the triggering interrupt.

IO_CREG_GET (0x0A): a1a2a3 return CREG value.

IO_CREG_SET (0x0B): CREG is set to a1a2a3.

IO_FLAGS_GET (0x0C): a1 returns NVM backup timer, a2 returns the operation to be performed on the comparator’s interrupt. Maximum NVM backup frequency is 63 seconds. Operations:
0x00: do nothing (default)
0x01: add CREG to comparator (e.g. CNT mod CMP == 0 notifications can be requested that way)
0x02: subtract CREG from the counter
0x03: subtract comparator from the counter.

IO_FLAGS_SET (0x0D): Sets NVM backup timer and the flags.
RC_EVAL is returned if a1 > 63 or a2 > 3.

Operation Payload
CMD_IOACK
Size	Payload parameters
4 bytes	IO_STATE (1), counter (3 bytes)

Acknowledges msg_io being sent by the target node. The four bytes must be the same as in the msg_io being acknowledged. Note that this functionality is automatic if PAR_AUTOACK is set.

Note that a state change notification carries the counter value as well (if the counter is enabled).

If an interesting event occurs while the previous one is still unconfirmed, retries for the previous event are aborted, and reporting of the new one starts its cycle.

End of Transmission
EOT	Size		Description
0x04	1 byte

## Master to Host: Responses

Byte 0: starting byte 0x00,
Byte 1: instruction length, from the next byte to EOT, exclusive.
Byte 2: operation code (op_code).
Byte 3: operation reference (op_ref).
Byte 4: operation return code.
Bytes 5-6: node id.
Bytes to EOT: operation payload.
EOT ends the instruction.

Response layout:

0.	1.	2.	3.	4.	5..6.
0x00	len	Op_code	op_ref	Op_rc	node_id
len – 5 bytes			len+2.
op_payload (optional)			EOT 0x04

Response Details:

All fields but op_rc as in Instructions. In general, responses are returned to the Host when it makes sense, i.e. no implicit confirmation is expected via a message output, the command failed, or the response carries retrieved data. Also, all commands to the local target are “echoed”. However, the responses are forced back if the operation’s reference code has the MSBit set, e.g. a CMD_SET to a remote node with ref. code 0x0A will not return if successful (the result may be double checked with a CMD_GET), but ref. code 0xAA will force the command back, even if it is marked with RC_OK.

Operation return code
	Size (1byte)		Description
op_rc	value
RC_OK	0x00		Successful
RC_OKRET*	0x01		Successful, force the return to the issuer
RC_ERES	0x02		error, confused resources
RC_ENET	0x03		error, no network
RC_EMAS	0x04		error, no master
RC_ECMD	0x05		error, bad command
RC_EPAR	0x06		error, bad parameter
RC_EVAL	0x07		error, bad value
RC_ELEN	0x08		error, bad length
RC_EADDR	0x09		error, bad address
RC_NONE	0xFF		not set

* This is equivalent to RC_OK, but the system sees it important to force-return. The best example is a remote CMD_GET.

Operation Payload

Operation Payload
CMD_GET, rc == OK
Payload	payload parameters
Size per	Parameter	pvalue		Value Description*
1+2 bytes	PAR_LH	0x01		Local host
1+4 bytes	ATTR_ESN	0x02		Equipment serial number
1+2 bytes	ATTR_MID	0x03		Master id
1+2 bytes	PAR_NID	0x04		Network id
1+1 bytes	PAR_TARP_L	0x05		Tarp parameters**
1+1 bytes	PAR_TARP_S	0x06		Tarp parameters
1+1 bytes	PAR_TARP_R	0x07		Tarp parameters
1+1 bytes	PAR_TARP_F	0x08		Tarp parameters
1+1 bytes	PAR_BEAC	0x09		Beacon
1+3 bytes	PAR_CON	0x0A		Connectivity audit data***
1+1 bytes	PAR_RF	0x0B		Rf data
1+5 bytes	PAR_ALRM_DON’T	0x0C		ESN + status byte
1+5 bytes	PAR_STAT_REP	0x0D		Freq. in minutes, negative / positive reporting, time to next report****
1+2 bytes	PAR_RETRY	0x0E		# of retries, timeout in seconds
1+1 bytes	PAR_AUTOACK	0x0F		Master’s auto-acknowledgments
1+4 bytes	ATTR_UPTIME	0x10		In seconds
1+4 bytes	ATTR_BRIDGE	0x11		# of registered ESNs, # of statuses reported
1+2 bytes	ATTR_RSSI	0x12		RSSI, “link quality” from CC1100
1+6 bytes	ATTR_MSG_COUNT_T	0x13		Messaging counters (tarp_rcv, _snd, _fwd)
1+1 bytes	PAR_RFPWR	0x14		Power level (0-7, def. 3, only on CC1100)
1+6 bytes	ATTR_MEM1*****	0x15		Memory statistics 1
1+6 bytes	ATTR_MEM2	0x16		Memory statistics 2
1+1 bytes	PAR_ENCR_M	0x17		Encryption mode (0: free, 1: strict)
1+1 bytes	PAR_ENCR_K	0x18		Encryption key# (0..3)
1+1 bytes	PAR_ENCR_D	0x19		Encryption data (b2: mode, b1-b0: key#)
1+1 bytes	ATTR_SYSVER	0x1A		System version (1st release is 2.0; 0x0200)
1+2 bytes	PAR_UART	0x1B		UART speed /100 (e.g. 192 is 19200)
1+2 bytes	PAR_CYC_CTRL******	0x1C		Duty cycle controls (state, mode)
1+4 bytes	PAR_CYC_SLEEP	0x1D		Sleep period in seconds
1+2 bytes	PAR_CYC_M_SYNC	0x1E		Duty cycle master controls (spec. mode, sync period)
1+4 bytes	PAR_CYC_M_REST	0x1F		Rest period in seconds
1+6 bytes	ATTR_CYC_LEFT	0x20		Time in seconds left in present state (4B), state (1B), mode (1B)

*All are from the target node.

** In all cases all the parameters (1 byte) are returned

***Connectivity data:
Byte 1: expected msg_master frequency in seconds (0-255).
Byte 2:
Bits 7-4: # of missed beats before start blinking LED (warning)
Bits 3-0: # of missed beats before switching the LED off (bad)
Byte 3: missed beats

****Status reporting parameters:
Byte 1-2: frequency in minutes
Byte 3: 0 -- report ESN with no status reported (default), 1 -- report those with status reported.
Byte 4-5: time left to next reporting, in 64s units (0xFFFF eternity if the reporting process is not running)

*****Memory statistics:
Each entry is 1 word.
MEM1: Free memory, minimal free memory so far, shortest free stack so far
MEM2: Max free memory block available, number of free memory chunks, size of the static segment.

******Described in Operations document.

Response to CMD_SET is identical to the command, with the op_rc exception. It is sent back only if MSBit in op_ref is set.

Responses to CMD_SENS’s actions are discussed in the previous section.

## Master to Host: Message Output

Grammar:
0x00
msg_length
0xFF
msg_type
msg_specific
EOT (0x04)

Message types, output generating are highlighted:

(1) msg_master, (2) msg_trace, (3) msg_traceAck, (4) msg_cmd,
(5) msg_new, (6) msg_bindReq, (7) msg_bind, (8) msg_br,
(9) msg_alrm, (10) msg_st, (11) msg_stAck, (12) msg_stNack,
(13) msg_io, (14) msg_ioAck

msg_specific
msg_traceAck (3)
0. / # of forward hops (fh)	1. / # of backward hops (bh)	2… / node_ids*
1 byte	1 byte	2*(fh+bh) bytes

*The source = termination node id of the tracing loop is not shown in the output.

msg_specific
msg_bindReq (6)
0. newcomer’s ESN	4. newcomer’s tmp node id	6. binding / node_id
4 bytes	2 bytes	2 bytes

msg_specific
msg_br (8)
0. node id	2. connectivity		4. # of ESNs	6. # of statuses	8. auto ack
2 bytes	2 bytes		2 bytes	2 bytes	1 byte

msg_br:
byte 0-1: bridge node id
byte 2-3 (word): connectivity: warn (4 bits), bad (4 bits), missed (byte 3)
byte 4-5 (word): number of registered ESNs
byte 6-7 (word): number of ESNs with SensorRx-reported statuses
byte 8: auto-acked statuses (if 1, acks are sent automatically)

msg_specific
msg_alrm (9)
0. / bridge node id	2. / Type	3. / Rev	4..7 / ESN		6. / status	7.. / info	7+N. rssi
2 bytes (word)	1 byte	1 byte	lword (4B)		1 byte	N bytes

msg_specific
msg_st (10)
0. / bridge node id	2. connectivity / (missed beats)		3. # of ESN in this packet	4. auto ack	5… / ESN(s)
2 bytes (word)	1 byte		1 byte	1 byte	Up to 5x lwords

Note that auto acks pointed out in msg_br have the same meaning here, too, i.e. if they were set (and not cleared), there is no need for acks from the Host.

The status reporting session starts with msg_br followed by a number of msg_st, all of them to be acknowledged (auto acked, or by Host). For example, if msg_br shows 500 ESNs and 491 SensorRx-reported statuses, there will be two msg_st’s, one with 5 and one with 4 ESNs.

msg_specific
msg_io (13)
0. node id	2. io state	4. counter (a1a2a3)
2 bytes	1 byte	3 bytes

Pulse counter is recorded at the time msg_io was constructed, after the triggering event occurred. Note that with frequent pulses what is reported may be different from value at the trigger.

## SensorRx to SensorNodeHost: status info

0.	1.	2.	3.	4.	5..8	9.	10..	10+N.	11 +N.
0x00	9 + N	0xFE	Type	Revision	ESN	status	N bytes	rssi	0x04

Messages are echoed back, optionally with 0xFE replaced with an error code:
RC_ENET - if the bridge is not bound;
RC_EMAS - no master;
RC_ERES - this IS the master (can't be the master and bridge at a time);
RC_EADDR – Status aggregation in effect (only statuses from registered ESNs are reported), and the status info came from an unregistered ESN.
RC_ELEN – wrong length field – UART slip. Whole message must fit in the UART buffer (with the length set in options.sys).

## Debug / Diagnostics

In dbg_X, below, X is level_area, i.e. dbg_a (0xABCD) will produce output 00 04 FD 0A AB CD 04

By default, level_area 0, 1, 2, 9 are visible. Setting dbg_level in options.sys changes this visibility. The dbg_level is a bit map b0-b15, where bx enables / disables level_area x, i.e. its default is 0x0207.

The dbg_9 output reflects UART misses or bad format of remote commands, and may be used for regular functionality. If not needed, it should be disabled (dbg_level would be 0x0007).

In production versions, the default settings should be maintained, and all FD output (other than level_area 9) filtered out and reported.

At present, we have binary output for:

System errors:
dbg_0 (ec); // SYSTEM ERROR, reset
dbg_0 (0x1000); // net_init failed, reset

System messages:
dbg_1 (0x1000 | VERSION); // PicOS version (currently 2.00 i.e. 0x1200)
(followed by 1 FD output with number of free bytes in RAM)

dbg_1 (0x2000); // CC1100 chip data at init
(followed by 2 FD outputs with the chip data)

Serious errors, likely crashing the application. Should be reported and investigated:
dbg_2 (0x1000); // net busy
dbg_2 (0x2000); // Cannot open cc1100
dbg_2 (0x3000); // net_rx: no buffer or not net
dbg_2 (0x4000); // Unknown phys
dbg_2 (0x5000); // net_tx: corrupted input
dbg_2 (0x6000); // net_tx: no net
dbg_2 (0x6000 | net_phys); // net_tx: corrupted phys
dbg_2 (0x7000); // net_close: not opened
dbg_2 (0x8000 | rc); // net_close: tcv error
dbg_2 (0x9000 | phys);
dbg_2 (0xA000); // tcv_ope phy?
dbg_2 (0xB000); // tcv_clo desc
dbg_2 (0xBA00 | in_header(buf, msg_type)); // bad bindReq
dbg_2 (0xBB00 | is_master_chg);
dbg_2 (0xC100 | m[1]); // app_ser_out: > UI_OUTLEN
dbg_2 (0xC200 | cyc_ctrl.st); // cycle manager’s inconsistency
dbg_2 (0xC2F1); // cycle manager’s inconsistency (1)
dbg_2 (0xC2F2); // cycle manager’s inconsistency (2)
dbg_2 (0xC2F3); // cycle manager’s inconsistency (3)
dbg_2 (0xC2F4); // cycle manager’s inconsistency (4)
dbg_2 (0xC2F5); // cycle manager’s inconsistency (5)
dbg_2 (0xC2F6); // cycle manager’s inconsistency (6)
dbg_2 (0xC2F7); // cycle manager’s inconsistency (7)
dbg_2 (0xC400); // outserial fork failed
dbg_2 (0xC401); // outserial fork failed no cpy
dbg_2 (0xC402); // beacon fork failed
dbg_2 (0xC403); // oss_ret_out fork failed
dbg_2 (0xC405); // master beacon fork filed
dbg_2 (0xC406); // oss_traceAck_out fork failed
dbg_2 (0xC404); // oss_bindReq_out fork failed
dbg_2 (0xC407); // oss_alrm_out fork failed
dbg_2 (0xC408); // oss_br_out fork failed
dbg_2 (0xC409); // oss_st_out fork failed
dbg_2 (0xC40A); // oss_io_out fork failed
dbg_2 (0xE000 | (byte)wlen); // NVM inconsistency
dbg_2 (0xE100 | (byte)wlen); // NVM inconsistency
dbg_2 (0xE200 | p); // NVM inconsistency; ESN table lost

TARP, messaging:
dbg_8 (0x1000); // xmt off
dbg_8 (0x2000); // Tarp dup failed
dbg_8 (0x3000); // Tarp dup2 failed
dbg_8 (0x4000 | in_key); // strict mode & key# mismatch
dbg_8 (0x5000 | in_key); // bad decrypt (bad key)

UART misses, or bad format of remote commands:
dbg_9 (0x1000 | ui_ibuf[0]); // no START 0x00
dbg_9 (0x2000 | UI_TOUT);
dbg_9 (0x3000 | ui_ibuf[1]); // bad length
dbg_9 (0x4000 | ui_ibuf[ptr -1]); // no EOT 0x04
dbg_9 (0x5000 | cmd_ctrl.opcode);
dbg_9 (0x6000 | cmd_ctrl.oprc);

Application debugging:
dbg_a (0x0200 | in_header(buf, msg_type)); // Got ?
dbg_a (0x01FF); // net_rx failed (%d)...
dbg_a (0x8000 | packet_size); // ...packet_size
dbg_a (0x03FA); // beacon failed
dbg_a (0x0400 | in_header(buf, msg_type)); // Dropped to lh
dbg_a (0x0500 | in_header(buf, msg_type)); // Tx failed

Memory (recoverable):
dbg_e (0x1000 | len); // get_mem() failed

Interesting event tracing:
dbg_f (0xC200 | m[1]); // app_ser_out: wait for previous
dbg_f (0xC300 | m[1]); // app_ser_out: wait for mem
dbg_f(0xF000 | (a)); // NVM page erase