How to use front.tcl

November 20, 2008

# Prerequisites

Install ActiveTcl from this site: http://www.activestate.com/. Default installation options are fine.

# Usage

Double click on front.tcl. With the default installation setup of ActiveTcl, the “tcl” file name extension will be automatically handled by Tcl. A command-line window will open with this line at the top:

Enter COM port number:

Do exactly as asked, i.e., enter the COM port number of the USB dongle connecting you to the master node.

At any time, you can enter “h” (or any “illegal” command) to see this list of legitimate commands:

Commands:
  start sec [continue] - start sampling at sec intervals
  stop - stop sampling
  show off|on - show received values while sampling
  echo off|on - show dialogue with the master
  extract filename - extract stored samples to file
  quit - exit the script

if you don't know what is happening to the master node, execute “stop”. This will reset the node and bring it to the default decent state. If you are not sure what is going on, and would prefer not to interrupt an ongoing collection, execute “show on”. If you see no samples within some reasonably long interval, then most likely the master is “stopped”.

Note that if you do quit, the master will keep working (collecting data) for as long as it is powered up.

To start data collection, make sure that the collector nodes you want to use for the experiment are powered up, their sensors connected, and so on. If you do something like this:

start 30

the master will clear its EEPROM (storage of samples), set up parameters to collect samples from the audible collectors at 30 second intervals, and send out the requisite commands to the collectors.. If you put “continue” after the interval specification, the master will do the same except that it will NOT erase the storage, i.e., new samples will be adding at the end of any previously collected data.

The minimum collection interval is 30 seconds.

The sampling is synchronized by the master, such that it happens at the same instants at all collectors, even though the arrival times of samples at the master may be different. This is intentional: the transmissions are spread in time to avoid collisions. Note that during some initial period (while the collectors are still getting the parameters from the master), they may be out of sync.

Note: the storage size at the master allows it to accommodate up to 16,382 samples. Thus, for example, 5 collectors running every 30 seconds will use it up in 16,382/(5x2) minutes (i.e., about 27 hours).

When you execute stop, the master will not be storing any new samples arriving from the collectors, even if they are active.

If you want to see the values being received by the master (as they are collected and stored), do “show on”. “show off” will cancel that.

If you want to see the dialogue between the script and the master (i.e., the actual messages exchanged by the two, which may be useful for debugging), use “echo on”.

To extract all samples present in the master's storage execute

extract filename

where filename identifies the file where you want them stored. Usually, you will execute extract after stop (in the stopped state), although it is legal to do it on line. In principle, the extraction should not interfere with ongoing collection. The operation may take a while (the script displays its progress by showing you the sample numbers as they are being extracted). In the future, we will speed up this operation a bit.