# DecaWave DW1000
# driver

August 27, 2015

© Copyright 2015, Olsonet Communications Corporation.
All Rights Reserved.

# Preamble

DecaWave DW1000 is a UWB radio module with built in precise packet timing capabilities, intended for indoor positioning. The module is described in detail in these documents:

DW1000 User Manual
DW1000 Data Sheet, version 2.04
DWM1000 Data Sheet, version 1.01

available from DecaWave's web site at: http://www.decawave.com/

This document sketches the practical functionality (interface) of the present PicOS driver for the module. There is no need to refer to the above documents, unless you want to understand in depth what is going on inside the module (or in the driver). Needless to say, the present driver is preliminary and intended solely for experiments (and this document is intended as a starting point for discussion). We don't know yet whether the module is going to be useful for us at all.

# The assumptions

At present, we focus solely on the location tracking capabilities of the module. While the device can be used for straightforward RF communication (say as a replacement for CC1100), and the present driver can be quite easily (almost trivially) extended in that direction, the option doesn't immediately appear attractive to me, because the device's power consumption is one order of magnitude (in fact almost exactly 10 times) higher than for CC1100 (say with the receiver on) while its RF range appears very short (10m or so), at least with the present settings (recommended by DecaWave). On the other hand, DW1000 has a number of interesting features reducing the length of duty cycles in some communication scenarios (plus some lower power listening modes similar to WOR). Those scenarios are related to IEEE 802.15.4 (ZigBee) and (sort of) assume (or at least facilitate) point-to-point communication, so it is not immediately clear how attractive the module can be for our applications.
Consequently, the present driver does not make the device available as a PicOS PHY. Instead, it implements a sensor-actuator pair. To see how the two conceptually simple interfaces can represent the device for our purpose, we have to learn a bit about location tracking with DW1000.

# Ranging, i.e., measuring distance with DW1000

The extra features of DW1000 (compared to other radios, e.g., CC1100) boil down to a configuration of precise timers that can be used to estimate the Time of Arrival (TOA) of a packet together with its Time of Departure (TOD). Consequently, we can estimate the packet's Time of Flight (TOF), which can be translated into the distance between the sender and the receiver. Having three or more distances between a Tag and a number of Pegs (whose locations are known) will let us estimate the location of the Tag.
Suppose that some two nodes, call them A and B, want to determine the distance between themselves. The nodes are equipped with precise (albeit independent, i.e., not synchronized) timers. A sends a packet addressed to B. A marks the packet's transmission time as TSP, B marks its reception time as TRP. Having received the packet, B responds with its own packet transmitted at TSR > TRP which A receives at TRR > TSP.[1] Then TOF = (TRR – TSP) – (TSR – TRP) is twice the propagation distance between A and B.
[1] Note that we only compare timers belonging to the same node.
In the actual implementation (in our driver), the nodes carry out a handshake of sorts with one node going first. The initiating node (A) sends the first packet of the handshake which I call POLL. The packet needs no particular structure or content (payload). The only important thing is that the other node (B) should recognize it as a POLL packet and should also learn the identity of the initiating node. Any packet exchanged within the handshake is a ranging packet (it is marked in a special way), which means that:
- the sending device precisely determines the time of its departure
- the receiving device precisely determines the time of its arrival
Specifically, there is a special marker symbol within the packet's header whose transmission is used as the relatively sharp reference point for the timing (the device executes a rather complicated [microcoded] algorithm aimed at reducing the uncertainty in timing of that symbol). As we said earlier, the timers are local, so the scheme does not assume that nodes synchronize their clocks. As is clear from the above formula, the TOF estimation is based on differences in the indications of local timers only.
When the initiating node A sends the POLL packet, it marks the time of its departure (using its local clock) as TSP. The other node, B, receiving the POLL packet, marks its arrival time (using its local clock) as TRP.
Having received the POLL packet, B responds with a RESP packet addressed to A. Again, the packet needs no special content[2] other than being identifiable as a RESP packet sent by B and addressed to A. B marks the departure time of the RESP packet as TSR, and A marks its reception time as TRR.
[2] In fact, those packets, i.e. POLL and RESP, have no payload and consist exclusively of (some variants of) 802.15.4 headers.
Having received the RESP packet, A sends the final packet of the handshake to B. I call this packet FIN. A inserts into the FIN packet (in contrast to the previous two packets, this one does have a payload) three timer values: TSP, TRR, and TSF, where TSF is the departure time of FIN. The role of FIN is:
1. to communicate the values of A's timers to B (the ones B doesn't know), so it can compute the time of flight
2. to provide for one more estimate of the time of flight (the three packets can be viewed as two exchanges)
The tricky bit is that A has to know the transmission time of FIN before sending the packet (so it can insert that time into the packet's payload). To make that possible, the device has a feature whereby it can be instructed to dispatch the next outgoing packet in such a way that the packet's marker symbol is transmitted precisely at a preset (advance) timer value. Thus, the driver calculates a safe (delayed) transmission time of FIN, based on current time + some processing interval, sets TSF to that time, inserts TSF into FIN (along with the other two timers) and tells the device to transmit the packet exactly at TSF. The actual action is a bit more complicated, but it pretty much amounts to this.
When the FIN packet gets to B, the node has enough information to calculate two estimates of the distance between the two nodes (note that it is B that does the estimation). The node has these six time stamps:
TSP – departure time of POLL at A
TRP – arrival time of POLL at B
TSR – departure time of RESP at B
TRR – arrival time of RESP at A
TSF – departure time of FIN at A
TRF – arrival time of FIN at B
Now, the two estimates of TOF are calculated as:
TOF1 = ((TRR – TSP) – (TSR – TRP)) / 2
and:
TOF2 = ((TRF – TSR) – (TSF – TRR)) / 2
Then the node can take the average of the two values:
TOF = (TOF1 + TOF2) / 2
as the single estimate of the time of flight. Note that all the differentials refer to timers from the same side.
The timers are in fact 40-bit values and the arithmetic is a bit involved for MSP430, so it makes sense to pass the timers to the OSS for calculations (and this is what the present driver does). This makes even more sense considering that (rather unavoidably) some Tag/Peg-specific adjustments (calibrations) will have to be applied to them. While the chip incorporates internal adjustments, i.e., provides for storing pre-calibrated antenna delays (and a few other things) in the so-called one-time programmable (OTP) memory, it seems much easier (and more cost effective) to do the calibration in the OSS, which will simplify both the firmware as well as the calibration procedure (which can be carried out during production and using production firmware).
Thus, the last leg of the handshake (i.e., the FIN packet) should arrive at a Peg, such that the relevant information can be directly passed to the OSS. Consequently, POLL packets should be issued by Tags. It can hardly be any other way, because keeping the receiver open in a Tag for any nontrivial amount of time is out of the question. The module facilitates some low power listening modes (akin to WOR) which have to be studied, if the preliminary tests turn out promising.
The timer resolution is formally about 1/63897600000s which roughly translates into about 5 mm at the speed of light. This is the granularity, not the accuracy. There is a healthy bit of guessing involved in the timing of the marker symbols, and this seems to be the primary internal source of inaccuracies. Moreover, there are external sources: signals can get reflected, and so on. They suggest procedures and heuristics to detect and discard such signals (basically by looking into the very rich set of various quality indicators). There is no RSSI, but they say how it can be computed from those indicators in a rather messy sort of way.
The wrap around time of the 40-bit timer is about 17.2 seconds. Owing to the fact that a handshake is carried out without unnecessary (non-deterministic) delays (like LBT, or other collision avoidance schemes), its duration (if successful) is highly predictable and, regardless of the setting of RF parameters, always below 12ms (counting from the transmission of POLL until the reception of FIN. When we strip the 40-bit timer of its most significant byte (to make it look like a simple longword), its wrap around time becomes ca. 67ms which, in confrontation with handshake duration, is still OK for ranging. The driver has a compilation option to use 4-byte timers instead of the 5-byte ones. Based on my experiments, this option is probably prefered.

# The interface

The (potentially relevant) compilation options of the driver are captured by the constant DW1000_OPTIONS which is a collection of binary flags. The default value of that constant is 0. Here is the list of flags:
0x01	DW1000_OPT_DEBUG
The option includes some internal tests and diag messages that may be useful for debugging. It should not be selected for production (or realistic, production grade, timing tests).
0x02	DW1000_OPT_SHORT_STAMPS
The option selects short (4-byte, as opposed to 5-byte) time stamps. Short stamps reduce the size of the FIN packet as well as the data structure representing the sensor value (see below), and also simplify some processing in the driver (but not a a lot).
0x04	DW1000_OPT_NO_ANT_DELAY
The option removes from the driver the code for internally adjusting the timer values by preset antenna delays. Such delays can be pre-calibrated and stored in the module's OTP (one-time programmable) memory. This option makes sense, if we prefer to store the calibration data in the OSS, which we most likely do.
I am contemplating an option to replace the bunch of time stamps returned by the driver with a single-value TOF estimate. This is doable (and will simplify the interface), especially if:
- we use short (4-byte) time stamps
- we conclude that the (external) calibration procedure can work on the single TOF estimate and needs no individual time stamps; I am inclined to think that this is the case
Of course, the options can be eliminated when we get to a production version of the driver and preset in the most suitable way.
Note that when DW1000_OPT_NO_ANT_DELAY is not selected, the driver assumes some default value for the antenna delay recommended by DecaWave. That value seems to work almost fine (with only a slight shift) for three of the four modules I have, but produces a large discrepancy for the fourth one. That fourth module is generally problematic (I have had some problems with it, but it seems to work now [except for the discrepancy]), so I am not sure what to think. With DW1000_OPT_NO_ANT_DELAY set, the antenna delay is assumed to be zero, so the estimates need to be offset.
The device is started (initialized) with the following operation:
void dw1000_start (byte mode, byte role, word pan);
where:
mode	is one of 8 RF configurations (frequency, preamble, channel, etc.) which I have copied from the reference driver by DecaWave
role	determines the node's role, i.e., which end of the handshake the node wants to play; 0 means Tag (node A, according to the procedure described above), 1 means Peg (node B)
pan	is basically the network Id (the so-called PAN in 802.15.4 parlance); nodes belonging to different networks will not talk to (handshake with) each other (similar to our Network Id)

Note: theoretically, I could use our Network Id for the PAN, but the driver cannot assume that another radio (like CC1100, where the Network Id is prominent) is configured into the system. On the other hand, I am using our standard Node Id (the lower word of host_id, which is always known for every node) as the node's (short) address.
To switch the device off execute this:
void dw1000_stop ();
When the device is started with role 1 (Peg), the receiver is immediately switched on (note that it drains about 160mA) and the device begins to listen for POLL packets. Completed handshakes are communicated to the praxis as (compound) values arriving on a sensor (see BOARDS/OLIMEX_CCRF_DW1000 for the way that sensor is configured). A single value is described by this data structure (defined in dw1000.h):
 typedef struct {
word tag;	// Source
byte tst [6*DW1000_TSTAMP_LEN];	// Six time stamps
byte seq;	// Sequence number
} dw1000_locdata_t;
where:
tag	is the Tag Id of the handshake (the node sending the initial POLL packet)
tst	is a byte array storing the six time stamps produced by the handshake and consisting of 6*5 = 30 bytes, if DW1000_USE_SHORT_STAMPS is 0 (DW1000_TSTAMP_LEN is then 5), or 24 bytes, if short stamps are selected at compilation. The byte offsets to the respective timers are represented by these constants (defined in dw1000.h): / #define DW1000_TSOFF_TSP (DW1000_TSTAMP_LEN * 0) / #define DW1000_TSOFF_TRR (DW1000_TSTAMP_LEN * 1) / #define DW1000_TSOFF_TSF (DW1000_TSTAMP_LEN * 2) / #define DW1000_TSOFF_TRP (DW1000_TSTAMP_LEN * 3) / #define DW1000_TSOFF_TSR (DW1000_TSTAMP_LEN * 4) / #define DW1000_TSOFF_TRF (DW1000_TSTAMP_LEN * 5)
seq	is the handshake's sequence number (a single-byte value) arriving in the initial POLL packet (see below)

To retrieve the handshakes, the praxis should run an FSM with a state organized like this:
...
dw1000_locdata_t	location;
…
fsm … {
...
state EVENT:

read_sensor (EVENT, SENSOR_RANGE, (address)&location);
if (location.tag == 0) {
wait_sensor (SENSOR_RANGE, EVENT);
release;
}
...
If the tag attribute of the sensor value is zero, it means that there is no new handshake value to see. The sensor generates an event whenever a new handshake is received. Then, the tag attribute of the returned structure is set to the originating Tag Id.
When the node's role is 0 (Tag), the device is put to sleep after startup (the current drain is of order nanoamps). To start a handshake, the praxis has to store a value in an actuator (see BOARDS/OLIMEX_CCRF_DW1000 for the way that actuator is configured). The value consists of a single byte specifying the sequence number of the POLL packet, e.g.,
…
byte seq;
...
state POLL:
write_actuator (POLL, ACTUATOR_RANGE, (address)&seq);
...
If the driver is busy doing the previous handshake, the operation will block and auto-restart when ready.
A handshake is retried up to 4 times, if the RESP packet fails to arrive within 10 milliseconds after POLL. The Tag doesn't verify whether its FIN packet makes it to the Peg. Its end of the handshake completes with the departure of the FIN packet.

# Comments on power requirements

In the full listen mode, the device drains ca. 160mA. This (+ whatever negligible extras are needed for the microcontroller) is the current drain for a Peg constantly listening for POLL packets from Tags. With CC1100 on (in its full listen mode), the total drain is going to be about 180mA (i.e., a lot compared to our typical devices).
From the viewpoint of a Tag, about this much current is needed for the entire duration of a (proper) handshake which consists of a short TX burst (140mA), followed by listen (160mA), followed by another short TX burst. The duration of TX bursts is practically negligible (besides, the current drain is almost the same, only slightly less for TX than RX).
Before starting a handshake, the Tag wakes up the chip. Fortunately, while sleeping, the device needs a negligible amount of current (about 200nA). Initially, inspired by the reference driver, I used a relatively long delay, about 80ms to stabilize the chip's clocks. My recent experiments suggest that this delay is not necessary, but we have to perform more comprehensive tests. Practically, we can assume that the handshake cycle (as viewed by a Tag) consists of:
1. some initial delay at the current drain of 13-14mA
2. 9ms of the proper handshake at the current drain of 160mA
This is when the payload data rate is 100kbps (modes 0, 2, 4, 6). For the other data rate option, 6.8Mbps (modes 1, 3, 5, 7), the handshake duration reduces to about 4ms. For a Tag, this is the amount of time measured from the beginning of POLL transmission until the complete transmission of FIN. Optimistically, the first delay is just 1ms extra (but I am not 100% sure), so it (probably) can be ignored.

# Comments on calibration

My experiments so far have been very superficial. Given a pair of nodes, one acting as Peg, the other as Tag, I have compared estimates to actual distances (measured with a tape). Here are a few numbers (short stamps, no antenna delay).
Node 1 is Peg, Node 2 is Tag. The nodes are located 160cm apart (measuring from the centers of the antennas). No obstacles between the nodes. The estimate comes up as 155.69 (the average of 15 tests, the differences being surprisingly low, below 5cm). I have tried some other distances under the same circumstances. Here is the table:
distance (m)	estimate (m)	offset (m)
1.60	155.69	154.09
2.46	156.52	154.06
3.00	157.12	154.12

Thus, the offset is within the advertised 10cm accuracy margin (even considering the rather poor quality of my distance measurement). When I put myself in front of the Tag's antenna, the estimate for the 3.00m distance became 157.57, i.e., 45cm more, which may suggest that obstacles do play a role.
When I replaced the Tag node with another specimen (Node Id 3), the estimate for 3.00m distance was 157.11 (very close to that for Node 2). But for Node Id 4 (yet another specimen), it was 118.85, i.e., way off. Node 4 exhibited stable and correct indications, except for the different offset.
My initial idea for calibration (which seems to coincide with the rather simplistic treatment of that issue in the manual) is to assume that there are two additive components of the offset, specific to each of the two nodes. By trying the same Peg with a number of different Tags, one can arrive at the reliable estimate of the Peg's component. Then, assuming that Pegs have been calibrated, firing off a Tag once from a known location should yield the Tag's component.