# 10/05/08, 10/07/20
# Preamble

The role of this simple praxis is to test transmission/reception capabilities of nodes operating in a group. The present version is just something to start with. Probably, we will be adding more capabilities as needs arise.

# Preparation

Compile and download. All nodes in the test setup run the same code. They tell their IDs (which should be different) based on the flashed HOST_ID, whose interpretation is similar to, say, EcoNet. Use genimage to create downloadable images from the generic compilation output.

The Node ID, via which a node can be referenced, is the lower half of HOST_ID, which corresponds to the "Node number" as inserted by genimage. The prefix part, i.e., the upper half of HOST_ID encodes some startup parameters as follows:

16	8 7	0
_________________________________________
D A Z Z Z P P P C C C C C C C C

The lower byte encodes the RF channel, which, formally, can be any number from 0 to 255. Bits 8-10 encode the initial setting of transmitter power (0 - 7), bits 11-13 are the three least significant bits of the Network ID (and can be used to differentiate among multiple test setups operating in the same neighbourhood), bit 14, if set, indicates that the node should start "active", i.e., it will be transmitting measurement packets at the default interval of 1 second), bit 15 (the most significant bit) indicates power-down mode of the CPU (if set, the node begins in power-down mode).

For example, the standard prefix BACA (if you leave it as is), expands into:

1 0 1 1 1 0 1 0 1 1 0 0 1 0 1 0

which means: channel 202 (0xCA), transmission power 2, Network ID 0xF617 (0xF610 is the standard prefix used by the praxis), transmitter initially inactive, and starting in power-down mode. On the other hand, to select the maximum transmission power, channel 0, and power-up mode with active transmitter, you can use this prefix:

0 1 0 0 0 1 1 1 0 0 0 0 0 0 0 0

i.e., 0x4700. The Network ID field is arbitrary, but it must be the same for all nodes of the same setup. Note that nodes can be rendered active/inactive remotely. Also, their transmission power levels can be changed, as well as their power-down/power-up status. There is no way, however, to change remotely the channel number or the Network ID.

# Operation

Any node can be used to orchestrate an experiment. Such a node must be connected to UART at 9600 bps.

When a node resets, it produces a message that looks like this:

    Node: 19, NetId: F610, Channel: 6, XPower: 7, Powerup, Active
    Ready:

where your actual indications may vary depending on the initial settings (see the previous section). All numbers except Network ID are in decimal.

We shall discuss the operation of the praxis by explaining the meanings of commands that you can issue over the UART.

Command s (continuous transmission of measurement packets):

s [mindel [maxdel [minpl [maxpl]]]]

All parameters (four unsigned numbers) are optional. The command puts the node into active state whereby it will be transmitting so-called "measurement packets" at prescribed intervals. The idea is that nodes receiving such packets are expected to count them and report (upon request) the received counts. The arguments have the following meaning:

mindel	the minimum inter-packet interval in (PicOS) milliseconds (the default is 1024)
maxdel	the maximum inter-packet interval (defaults to 1024)
minpl	the minimum packet length (see below)
maxpl	the maximum packet length (defaults to 60)

A value that is not specified retains its previous (last or default) setting with the sanitizing procedure described below. If mindel < maxdel, the actual inter-packet interval will be randomized between the two values. The absolutely lowest limit is 256 milliseconds. Whatever values you specify, the praxis will try to sanitize them, i.e.,

- If the specified minimum is less than 256, it will be set to 256.
- If the specified maximum is less than the minimum, it will be set to the minimum. This also applies to the case when only the minimum is specified and the previous setting of the maximum turns out to be less than the new minimum.
- There is no limit on the maximum interval other than 65535.

Regarding the packet length, the absolute minimum is determined by the compiled-in configuration of sensors (whose values are reported in every measurement packet). In the present version of the praxis, the number of sensors is 4 (which coincides with the configuration of WARSAW_ILS). Whatever you specify for the packet length, the praxis will make sure that the actually assumed minimum is not less than the required minimum and that the assumed maximum is not less than the assumed minimum.

The layout of a measurement packet, which you don't have to know to run tests, is this (in words, starting from the very beginning):

NID	Network ID (required by the driver)
RCV	zero (this is used to tell measurement packets from other packets)
SND	Node ID of the sender
FLG	node flags associated with the sender (xmit power level + power-down state)
SEN	first sensor value
...
SEN	last sensor value
RND	random contents
...
RND	random contents
CHK	CRC (required by the driver)

The number of sensor values equals the declared number of sensors (i.e., 4 in the present version) and can be changed at compilation. Thus, the minimum length of a measurement packet, in bytes, including the CRC, is 10 + 2 x N, where N is the number of sensors. This amounts to 18 in the present version. If your specified minpl less than that, it will be bumped up to the required minimum. Also, if your specified (or previous) maximum (maxpl) is less than the new minimum, it will be set to the new minimum. If the maximum is greater than 60, it will be truncated to 60. In other words, whatever you specify, the praxis will make sense out of it.

If the effective minimum packet length is strictly less than the maximum, the praxis will randomize the actual packet length. Note that the specified minimum can be more than the absolute minimum. In any case, when a packet's length is more than needed to accommodate the sensor values, the unused words are filled with random contents.

Whenever a node receives a measurement packet, it is supposed to count it. If this is the first time the node hears from this particular sender, it will create an entry for the sender with the initial count of 1. At present, a node can accommodate up to 8 different senders. This can be increased in principle, but the format of reports (that you can request from nodes remotely) restricts that population to 9 nodes (that much can fit into one packet). We will do something about it, if it turns out to be a serious limitation.

Command q (stopping transmission):

The node's transmitter can be stopped (the node rendered inactive) with this command:

q

It can also be used to stop (abort) a collection of PATABLE statistics in progress (see command m below).

Command r (measurement report):

By executing this command, you can obtain a report from the current node (this report will be written to UART):

r

For example, you may see something this:

Stats:
Sent: 3576
Received from: 19: 2491
Received from: 20: 3387
Received from: 22: 831
Driver stats: 5976, 2, 0, 0
Ready:

The first value (Sent) is the number of measurement packets sent so far by the node itself. This is followed by the list of entries for all nodes from which the node has received measurement packets, along with the number of packets received. At the end we see the "driver statistics", i.e., four numbers produced by querying the PHY with PHYSOPT_ERROR. They stand for, in this order:

1. The total number of activations of the receiver. This happens whenever the device thinks it perceives something looking like a packet. This counter wraps around at 64K. When that happens, the next counter is automatically zeroed out.
2. The total number of packets that have been correctly received and passed to TCV/VINETI. Note that this can never be more than the previous value. Also note that with hardware CRC and the AUTOFLUSH option on, the two values will always be the same.
3. The exponential moving average of the transmitter's waiting time for channel access maxed at 4095 (PicOS) milliseconds. The formula, which is evaluated at every attempt at channel grab, is W_{n} = W_{n-1} times 0.75 + b times 0.25 , where W_n is the new calculated average, W_{n-1} is the previous average, and b is the current backoff (in PicOS milliseconds). If the transmitter gets the channel immediately, the backoff is assumed to be zero. Note that the reported value never grows above 4095 (which is considered an alarm condition).
4. The maximum backoff suffered so far by a single packet. This is maxed at 64K (i.e., word size).

Note that the driver statistics may include overheard packets belonging to other setups. They also include non-measurement packets of the present setup (see below). Thus, tallying them up with measurement reports may be difficult, depending on how clean your setup is.

Command c (clearing measurement statistics):

Here is a command to clear all the numbers shown with r:

c

It zeroes out all packet counters, as well as the driver statistics.

Command v (viewing received measurement packets):

v

will switch on reports on all received measurement packets. You will be seeing lines like this:

S: 19, L: 58, P: 7, R: 101, Q: 0, M: U, V: 2365, 234, 0, 1

The first number is the Node ID of the sender, the second number is the total length of the received packet, including the CRC. This is followed by the transmission power used by the sender, the RSSI reading at the receiver, and link quality (as returned by CC1100). Then (labelled with M) we have the power-down/power-up status of the sender (U means up, D means down) followed by the list sensor values. All numbers are in decimal. Note that stuffed words filled with random contents are not displayed.

Command n (cancelling packet viewing):

The reports are cancelled with:

n

Command d (putting the node in power-down mode):

This command:

d

to put the node into power-down mode.

Command u (putting the node in power-up mode):

u

puts the node into power-up mode. Note that the mode the node has started in is determined by its HOST_ID.

Command p (selecting transmission power):

This command:

p val

where val is between 0 and 7 inclusively, sets the node's transmission power according to the PATABLE in effect.

Command m (changing the contents of CC1100 registers):

When compiled properly [#define RADIO_OPTIONS ( ... + 0x40 ...)], the CC1100 driver allows you to provide supplementary definitions for the chip's registers that override standard definitions (this is done via PHYSOPT_RESET). With this command:

m reg1 val1 ... regn val4

you can redefine the contents of indicated registers. The arguments are byte-sized hexadecimal values. Their total number must be even. The first value gives the register number, the second its new content. Every m command overrides the effect of the previous one. An empty argument list removes the supplementary definitions.

Command t (collecting PATABLE statistics):

With this command you can start an experiment whereby the node scans through all 256 possible power settings corresponding to a PATABLE entry and exchanges packets with a selected neighbour to determine the perceived RSSI reading corresponding to the particular setting. The command takes two arguments:

t n c

where n is the node ID of the selected neighbour and c is the number of samples per one PATABLE setting (to average the readings).

The initiating node will set its formal power level to 0 (selecting the first PATABLE entry) and enter a loop in which it will reset the first entry starting from zero and going up to 255. For each setting, the node will poll the selected neighbour, which will subsequently respond with the RSSI at which the polling packet has been received. The node will try to receive c responses for each PATABLE setting re-trying every poll up to 16 times. For each PATABLE setting, from 0 to 255, the node will write to the UART a line like this:

PA: 00xx, rrr, cc

where xx is the PATABLE setting in hexadecimal, rrr is the averaged RSSI reading, and cc is the number of samples used to calculate the average. Normally, cc is equal to the c argument of the t command, however, it can be less if some responses haven't made it (despite 16 retries).

To interpret the results, it is recommended to direct the terminal output to a file and then read that file (as a comma-separated list of values) into a spreadsheet program and sort the lines by the second column.

A collection in progress can be interrupted (prematurely) with q. At the end of collection, the node resets the power setting to as it was before the collection.

Remote commands (S):

The interesting bit is that you can issue practically any of the above commands addressing it to a remote node (similar to Wlodek's old patent) by executing this:

S n command

where n is the Node ID of the node on which the command should be executed. For example, you can do something like this:

S 19 s

which will activate (start the transmitter of) node 19 with the standard (or previous) parameters. Needless to say, the following examples should all work (assuming the nodes are reachable):

S 19 s 512 4096 44 58
S 23 d	[putting node 23 into power-down mode]
S 19 q
S 25 p 6
S 21 m 1C 01 24 1F
S 24 v

The last one may make little sense, as the reports about received packets will be shown on the target node's UART, but is legit. You can also say something like this:

S 19 S 24 s 1024 1024 56 60

It may not be useful, but comes for free.

Note that remote commands (as well as responses to them) are sent in packets that are not considered measurement packets, so they are not "officially" counted by their recipients (although they do contribute to driver statistics). A packet carrying a remote command is characterized by nonzero in the RCV field, which identifies the single recipient of the command. The full format of a command packet (in case you think it concerns you) is this:

NID	Network ID
RCV	Node ID of the recipient
SND	Node ID of the sender
SER	serial number (used to match responses to commands)
CMD	command text
...
CMD	command text
CHK	CRC

The command text is represented as a straightforward string terminated with a NULL byte. Note that there is a limit on how much of the command string can fit into a packet. Excluding the NULL byte, this limit is 49 characters. BTW: the maximum length of a line entered from UART is 80 characters (excluding CR/LF).

Having received a command, the recipient responds with an ACK, which, in particular, gives some indication of success/failure. For example, you may see something like this:

Ready:
S 19 d
Ready:
OK from 19

The last line indicates that the command has been accepted by the recipient and, apparently, executed fine.

The sender will retry the command up to five times at 1 second intervals. If it receives no reply from the recipient, you will see something like this:

Ready:
S 233 d
Ready:
Timeout reaching 233

A reply looks like the original command packet up to and including the SER field, with the command text replaced with a response. In the simplest case, the response is a single word with 0 meaning OK, and nonzero indicating a failure. For example, instead of OK, you may see:

Error 6 from 23

I may make this message more friendly later. Here is the list of numerical error codes:

1. formal error (probably cannot happen)
2. no memory to acquire packet
3. node busy with a previous command
4. command syntax error
5. node out of memory (umalloc failure)
6. no room to run more threads
7. no such command

In the present version, only one (remote) command, r, triggers a non-trivial response. Having received it, the node will not send the count report to its UART, but rather to the sender. For example:

S 19 r
Ready:
OK from 19:
Stats of node 19:
Sent: 2108
Received from 17: 3908
Received from 18: 2201
Driver stats: 6001, 4, 2, 1

This way you can conveniently collect all reports from one place.

Please note that the range of packet counters is 65535. There is little sense, e.g., to leave an overnight experiment when a single node can transmit more than 64K packets (but you should be fine with, say, 12 hours, 1 packet per second).

Command C (changing the channel):

With this command you can change the RF channel of the node:

C ch nsec

where ch is the channel number (0 – 255) and nsec is a timeout interpreted as the number of seconds. The timeout argument is only interpreted when the command is received over the radio (it is ignored if the command has arrived from the UART). The node will switch to the indicated channel. If the command has been received remotely, the node will reset (interrupting any activity and effectively reverting to the default channel) if it receives no packet for the specified number of seconds. Use a large value for a semi-permanent switchover. The maximum timeout is 65536 seconds.

When sent remotely, the command will receive no acknowledgement (the sender will signal a timeout), which is normal.

A sample experiment:

Compile the praxis:

cd PICOS/PicOS/Apps/VUEE/RFTEST
mkmk WARSAW_ILS
make

Execute genimage. Set Image.a43 in the praxis directory as the input file, and, say, Load.a43 as the output file. Leave the Cookie field as is, and enter 0700 into the Prefix field. This prefix selects channel 0, power 7, and makes the nodes initially inactive. Create images for, say, six nodes. Enter 1 into the From field and 6 into How many. Press Generate. This will produce six files named like Load_07000001_00001.a43 through Load_07000006_00006.a43. Load those files into the nodes and power them up.

Connect UART to node 1. Execute:

s

on that node. This will activate the transmitter on node 1. After some time, execute:

q

to stop the transmitter. Then fetch reports from the remaining nodes, e.g.,

S 2 r
S 3 r
...

and so on. Compare the numbers. You may also start transmitters on multiple nodes, in particular all of them and, at the end, compare the per-sender counts for all recipients.

Here is how you can try to find a good PATABLE setting for your frequency. Execute:

v

which will allow you to see all received packets, including their RSSI. Then select zero power level on some other node, e.g.,

S 2 p 0

This selects (for node 2) the first (number zero) entry from PATABLE whose formal location (register number is 0x3E. Start periodic transmissions on node 2, e.g.,

S 2 s 1024

and inspect the RSSI readings of the received packets. Be executing:

S 2 m 3E 1F

you change the effective PATABLE entry to 0x1F (note that both values are in hex), which should affect the RSSI readings from node 2. You can try any value from 00 to FF.