# RFTEST 18/06/24

Quick instructions for a CC1350 test involving LAUNCHPAD and SENSORTAG

Read the full document for a comprehensive review of the commands.
Do this:
1. Compile the program for the LAUNCHPAD. In PIP, make sure to select CC13XX → CC1350_LAUNCHXL from Configuration → Arch + Board …, then do Build, as usual.
2. Customize the image. Do Execute → Customize image … In the Type selection, choose IHEX, set NetId to 8700, set From to some initial node Id, e.g., 10, and How many to the number of LAUNCHPAD nodes that you want to flash. Click Generate to create the images.
3. Configure the flash loader. I am assuming you have installed Flash Programmer 2 from Texas Instruments. In Configuration → Loaders … select Use at Command line and Select the loader program. For that, browse to srfprog.exe in the bin folder of your Flash Programmer 2 installation folder. Note that the default (my) setting for the project may be different from yours. Make sure that the Arguments line looks like this:
  -t lsidx(0) -e pif -p -f %f.hex
4. Flash the images into the LAUNCHPAD devices. For each device, in turn, plug it to the computer via a USB cable. Click Execute → Upload image … and select the corresponding customized image for the device, such that different devices are assigned different Id's. Then click Go ahead. The flasher occasionally hangs. Should that happen, Abort it (from the Execute menu) and try again. When the operation succeeds and the device resets, it will blink both LEDs once, and then quickly blink the red LED 8 times. Then the green LED should blink once every 4 seconds indicating that the device is up and running with the radio in the default off state.
5. Do the same for the SENSORTAG devices. Compile the same application for CC1350_SENSORTAG, customize it in exactly the same way as before (selecting a different initial node Id, e.g., 20), and flash those devices using the same loader configuration. The (single) LED on each device should blink 5 times after reset (the different number of blinks indicates that the SENSORTAG device is configured without UART). Then, the LED should briefly blink once every four seconds to indicate that the node is operational with the radio off.
6. Connect at least one of the flashed LAUNCHPAD devices to the computer (via a USB cable), so you can access the UART. When you plug in a LAUNCHPAD device and then invoke piter, you will see two COM ports. One of them is the UART port (the other is for JTAG access). The best way to see which is which is to to see Ports in Device Manager (they are clearly marked in there). Connect Direct, at 9600. When connected properly, and the device resets (for which you can use the button on the programmer's side), you will see the standard PicOS banner, plus a message looking like this:
  Node: 10, NetId: F610, Rate: 3, Channel: 0, XPower: 7, Powerdown, Passive
  Ready 10:
The number (10) is the Node Id.
1. Power up the remaining nodes you want to play with. They all start in the “radio off” state and blink LEDs on startup (as described above). For a trivial experiment, let us assume one LAUNCHPAD (connected to piter) + one SENSORTAG.
2. In the piter window (connected to the LAUNCHPAD) enter these commands in sequence (see the full document for their interpretation):
  v 3	[ verbose, i.e., show transmitted and received packets ]
  s	[ start sender ]
  g	[ start receiver ]
As soon as you start the sender, you should be seeing outgoing packets in the piter window, the message looking like (→ N: number, etc.).
1. Turn the radio on on the SENSORTAG. For that, press button number 0, the one on the opposite side of the connector. The LED on the SENSORTAG will blink quickly 4 times, and then it will be blinking on every packet reception (the node should immediately start receiving packets from the LAUNCHPAD). You will also see the packets received by the LAUNCHPAD in the piter window.
2. When you get bored, you can turn off the SENSORTAG. To turn off the radio, press the button (the same button) briefly. This reverts the device to the initial “radio off” state. The LED will blink briefly once every 4 seconds. The current drain in this state is about 10 μA, so there should be no need to remove the battery/batteries.
3. To reduce the current drain even further, you can shutdown the SENSORTAG (deep power-down). For that, push the button and hold it for 5+ seconds, until the LED begins to blink rapidly; then release the button. Note that, while you are holding the button, the LED may still blink once normally (as it does every 4 seconds); don't release the button then, but wait for the series of quick blinks. The device shuts down (no more blinks). The current drain is about 4 μA. Normally, the device would drain less than 1 μA, but the SENSORTAG has a voltage regulator. To wake up the device from shutdown, just press (briefly) the same button. The device will behave, basically, as after reset, i.e., it will become active in the “radio off” state.
  The same mechanism works on the LAUNCHPAD, which means that you can also start and stop the radio on that device (as an alternative to the UART commands) by pushing button 0 (the one on the side of the USB socket). You can also shut the device down in the same way. In the standard power-down mode (with the radio turned off, but not in shutdown), LAUNCHPAD drains somewhat more current than SENSORTAG, because its low-power state is shallower (as needed by the UART). The low-power states on CC1350 are way more complicated than on MSP430.