The Location Engine

Version 0.052
May 31, 2013

Proprietary and confidential
# Preamble
This document describes software for experimenting with profiling-based, indoor location tracking systems built of Olsonet wireless nodes. The only hardware prerequisite assumed from the RF module is its ability to report some measure of RSS (the so-called Received Signal Strength Indication) of a packet arriving from a node in the neighborhood.
# The principle of operation
A deployed location tracking system consists of a number of static Pegs collecting RF signals from mobile Tags whose locations are tracked. The tracking is driven by a database of points, which represent aggregate signal samples collected at known locations within the perimeter of the monitored area. At this time, we assume 2-D tracking. Should it work, we may want to upgrade the system to 3-D.
## The database of points
Following the deployment of Pegs, the system has to be fed with knowledge consisting of reference readings collected at selected points within the monitored area. This is accomplished by using a Tag node (or multiple Tag nodes) to send signals from known locations. Each time a signal is received by the OSS monitor, the Tag's location (in terms of Cartesian coordinates) is stored in the database along with the RSSI readings of those Pegs that could directly perceive its signal. In the target version of the system, there will be a special embodiment of a Tag node to assist the operators in this task. Such a node may have the capability to convey to the OSS its location, which can be entered manually by the operator, e.g., based on a clickable map of the area. The design details of such a node are beyond the scope of the present study.
A single measurement collected in the fashion described above and entered into the database will be referred to as a point. It is characterized by the following set of attributes:
1. coordinates, i.e., two floating point values denoted x, y. We assume that the coordinates are expressed in meters
2. properties: a 32-bit value
3. Tag: the 32-bit identifier of the node sending the sampling packet
4. the list of associations, consisting of one or more pairs <peg, s>, where s represents the RSSI reading of the packet at the respective Peg.
We assume that nodes are uniquely identified by 32-bit unsigned integer numbers different from zero. Node roles are transparent with respect to this numbering, i.e., two different nodes always have different numbers regardless of their roles (Tag, Peg). Also, the Tag attribute of a point need not refer to an actual Tag; the semi-infrastructure of (immobile) Pegs can auto-profile itself (as explained below) whereby the Pegs are also allowed to send sample packets (pretending to be Tags).
The role of properties is to differentiate among points collected under incompatible conditions, e.g., transmission power, frequency, and so on. The idea is that the RSSI readings of packets emitted by Tags under specific conditions should only be interpreted within the context of points collected under the same conditions. Here is the present assignment of bits in properties (bit 0 is the least significant one):
0–2	The transmission power of the sample packet encoded into one of eight discrete levels.
31	The “static” flag; if set, it means that the Tag attribute of the point refers in fact to a Peg, as opposed to a (mobile) Tag. In other words, the “Tag” can be assumed to be an immobile member of the semi-infrastructure of Pegs.

The remaining bits are reserved for future extensions.
The second element of an association pair (s) encodes the RSSI reading at the corresponding Peg when it received the reference signal from the Tag. Note that for the actual comparisons and calculations applied to the points when estimating locations it may make sense to transform the RSSI values, e.g., by shifting them such that the minimum value is zero, amplifying (expanding) some ranges (considered more reliable), and so on. To avoid confusion with the raw RSSI readings, such a transformed value will be referred to as SLR, for Signal Level Representation. It should be noted that the values stored in the database (as second elements of association pairs) are always raw and unprocessed RSSI readings as returned by the RF module. Any transformations needed to turn them into SLRs are applied when the database is read from its file representation into memory. When the (possibly updated) database is written back to a file, only the raw RSSI values are stored. This approach facilitates experimenting with various RSSI → SLR conversion functions without loosing the original information stored in the collected samples.
The system avoids a physical interpretation of RSSI/SLR, except for assuming (implicitly and loosely) that values collected from close points will tend to be close. The primary measure of closeness of the tracked Tag to a point is the discrepancy between the point's association list and the current association list of the querying Tag.
Generally, the coordinates of points stored in the database need not follow any particular geometric distribution or patterns. The only assumed property of a point is that its coordinates are reasonably accurate and that its association list represents an actual set of readings for a Tag that sent a signal from that location. Clearly, the points' locations should collectively well cover the entire area. It may make sense, especially in regions with tricky RF propagation characteristics, to collect multiple points at the same (or close) locations. The procedure of collecting points for the accurate operation of our location tracking system may require a bit of insight, experience, and luck. Notably, inaccuracies perceived during normal operation of the system can be rectified on-the-fly, e.g., by adding new points and/or removing some points from the database.
## Location tracking
Consider a mobile Tag periodically broadcasting RF packets within the monitored area. A complete reading of such a packet conveyed to the OSS monitor is a list of associations, i.e., <peg, s> pairs, identifying the Pegs that have directly received the packet and including their RSSI readings. This list of associations is matched against the points stored in the database with the objective to identify the set of points that most closely match the list. Once those points have been found, the Tag's location is estimated as a weighted average of their coordinates, where the weights depend on the discrepancies between the the Tag's association list and the association lists of the respective points extracted from the database.
Note that this approach does not attempt to triangulate anything or guess at a correlation between RSSI/SLR values and geometric distance. It is solely concerned with finding good matches in the database, which need not depend on any particular signal propagation properties, but only on the actual readings obtained from the reference points.
# The experimental location software
The root directory of the set is named LOCATION. By executing make in that directory, you will build libloc.a, which is the location library to be linked to the application. By including locengine.h, the application can take advantage of simple database functions and the experimental version of the location engine.
The pivotal data structure described in locengine.h represents a point stored in the database and looks like this:
typedef struct {
float	x, y;
u32	Tag;
u32	properties;
u16	NPegs;
alitem_t	Pegs [0];
} tpoint_t;
Types u32 and u16 are simple unsigned integer types defined in ntypes.h. NPegs determines the length of the association list stored in the Pegs array. As the length of this array depends on the length of the association list, the actual complete size of a point structure varies. Here is the way to allocate memory to a point (assuming NPegs stores the number of entries in the association list):
tpoint_t *pp;
...
pp = (tpoint_t*) malloc (tpoint_tsize (NPegs));
The requisite macro (tpoint_tsize) is defined in locengine.h.
A single element of the association list is described by this structure:
typedef struct {
u32	Peg;
u16	RSSI;
float	SLR;
} alitem_t;
Note that the SLR value is a float-type number while RSSI is a not-too-long integer. The RSSI values produced by CC1100 (in the “Warsaw” board used for our experiments) are 8-bit, unsigned, integer values.
## The database
The present implementation of the database is naive, but it does work and provide most of the functionality that may ever be needed (so it should be perfectly OK for experiments). I have encapsulated those operations in a way that should make it easy (hopefully trivial) to port this system to a real database. As it is now, the points are simply stored in a file sequentially as ASCII strings (which, BTW, makes it easy to inspect them directly), and they are all read into memory when the database file is opened. Also, when the database is closed (and it has been modified), the points are written back to the file overwriting the previous content.
Here is the list of database operations:
int db_open (const char *fname, const char *pname);
Opens the database stored in file fname. If the file doesn't exist, a new database is created, which is initially empty. Returns 0, if the database is new, and 1 otherwise.
The second argument is interpreted as the name of an XML file providing parameters for the location engine. The format of that file is described below (in Section 3.2). The argument can be NULL in which case the parameters will assume default values.
void db_close (void);
Closes a previously opened database. If the database has been modified (some points have been added or deleted), it will be written back to the database file (that was previously specified as the first argument of db_open).
void db_add_point (tpoint_t *tp);
Adds the specified point to the database. The argument must be a pointer created by malloc (see above). The structure passed via this pointer must not be touched by the program after the function returns. In particular, it must not be deallocated (freed).
void db_start_points (u32 peg);
The function initializes the operation of reading through a set of points. If the argument is zero, that set covers all the points stored in the database. Otherwise, the argument identifies a Peg, and the set of points is restricted to those that include the Peg in their association lists.[1]
[1] This feature (i.e., the possibility to restrict the scan to points including a specific Tag in their association lists) was relied upon by the previous version of the engine. It is less useful now, but has been retained just in case.
tpoint_t *db_get_point (void);
Returns the next point from the set initiated with db_start_points. Subsequent calls to db_get_point return the same point until the cursor is advanced with this function:
void db_next_point (void);
The set has been completely scanned when db_get_point returns NULL. Here is the way to read through all points in the database:
tpoint_t *tp;
...
for (db_start_points (0); (tp = db_get_point ()) != NULL;
db_next_point ()) {
... handle_point (tp);
}
Note that tp points directly to a point structure stored in the database. Consequently, the program should not change its attributes or try to deallocate it.
void db_delete_point (tpoint_t *tp);
The function deletes the indicated point, which must be one of the points actually stored in the database.
void db_sort_al (alitem_t *al, int n);
The function sorts the association list (array) specified as the first argument whose length is assumed to be n, such that the Pegs occur in the increasing order of their identifiers. Before a new point is added to the database, this function is applied to the point's access list to make sure that all points stored in the database have their association lists sorted this way. This facilitates searching for specific Pegs and matching two association lists for calculating their discrepancy (see Section 3.2).
## Procedures and parameters
The optional XML data file specifies a few parameters affecting the operation of the location engine. The list of parameters will likely grow, especially if our tests are successful. We shall discuss those parameters in the context of the relevant components of the location estimation procedure.
Here is a sample data file mentioning all the parameters:
<data>
<slr> (30 0.0) (240 210.0) </slr>
<dis min="2" fac="1.5" tag="-140"/>
<sel min="3" max="9" fac="2.7"/>
<ave for="exp" fac="3.2">
</data>

### RSSI → SLR conversion
The <slr> element of the data set describes the mapping of RSSI to SLR. Its body consists of a set of pairs interpreted as a piecewise linear function. The minimum number of pairs is two, like in the above example which says that RSSI 30 should be translated to SLR 0.0, and RSSI 240 should map to SLR 210.0. All values in between will be interpolated linearly, so for example, RSSI 50 will become SLR 20.0. Also, any value of RSSI below 30 will be treated as 30 (map to SLR 0.0) and any value above 240 will be treated as 240 (map to SLR 210.0), i.e., the edge pairs bound the function.
Note that RSSI is integer while SLR is float. The RSSI values must be monotonically increasing, but the SLR values need not. The limit on the number of pairs is 256. The parentheses are optional: any non-numerical delimiters can be used to separate the numbers.
The default way to transform RSSI into SLR, assumed if there is no XML data file (the second argument of db_open is NULL) or the file contains no <slr> element, is to use identical mapping SLR = RSSI whose only effect is to translate the integer values to float.
### Calculating distance between association lists
The <dis> element (whose body is ignored) affects the procedure of calculating the vector distance (we call it discrepancy to avoid confusion with the geographical distance between points on the plane) between association lists or, more specifically, between the association list of a query and the association list of a point stored in the database.
The input to the procedure consists of these items:
1. the ID of the node sending the query
2. the association list of the query.
3. the point
Its purpose is to determine how close the query's association list is to the association list of the point and to either select or reject the point as a prospective contributor to the location estimate. The idea is to focus on a few points closest to the query's association list and then average their coordinates into the estimated coordinates of the node (Tag) sending the query.
The first item from the above list, i.e., the ID of the Tag sending the query, is not used by the present version of the discrepancy function. Note that it is conceivable to use it in the future, e.g., to correct for the known (precomputed and stored in some database) characteristics of specific devices.
In the first step, the function determines how many Pegs occur simultaneously in both association lists, i.e., in the association list of the query as well as in the association list of the point. Let this number be M{} . If M < min , the discrepancy is assumed to be infinite and the point is ignored (rejected). This means that only those points whose association lists share at least min Pegs with the association list of the query will be taken into account.
Let 1<=j<=M {} index the SLR values in the two association lists corresponding to the shared Pegs. The discrepancy is calculated as:
D = sqrt {{ sum_{j=1}^M ({bar v}_j - v_j )^2 } over {M^{fac} } }
where { bar v }_j and v_j are the SLR values from the corresponding entries of the two association lists and fac is a factor (in fact an exponent) rewarding (on perhaps penalizing, if less than zero) larger values of M , i.e., longer matched subsets of the two lists. The default value of fac = 1 normalizes the distance to the number of vector dimensions.
The parameters min and fac are specified as attributes of the <dis> element in the data set. The third attribute of that element, tag , specifies how to interpret the Tag attribute of the point. Note that for some points, when the “static” bit in the point's properties is set (Section 2.1), the Tag attribute can be interpreted as one of the Pegs. This interpretation is intended for auto-profiling whereby the Pegs can also send sample packets causing points being added to the database. Note that the association list of a point resulting from such a packet will have no entry for the sending Peg, even though had the packet been sent from the Peg's location by a regular Tag, there most likely would have been a strong reading reported by that Peg. Consequently, it may make sense to account for this special feature of such a point by trying to interpret its Tag attribute as a Peg (effectively adding an entry to the point's association list) with some assumed strong reading.
If the <dis> element specifies a tag attribute, the value of that attribute is interpreted as the assumed RSSI (note: RSSI, not SLR) reading of any “static” Tag. The effect will be as if the association list of the point were extended by one more entry with the Tag attribute used as the Peg, and the tag value (from <slr>) inserted as the corresponding RSSI. If tag is negative (as in the above example), its effective value is negated (i.e., taken as absolute value) and assumed to represent the lower limit above which the discrepancy will be set to zero. This means that any query reading (whose Peg matches the point's Tag) equal to or larger than the absolute value of tag will be treated as exactly equal to that value, i.e., the difference { bar v }_j - v_j for that particular element of the vector will yield zero (for a smaller reading, the difference will be calculated as usual).
The defaults assumed if there is no data file, or there is no <dis> element, or the <dis> element does not specify a particular attribute are: min = 1 , fac = 1 , tag = 0 . The last setting means “no Tag interpretation”, i.e., the association list of a point is never extended by the Tag entry.
### Selecting close points
Given a query, the location engine scans all points in the database and (conceptually) sorts them in the increasing order of their discrepancies calculated as described in Section 3.2.2. Points with properties different from the properties attribute of the query[2] or yielding infinite discrepancy are immediately rejected. Only the first max points are stored at any time, i.e., at the end of the pass the program has located up to max points closest to the association list of the query. Note that we mean closest in the sense of our vector metrics described in Section 3.2.2, rather in any geographical sense. Also note that in a pathological case the number of points produced this way can be zero. When this happens, the procedure immediately fails.
[2] Ignoring the “static” flag.
If everything is OK, the set of points undergoes a further trimming. Suppose that the number of points is 0 < N <= max , and D_i, 1 <= i <= N denote their discrepancies calculated as prescribed in Section 3.2.2. The program calculates the average discrepancy:
D_{avg} = { sum_{i=1}^N D_i } over N
and multiplies it by the tolerance factor fac to obtain D_{max} = D_{avg} times fac . Then it goes through all N points in the decreasing order of D_i rejecting those points where D_i > D_{max} , for as long as the number of remaining points does not fall below min . If the set of points has been reduced this way (i.e., any points have been trimmed out), and the new value of N is still greater than min , the program repeats the trimming procedure (with the new values of N , D_{avg} , and D_{max} ). These iterations continue until either N reaches min , or no more points can be eliminated. Whatever remains is the final set of points to be used for location estimation.
The three parameters of the above procedure: min , max , fac , are specified in the <sel> element of the data set. The defaults assumed if there is no data file, or there is no <sel> element, or the <sel> element does not specify a particular attribute are: min = 1 , max=1000 , fac = 0.1 .
### Location estimation
Given the final (nonempty) set of points calculated as described in Section 3.2.3, the location of the query is determined by averaging the coordinates of the final set of points. Suppose that the number of those points is N and their coordinates are u_i = (x_i, y_i), 1 <= i <= N . As before D_i denote their respective discrepancies. The averaging is weighed by the discrepancies, such that points with smaller discrepancies contribute more. There is a choice between two averaging formulas.
The linear formula works like this. Let
 D = sum_{i=1}^N D_i
be the sum of all discrepancies of the final set of points. The (unnormalized) weigh of point i is calculated as:
W_i = (D – D_i)^fac
Note that lower D_i results in a higher weigh with the difference amplified by fac .
With the exponential formula, the weighs are:
W_i = e^{-{D_i over D_{avg}} times fac}
where D_{avg} is the average of all the discrepancies D_i . The average is introduced to make the weights scale invariant.
Then, in both cases, the location estimate is calculated as:
u_e = { sum_{i=1}^N W_i times u_i } over { sum_{i=1}^N W_i }
The program accounts for the pathological case of all D_i being zero (or very close to zero) in which case all weighs are assumed to be equal (note that this is taken care of automatically by the exponential variant).
The two parameters of the above scheme are specified by the <ave> element of the data set. The for attribute selects the averaging formula: “lin” or “exp”, and the fac attribute specifies the factor. The defaults assumed if there is no data file, or there is no <ave> element, or the <ave> element does not specify a particular attribute are “lin” and 1.
## Using the location engine
Assuming that a database of points has been opened, this function carries out the actual location tracking:
int loc_locate (u32 tag, alitem_t *al, int N, u32 prop,	float *X, float *Y);
where:
tag	is the ID of the querying node (ignored by the present version)
al	is the association list of the query
N	is the length of the association list
prop	is the properties attribute of the query
X,Y	are the return values of the estimated coordinates

The function carries out the procedure described in Sections 3.2.1 through 3.2.4 and returns the number of points in the final set (Section 3.2.3). Zero means that the procedure has failed and the return coordinates have not been set. Anything other than zero can only be positive and it means that the estimated coordinates have been assigned.
Note that the association list passed as the second argument to the function need only provide the RSSI values (not the SLR values, which will be calculated by the function). Also, the list doesn't have to be sorted, i.e., the Pegs can occur in any order. The function starts by preprocessing the list sorting it by Peg numbers and transforming the RSSI values into SLR.
One more function provided by the location engine (which is in fact more related to database operation) is:
int loc_findrect (float x0, float y0, float x1, float y1,
tpoint_t **tps, int N);
which returns up to N points falling into the specified rectangle. Those points are returned in tps, whose size should be at least N. The total number of such points in the database is returned via the function value. If it is greater than N, it means that some points could not be accommodated in the array.
# Two programs using the tools
Subdirectory TEST contains two programs. One of them generates a randomized database of points, the other provides a simple interface to the functions described above, i.e., allows you to manually enter queries to the database and the location engine. Having executed make in the main directory (and generated libloc.a), you can run make in TEST, which will create two executables: gen_random_db and query.
## Generating random databases
This is accomplished by gen_random_db. The databases generated by the program are naive and unrealistic, and their sole purpose is to test the engine functions.
The program reads a few numbers from standard input (see file g_data.txt for an example) and creates a database in file points.db. Make sure that this file doesn't exist (or is empty) before executing the program, as otherwise the new points will be added to the existing database. The data set consists of 9 numbers. The first four describe the bounding rectangle for the set of points: X_0, Y_0, X_1, Y_1 . The next two numbers specify the propagation range r (in meters) and the redundancy u , which will affect the population (density) of Pegs. The seventh number tells how many auto-profile points should be generated for each Peg. The next number determines the fuzziness (the extent of randomization) and should be well below 1.0. The last number, N , tells the program how many points are to be generated.
The program starts by generating Pegs on a regular grid spaced about r/(1+u) meters apart. The spacing is adjusted, such that the distribution of Pegs is even, i.e., the boundary rows and columns of Pegs fall exactly on the rectangle's perimeter. Then, the program generates N points randomly distributed within the rectangle. The association list of each point consists of those Pegs that are located no further than r meters away from the point (with some randomized factor depending on the fuzziness). The RSSI of each Peg on the list is a number between 0 and 250 linearly scaled to the distance and slightly randomized.
If the specified number of auto-profile points per Peg is nonzero, the program will add to the set of points that many points per every Peg coinciding with the Peg's location. Note that they are generated above the N points created in the previous step. The association list for such a point will be built in the same way as for a regular point, except that the Peg will be guaranteed “not to receive the query packet”, i.e., it will have no entry in the association list. Instead, it will be included as the Tag of the point, and the “static” flag will be set in the point's properties.
## Queries
The second program, query, provides a command-line interface to the engine. When you call it without arguments, it will open or create a database file with the standard name points.db using the standard XML data file params.xml. If there is a single argument, then it provides the file name for the database (with the default name used for the data file). If there's a second argument as well, then it is interpreted as the data file name.
Here is the list of commands (you will see a brief menu when you enter an invalid command, in particular help). The first letter of the command keyword is all that matters: any subsequent letters are skipped until a blank.
a x y tag prop npegs p v ... p v
Example:
a 110.3 221.1 401 0 7 1 34 2 39 3 55 9 16 12 35 17 88 22 255
The command adds a point to the database. The first two arguments are the coordinates, the third number is the Tag attribute, the fourth argument provides properties, the fifth argument specifies the length of the association list. This is followed by the association list consisting of the prescribed number of pairs: Peg, RSSI.
For legibility, you can group values using brackets < >, as well as commas, which are ignored in the command string, e.g., the above command can be written as:
a <110.3 221.1> 401, 0, 7, <1 34><2 39><3 55><9 16><12 35><17 88><22 255>

f x y	or
f x y r	or
f x0 y0 x1 y1
Examples:
f 122.3 456.1
f 122.3 456.1 3.5
f 122.3 456.1 256.5 789.0
The command finds and displays points. In the first case, it finds the single point located closest to the specified coordinates. In the seconds case, it finds all points located within the radius r of the specified coordinates. In the third case, it finds all points within the rectangle described by the four coordinates.
The located points are stored in a buffer from where they can be listed again with this command:
s
which takes no arguments. The points stored in the buffer are numbered from 1 up.
This command:
d pn ... pn
deletes from the database the indicated points. The numbers following d refer to entries the point buffer.
p peg
This command locates all points having the specified Peg in their association lists. The located points are displayed and stored in the buffer.

l tag prop npegs p v ... p v
Example:
l 5 0 4 1 34.5 2 55.6 7 88.2 19 41.6
This command invokes the location engine to estimate the coordinates of a hypothetical Tag with the specified properties and association list. The arguments are as for the a command with no coordinates (see loc_locate in Section 3.3). In response, the program displays the estimated coordinates and the value returned by loc_locate (the actual number of points used for the estimation).
z
This commands lists the parameters as read from the XML data file as well as some statistics regarding the set of points currently present in the database.
q
This command takes no arguments. It closes the database (writing it back to the file, if modified) and exits the program. Note that all modifications to the database (introduced with commands a and d) are volatile until the database is closed.