Location Engine
Attempt 1

Version 0.02
March 13, 2008

Proprietary and confidential
# The Principle of Operation

The enclosed software implements a tentative idea to be explored and verified. If the idea works, this software can be used as the seed of a true location tracking system. The present version is intended for experiments only.

A deployed location tracking system consists of a number of static Pegs collecting RF signals from mobile Tags whose locations are tracked. The tracking is driven by a database of points, which represent aggregate signal samples collected at known locations within the perimeter of the monitored area. At this time, we assume 2-D tracking. Should it work, we shall upgrade the system to 3-D monitoring, possibly treating the third dimension (i.e., height) differently from the other two.

# The database of points

Following the deployment of Pegs, the system has to be fed with knowledge consisting of reference readings collected at selected points within the monitored area. This is accomplished by using a Tag node to send signals from known locations. Each time a signal is received by the OSS monitor, the Tag's location (in terms of Cartesian coordinates) is stored in the database along with the RSSI readings of those Pegs that could directly perceive its signal. In the target version of the system, there will be a special Tag node to assist the operators in this task. Such a node may have the capability to convey to the OSS monitor its location, which can be entered manually by the operator, e.g., based on a clickable map of the area. The design details of such a node are beyond the scope of the present study.

A single measurement collected in the fashion described above and entered into the database will be referred to as a point. It is characterized by the following set of attributes:

1. coordinates, i.e., two floating point values denoted x, y. We assume that the coordinates are expressed in meters
2. properties: a 32-bit value
3. the list of associations, consisting of one or more pairs <peg, s>, where s represents the RSSI reading of the reference Tag at the respective Peg.

We assume that Pegs are identified by 32-bit unsigned integer numbers different from zero. The role of properties is to differentiate among points collected under formally different conditions, e.g., transmission power, frequency, and so on. The idea is that signals emitted by Tags under specific conditions should only be interpreted within the context of points collected under the same conditions. The various possible discrete sets of conditions can be represented as bit patterns encoded into the single properties attribute. The assignment of values to this attribute will be decided later. For now, we may assume that it is zero: our experiments will be done under uniform conditions.

The second element of an association pair (s) represents the RSSI reading at the corresponding Peg when it received the reference signal from the point. It does not have (an probably shouldn't) be equal to the physical RSSI reading. It may make sense to transform the RSSI values to make the matching described further in this document work better. For example, large values may be amplified. As the transformation will be performed by the OSS monitor, rather than the Pegs, the program can factor into it potentially complex criteria. In particular, different transformation formulas may be applied to different Pegs, e.g., some Pegs may be considered more authoritative or reliable than others. To avoid confusion with physical RSSI, from this point on, the value in question will be referred to as SLR, for Signal Level Representation.

The system assumes little about the physical interpretation of SLR. The algorithm described further in this document tacitly treats larger values as indicative of proximity (specifically in step 1, where the population of points to examine is narrowed down to those that are perceptible by the Peg that appears to be “the closest” to the tracked Tag). But that can be easily changed and replaced with other criteria. The primary measure of closeness of the tracked Tag to a point is the discrepancy between the point's association list and the current association list of the Tag.

Generally, the coordinates of points stored in the database need not follow any particular geometric distribution or patterns. The only assumed property of a point is that its coordinates are reasonably accurate and that its association list represents an actual set of readings for a Tag that sent a signal from that point. Clearly, the points should collectively well cover the entire area. It may make sense, especially in regions with tricky RF propagation characteristics, to collect multiple points at the same (or close) locations. The procedure of collecting points for the accurate operation of our location tracking system may require a bit of insight, experience, and luck. Notably, inaccuracies perceived during normal operation of the system can be rectified on-the-fly, e.g., by adding new points and/or removing some points from the database.

# Location tracking

Consider a mobile Tag periodically broadcasting RF packets within the monitored area. A complete reading of such a packet conveyed to the OSS monitor is a list of associations, i.e., <peg, s> pairs, identifying the Pegs that have directly received the packet and including their SLR indications. This list of associations is matched against the points stored in the database with the objective to identify the set of points that most closely match the list. Once those points have been found, the Tag's location is estimated as a weighted average of their coordinates, where the weights depend on the discrepancies between the the Tag's association list and the association lists of the respective points extracted from the database.

Note that this approach does not attempt to triangulate anything or guess at a correlation between RSSI and geometric distance. It is solely concerned with finding good matches in the database, which need not depend on any particular signal propagation properties, but only on the actual readings obtained from the reference points.

# Experimental location software

The main directory contains these files: ntypes.h, locengine.h, locdbase.c, and locengine.c. By executing make in this directory, you will build libloc.a, which is the location library to be linked to the application. By including locengine.h, the application can take advantage of simple database functions and the experimental version of the location engine.

The underlying data structure, described in locengine.h, represents a point stored in the database and looks like this:

typedef struct {
float	x, y;
u32	properties;
u16	NPegs;
pegitem_t	Pegs [0];
} tpoint_t;

Types u32 and u16 are simple unsigned integer types defined in ntypes.h. NPegs determines the length of the association list stored in the Pegs array. As the length of this array depends on the length of the association list, the actual complete size of a point structure varies. Assuming that N stores the length of the association list, here is the way to allocate memory to a point:

tpoint_t *pp;
...
pp = (tpoint_t*) malloc (tpoint_tsize (N));

The requisite macro (tpoint_tsize) is defined in locengine.h.

A single element of the association list is described by this structure:

typedef struct {
u32	Peg;
float	SLR;
} pegitem_t;

Note that the SLR value is a float-type number. There is no need to use type double for storing point locations and SLR readings, as the accuracy of representation is unavoidably going to be quite crude. On the other hand, all calculations carried out by the program are done with type double, to keep their numerical properties as decent as possible.

# The database

The present implementation of the database is a stub, but it does work and provide most of the functionality that may ever be needed. I have encapsulated those operations in a way that should make it easy (hopefully trivial) to port this system to a real database. As it is now, the points are simply stored in a file sequentially as ASCII strings (which, BTW, makes it easy to inspect them directly), and they are all read into memory when the database file is opened. Also, when the database is closed (and it has been modified), the points are written back to the file overwriting the previous content.

Here is the list of database operations:

int db_open (const char *fname);

Opens the database stored in the specified file. If the file doesn't exist, a new database is created, which is initially empty. Returns 0 (if the database is new), and 1 (otherwise).

void db_close (void);

Closes a previously opened database. If the database has been modified (some points have been added or deleted), it is written back to the database file.

void db_add_point (tpoint_t *tp);

Adds the specified point to the database. The argument must be a pointer created by malloc (see above). The structure passed via this pointer must not be touched by the program after the function returns. In particular, it must not be deallocated (freed).

void db_start_points (u32 peg);

The function initializes the operation of reading through a set of points. If the argument is zero, that set covers all the points stored in the database. Otherwise, the argument identifies a Peg, and the set of points is restricted to those that include the Peg in their association lists.

tpoint_t *db_get_point (void);

Returns the next point from the set initiated with db_start_points. Subsequent calls to db_get_point return the same point until the cursor is advanced with this function:

void db_next_point (void);

The set has been completely scanned when db_get_point returns NULL. Here is the way to read through all points in the database:

tpoint_t *tp;
...
for (db_start_points (0); (tp = db_get_point ()) != NULL;
db_next_point ()) {
handle_point (tp);
}

Note that tp points directly to a point structure stored in the database. Consequently, the program should not change its attributes or try to deallocate it.

void db_delete_point (tpoint_t *tp);

The function deletes the indicated point, which must be one of the points stored in the database.

# The location engine

Assuming that a database of points has been opened, this function carries out the actual location tracking:

int loc_locate (int K, u32 *pg, float *slr, int N, u32 prop,
float *X, float *Y);

where:

K is the suggested number of points to be used as the basis for estimation

pg is the array of Pegs of size N, and slr is the array (also of size N) of the corresponding SLR readings. Together, the two arrays describe the current association list of the tracked Tag.

prop is the properties attribute for the current association

X, and Y are the return parameters for passing to the caller the estimated coordinates of the Tag.

The function returns the number of points that were actually used in the estimation, which can be between 0 and K, inclusively. Zero means that no estimation could be made. Here is how the algorithm works:
1. The association list, i.e., the two arrays pg and slr, are sorted in the decreasing order of slr. This way, pg [0] is the Peg with the highest SLR. Full sorting is not needed in the present version, except for the selection of the highest SLR, but it is left to facilitate experiments (I had some ideas, but they can wait).
2. Let p = pg [0], and P_p be the set of all points in the database whose association lists include the Peg p . In other words, P_p consists of all those points from which p appears to be directly reachable. Let m = overline { P_p } denote the size of this set. All points in P_p are examined, and for each of them, its discrepancy from the Tag's association list is calculated as:

D_j = sqrt (sum_{i=1}^{k} (v_i^j - v_i )^2 )
where j indexes the set P_p (1...m) and i ranges through the Tag's association list, i.e., indexes the Pegs and their SLRs in arrays pg and slr. Specifically, v_i in the formula represents an element of slr, and v_i^j refers to the SLR of the same Peg in the association list of the examined point from P_p . If the point's association list does not include this particular Peg from pg, then the corresponding v_i^j is set to zero. This effectively assumes that SLR equal zero is equivalent to no reception at all. Any function transforming RSSI into SLR should take this into account.
1. Let M = min lbrace m, K rbrace . Let P_M subset P_p denote the subset of P_p consisting of M points with the smallest values of D_j . In plain words, we select K best matches from the set. If the set has less than K points, we select whatever we have. Let D_{max} = max lbrace D_i rbrace and S = sum_i D_i be respectively the maximum discrepancy and the sum of all discrepancies over those M best points. The resulting coordinates of the Tag are estimated as:

X = { sum_{i=1}^{M} x_i times {(D_{max} - D_i )} over { M times D_{max} - S} }
Y = { sum_{i=1}^{M} y_i times {(D_{max} - D_i )} over { M times D_{max} - S }}

The case when M is small (say less than 3) should be considered pathological. Note that the number of points used in the estimation is returned as the function value and made known to the caller. In particular, if only one point was available, then the estimated coordinates of the Tag are exactly equal to the coordinates of that point. If no points were available at all, then the returned values of the coordinates are 0.0, 0.0.

The formulas applied in step 3 calculate the weighted average of the coordinates of the matched points, with the weight being inversely proportional to the discrepancy.

Things to play with:

The mapping of physical RSSI into SLR. My first recommendation would be to use something that results in an approximately linear representation of distance, at least in typical noise-free environment within a room (easy to say). It should also decay to zero for the distance over which we would prefer to assume that the Peg does not really hear the Tag. That is to say, if at a certain (physical) RSSI value the Tag is supposed to be still visible, but not at a slightly smaller value, than the smaller value should transform to zero, while the slightly bigger value should map to something slightly above zero.

As I said earlier, there is no compelling reason for the mapping to be monotonic w.r.t. RSSI. At present, the selection (in step 1) of all points to be examined as prospective candidates for matching is restricted to those that associate with the Peg whose association to the Tag appears to be the highest (in terms of SLR). Other ideas are possible. For example, you can simply consider all those points in the database that associate at all to any Pegs appearing in the Tag's association list. With the proper organization of the database, such lookups can be simple and fast.

The way to calculate discrepancy in point 2. This may be related to SLR mapping. It may make sense to amplify the significance of truly close matches and, correspondingly, decrease the impact of weak associations.

The way to average the best matched points to produce the answer. Note that in some cases, the kind of averaging applied in step 3 may not be the best thing to do. For example, consider a region boundary. If the Tag is situated exactly at the boundary, say between two Pegs pinned to the perimeter, any Peg within the region will pull its location away from the boundary. Consequently, it may be wise to indicate to the algorithm that some Pegs are different.

The target number of reference points used for estimation. Instead of specifying this number as a parameter for loc_location, we may want the function to determine it based on some properties of the points. For example, all points whose discrepancies are below a certain threshold can be used, if their number is also above a certain threshold.

One more function provided by the location engine (which is in fact more related to database operation) is:

int loc_findrect (float x0, float y0, float x1, float y1,
tpoint_t **tps, int N);

which returns up to N points falling into the specified rectangle. Those points are returned in tps, whose size should be at least N. The total number of such points in the database is returned via the function value. If it is greater than N, it means that some points could not be accommodated in the array.

# Two programs using these tools

Subdirectory TEST contains two programs. One of them generates a randomized database of points, the other provides a simple interface to the functions described above, i.e., allows you to manually enter queries to the database and the location engine. Having executed make in the main directory (and generated libloc.a), you can run make in TEST, which will create two executables: gen_random_db and query.

# Generating random databases

This is accomplished by gen_random_db. The databases generated by the program are naïve and unrealistic, and their sole purpose is to test the engine functions.

The program accepts a simple data set (see file g_data.txt for an example) and creates a database in file points.db. Make sure that this file doesn't exist (or is empty) before executing the program, as otherwise the new points will be added to the existing database. The data set consists of 8 numbers. The first four describe the bounding rectangle for the set of points: X_0, Y_0, X_1, Y_1 . The next two numbers specify the propagation range r (in meters) and the redundancy u , which will affect the population (density) of Pegs. The next number determines the fuzziness (the extent of randomization) and should be well below 1.0. The last number, N , tells the program how many points are to be generated.

The program starts by generating Pegs on a regular grid spaced about r/(1+u) meters apart. The spacing is adjusted, such that the distribution of Pegs is even, i.e., the boundary rows and columns of Pegs fall exactly on the rectangle's perimeter. Then, the program generates N points randomly distributed within the rectangle. The association list of each point consists of those Pegs that are located no further than r meters away from the point (with some randomized factor depending on the fuzziness). The SLR of each Peg on the list is a number between 0 and 250 linearly scaled to the distance and slightly randomized.

# Queries

The second program, query, provides a command-line interface to the engine. When you call it without arguments, it will open or create a database file with the standard name points.db. If there is an argument, then it provides the file name for the database. Here is the list of commands (you will see a brief menu when you enter an invalid command, in particular help). The first letter of the command keyword is all that matters: any subsequent letters are skipped until a blank.

a x y prop npegs p v ... p v

Example:

a 110.3 221.1 0 7 1 34.5 2 39.0 3 55.1 9 16.2 12 3.5 17 88.0 22 255.3

The command adds a point to the database. The first two arguments are the coordinates, the third number is the properties attribute, the fourth argument specifies the length of the association list. This is followed by the association list consisting of the prescribed number of pairs: Peg, SLR.

f x y	or
f x y r	or
f x0 y0 x1 y1

Examples:

f 122.3 456.1
f 122.3 456.1 3.5
f 122.3 456.1 256.5 789.0

The command finds and displays points. In the first case, it finds the single point located closest to the specified coordinates. In the seconds case, it finds all points located within the radius r of the specified coordinates. In the third case, it finds all points within the rectangle described by the four coordinates.

The located points are stored in a buffer from where they can be listed again with this command:

s

which takes no arguments. The points stored in the buffer are numbered from 1 up. This command:

d pn ... pn

deletes from the database the indicated points. The numbers following d refer to entries the point buffer.

p peg

This command locates all points having the specified Peg in their association lists. The located points are displayed and stored in the buffer.

l k prop npegs p v ... p v

Example:

l 5 0 4 1 34.5 2 55.6 7 88.2 19 41.6

This command invokes the location engine to estimate the coordinates of a hypothetical Tag with the specified association using 5 best-matched points for reference. The arguments are as for the a command with the coordinates replaced by K (see loc_locate). In response, the program displays the estimated coordinates and the value returned by loc_locate (the actual number of points used for the estimation).

q

This command takes no arguments. It closes the database (writing it back to the file, if modified) and exits the program. Note that all modifications to the database (introduced with commands a and d) are volatile until the database is closed.