Pawel Gburzynski

# The Reflow Praxis

 December 29, 2012
Updated October 14, 2020

© Copyright 2011, 2012, 2020, Olsonet Communications Corporation.
All Rights Reserved.

Intro
The complete application consists of these components:
1. The node program to be run in a microprocessor. The microprocessor should be outfitted with a sensor (taking the temperature of the oven), and an actuator (setting the oven). The program amounts to a PID controller trying to follow a specified temperature curve. The controller is driven by the “plant” output supplied in the sensor and provides the input to the oven via the actuator.
2. The OSS GUI programmed in Tcl/Tk providing a user interface to the node program. The GUI can be used to input a curve to the program, start the reflow process, and monitor its progress.
3. An oven emulator programmed in SMURPH/SIDE that can interface to the node program executing in the virtual world (i.e., under VUE2). The node program itself comes with a built-in naive oven emulator that can be used to test the program and the GUI, also with the program running in a real device (that need not be connected to an oven).
One interesting feature of the praxis is the incorporation of the BOSS plugin for interfacing the GUI to the node program over the UART.
I have redone the previous version of the application trying to turn it into an educational demo/case study for a course on microcontroller programming that I was supposed to teach at some point.
External devices
The program assumes that the node has been interfaced to two devices: the sensor and the actuator. A real setup, involving a physical node and an actual oven, was implemented using these modules:
- a MAX6675 thermocouple temperature sensor (PicOS driver: max6675.c)
- a PWM relay (e.g., a thyristor) controlling the power supply to the oven
An MSP430-based device (known as the WARSAW board) provides the basis for the implementation. The respective board configuration can be found in BOARDS/WARSAW_REFLOW. See there for the relevant hardware options.
I have created a simple generic driver (pwm_driver.c) for the kind of PWM (pulse width modulation) control appropriate for a reflow oven. The idea is that the (default) total width of a power cycle is 1 second subdivided into 1024 slots corresponding to PicOS milliseconds. The setting parameter of the oven is a non-negative integer number from 0 to 1024 with 0 meaning “off” and 1024 meaning “fully on”. Anything in between represents the respective fraction of full power (the number of millisecond slots within one second when the PWM switch is on). At the beginning of each second, the driver switches the device on (by pulling a pin) for the number of ticks equal to the current setting of the control parameter. Then, following that many ticks, the device goes off for the remaining number of ticks within the second. This way, the on period is a continuous portion of every second. With the extreme settings (0 or 1024), the device never goes on or off, respectively. The PWM “device” is visible to the praxis as an actuator (see board_pins.h in BOARDS/WARSAW_REFLOW) whose range is 0–1024 (inclusively).
The thermocouple sensor requires calibration. The calibration data (obtained from a real-life setup) can be found (among other items) in file interface.h in subdirectory OVEN (the symbol THERMOCOUPLE_CALIBRATION) and consists of a sequence of pairs: <temperature, sensor reading> where the sensor readings must be strictly increasing and temperature must be non-decreasing.[1] The temperature is specified as an integer number in deci-degrees, i.e., in units of 1/10° C. This is also how temperature is represented internally in the node program.
[1] The data is used for bisection search and interpolation.
The idea is that subdirectory OVEN contains oven-specific parameterization of an actual oven connected to the application as well as the oven's SMURPH model that can be used for experimenting with the praxis in the virtual world.
Running the praxis in the real world
This assumes that the node program is executing in a real device (e.g., based on the WARSAW_REFLOW board). Make sure the node is flashed with the program. Connect the node to the PC (via a UART-over-USB dongle), reset it, and start the GUI script (see below). The script should auto-connect to the node after a second or two (assuming everything is OK).
The status is shown in the left upper corner of the main window. It can be one of:
disconnected	- the program is not connected to a node
connecting	- the program is trying to connect (polling some device)
idle	- the program is connected to the node and the node is idle
running	- the program is connected and the node is executing a reflow cycle
The interface is quite straightforward and, as all GUIs, intended to be self explanatory. Most widgets are equipped with tips which will show up when you hover the mouse over them. On startup (the first time around), the window shows the default profile which looks like a sequence of connected line segments (painted in green) ending with points (painted blueish). When you hover the mouse over a point, you will see the parameters of its segment (note that it is the segment preceding the point). These parameters are:
- the target temperature at the end of the segment
- the segment's intended duration in seconds
- the segment's intended end time in the complete sequence
You can easily edit the profile by dragging the points (the left mouse button). Note that you cannot drag a point sideways outside the time of its neighboring points. Time cannot flow backwards, but segment duration can be zero meaning that the target temperature should be reached as fast as possible. The specified timing of segments represents intended targets which need not be realistic, e.g., they may be impossible to obey by the oven (the target temperature may not be reachable within the prescribed time). The execution of a segment may take more than its specified duration, but it never takes less.
If you want to move the rightmost point beyond the edge (as to extend the timing of the whole set), right click the mouse within the display area and select one of the offered extensions. You can later select “trim” to remove any unused time beyond the rightmost point. The cycle always ends at the last point (associated the rightmost segment).
The menu that pops up after a right click varies slightly depending on the context. Note that you cannot edit the segments when running a cycle, so most of the useful clicks are not applicable in the “running” state. You need not be “connected” to edit profiles and save them for future usage.
When you right click over a segment point or near to its line, the menu shows the options of editing the segment (specifying its parameters as direct numbers instead of dragging the point), deleting the segment, inserting a new point (at the present location of the mouse), and reverting to the clean (unedited) version of the profile (as originally loaded). You can insert a new point anywhere by right clicking on the blank area of the display and making the proper selection from the pop-up menu.
Having edited the profile, you can save it (using the Save button, of course). The profiles are stored in the file named .rflowrc (in your home directory or its Windows equivalent) and will be available next time you invoke the program. The simple window you bring in with the Load button will allow you to load any of your saved profiles as well as delete them selectively. The DEFAULT profile cannot be deleted, but it can be edited and modified.
A profile is completely described by the three control parameters, S, I, D, and the list of segments. Each segment, in turn, is completely described by two parameters: the target temperature and the duration (the amount of time after which the temperature should be reached). Thus, assuming that NS is the number of segments in a profile, the profile is described by NS x 2 + 3 numbers. The maximum number of segments is 24. By modifying the current profile we mean changing any of the three (global) parameters or any of the two attributes of any segment. Once you have modified the current profile, and haven't saved it yet, the program will warn you whenever you try to do anything that would make you lose the changes.
Note that you can control the oven manually in the “idle” state (the Oven slider). The CT indicator tells you the temperature of the oven as reported by the node. The other temperature indicator, TT, is only active during a cycle run showing the target temperature at the moment, as implied by the current position within the segment.
When running a reflow cycle, you will see a red line of points representing the actual oven temperature at the respective time points as reported by the sensor. When the target end time of a segment is exceeded, the remaining segments will be shifted to the right, in accordance with the actual timing, and a gray dotted line will be inserted in between to represent the lag. One segment editing option, available (in the right-click menu) after a run (while the run data is still shown) is to adjust the segment timing to the actual timing. This will get you what you may consider an empirical, realistic adjustment of the profile to what the oven is able to accomplish.
Note that you cannot edit the profile during a run. When the run completes, the run data (the red points) are left on the screen. The right-click menu then gives you an option to remove the run data, which will also remove any dotted lag lines inserted between the segments. You cannot edit the profile segments (drag the points) while the run data is being displayed, except for adjusting the segment timing to the run data.
The GUI script features a button labeled Log On which, when clicked, opens a window logging the operation of the controller, including the numerical history of the reflow runs. When a cycle is on, a new line is produced every second showing:
1. the time (hour, minute, second)
2. the second of the current reflow cycle
3. the current temperature of the oven based on the sensor reading
4. the target temperature based on the current position within the segment
5. the segment number (counting from zero)
The log can be saved to a file by clicking the Save button in the log window.
The internal emulation mode
When you check the Emulation box in the upper line (above the profile graph), you will put the node into a mode whereby it will be emulating the oven. Note that this applies to a real node: the node will pretend that it is connected to an oven (ignoring the sensor and the actuator) mimicking its behavior in some (rather simplistic) sort of way. This feature is intended solely for testing the GUI script and its interface to the node. Better (external) oven models can be built for more serious experiments, as explained below.
Note that the emulation mode is implemented in the node, not in the GUI program, so the node must be connected for the emulation to work. For illustration, check the box (in the “idle” state) and move the oven slider to the right. You will see how the temperature of the dummy oven rises. You can run a complete reflow cycle in the emulation mode, but it is probably going to be unrealistic. Uncheck the box for normal operation.
The parameters of the controller
The three parameters of the control algorithm, associated with every profile, are:
S
The temperature span of the controller expressed in deci-degrees. If the target temperature at the time (according to the position within the current segment's slope) exceeds the measured temperature by more than S, then the oven is set at full throttle. Otherwise, i.e., the difference is less than S, the controller tries to be more subtle setting the throttle proportionally to the difference, with the maximum falling on S. The default setting is 200 (corresponding to 20 degrees). Reducing S makes the controller more aggressive. The maximum value is 1024.
For the settings 0 and 1 the oven goes full throttle for any positive temperature difference, so the control is effectively binary (on, off) with 1 second granularity.
I
The integral factor. The range is 0–1024. It should be set to something nonzero to prevent undershooting.
D
The differential factor. The range is 0–1024. Prevents overshooting and, probably, should be small.
I am contemplating ways to improve the control algorithm, but without increasing the number of parameters, which would be pointless and confusing (three is a lot already). Other enhancements are conceivable and probably natural (e.g., presetting the node for stand-alone operation).
Invoking the GUI script
The script is provided in subdirectory OSS as the file named reflow.tcl. It is possible to turn it into a clickable executable, which makes sense on Windows, by executing ./mkexe.h in the directory. Then the script can be invoked by clicking on the file, as a standard, directly executable, Windows program.
The script can be invoked directly (on a Linux system or under Cygwin on Windows) by executing:
./reflow.tcl arguments
These are the arguments accepted by the script:
–U dev ... dev
–V host port node
–D
with the items following –U or –V considered optional. An invocation without arguments is the same as with –U (not followed by anything else). Arguments –U and –V are exclusive: only one of them is legal at a time. The first one selects the physical mode with a connection to a real device over UART. If additional arguments are present, they are interpreted as the explicit list of devices to scan (as opposed to all serial devices currently visible to the system). For a Windows system, a device can be specified as COMx: where x is the COM number, or just a number (e.g., 3 means COM3:). On Linux, you can give the full path to the device, e.g., /dev/tty8, /dev/ttyUSB0, or a virtual device, e.g., /dev/pty3. A bare number defaults to a USB device, e.g., 7 translates into /dev/ttyUSB7. If the list is absent that all compatible devices appearing in the system are tried in turn.
When called with –V, the script will try to connect to a virtual UART of a virtual node emulated by VUE2. The remaining arguments default to localhost, 4443, 0, i.e., the model is running on the local system, operates using the standard VUE2 port, and the node number is 0. If the node number is preceded by the letter h, like h14, it is treated as the host number in a (TARP) network.
The last argument turns on debugging which means that the script will be writing messages to the standard output tracing its operation.
Note that when the script is turned into a Windows executable, it won't accept arguments (if run from a click). One can preconfigure it, e.g., for a virtual connection as the default, by editing the script before transforming it into the executable.
Experimenting in a virtual setup
When compiled and executed under VUE2, the node program behaves in exactly the same way as in a real device, except that:
1. the sensor and the actuator are virtual
2. the UART, over which the program talks to the GUI script is also virtual
It is possible in principle, with the assistance of an easily programmed kludge, to map the virtual sensors to real devices, pretending that the virtual node is real, but this is probably not the most interesting kind of exercise that one would want to carry out in the virtual setting.
The GUI script can be easily directed to connect to the virtual UART of the virtual node (see above), so the setup can be easily tested in the internal emulation mode. A more intriguing possibility is to interface an oven model to the virtual sensor and actuator of the virtual node. An example of such a model, programmed in SMURPH/SIDE, is present in subdirectory OVEN. To create its executable version, move to that directory and run the SMURPH compiler, like this:
mks -R
The compilation will produce an executable file called side (or side.exe on Windows/Cygwin) which can be simply run:
./side
to start the model (see README.txt in OVEN for the optional arguments). The program will be producing a line of output every second indicating the oven status. For as long as the model is detached from the virtual node (or, more specifically, its sensor and actuator), the line will say “not connected”. As soon as the node materializes, the model will connect to it, and the status line will change. The line presents (at 1 s intervals) these values:
1. the elapsed time in seconds.
2. the current temperature of the oven in °C.
3. the target temperature, as the oven interprets it based on the current actuator setting
4. the setting, i.e., the value in the actuator
5. the reading, i.e., the value returned in the senor
6. a letter in parentheses: h – heating, c – cooling, empty (dash) – idle
With the oven model, the setup is complete, and it operates pretty much as it would for a real node interfaced to a real oven. The model can be parameterized or tweaked to make things more interesting.