How to use front.tcl

November 27, 2008

# Prerequisites

Install ActiveTcl from this site: http://www.activestate.com/. Default installation options are fine.

# Usage

Double click on front.tcl. With the default installation setup of ActiveTcl, the tcl file name extension will be automatically handled by Tcl. If not, make sure to associate the tcl extension with C:\Tcl\bin\tclsh85.exe (or wherever you decided to install the Tcl package). A command-line window will open with this line at the top:

Enter COM port number:

Do as asked, i.e., enter the COM port number of the USB dongle connecting your PC to the node.

Note: the program works with collectors as well as aggregators. Some commands are only applicable to aggregators; some other commands have a different meaning depending on the node type. Generally, you never want to talk to a collector, unless you are going to run it in a stand-alone mode (see below).

At any time, you can enter “h” (or any “illegal” command) to see this list of legitimate commands:

Commands:
  start sec [continue] - start sampling at sec intervals
  stop - stop sampling
  show off|on - show received values while sampling
  echo off|on - show dialogue with the master
  extract filename - extract stored samples to file
  virgin [sec] - reset to factory state
  status - node status
  quit - exit the script

Talking to the aggregator (master)

Having connected to the master node, if you want to make sure that everything is nice and tidy, execute “stop”. This will reset the node and put it into to the default (idle) state. If you are not sure what is going on, and would prefer not to interrupt an ongoing data collection, execute “show on”. If you see no samples within some reasonably long interval (say two minutes), then most likely the master is “stopped”. You may also execute “status” (see below). If you see that “nothing” is being written to the EEPROM, then clearly the master is idle.

To start data collection, make sure that the collector nodes you want to use for the experiment are powered up, their sensors connected, and so on. If you do something like this:

start 60

the master will clear its EEPROM, set up parameters to collect samples from the audible collectors at 60 second intervals, and send out the requisite commands to the collectors to make sure they all know what to do. If you put “continue” after the interval specification, e.g.,

start 45 continue

the master will do the same except that it will NOT erase the EEPROM, i.e., new samples will be adding at the end of any previously collected data.

The minimum collection interval is 30 seconds.

Note that if you start a data collection and then exit the script (do quit), the master will keep working (collecting data) for as long as it is powered up.

At any time you can see that status of the node by executing “status”. Here is a sample output:

Aggregator 20:
      Audit interval: 59s
   Uptime: 7s
   Master: this node
   Stored samples: 0 / 16382
   Writing to EEPROM: nothing

This looks like a stopped node: no samples are being stored, and the buffer is empty. When you start data collection, the master's status may appear as:

Aggregator 20:
   Audit interval: 59s
   Uptime: 62s
   Master: this node
   Stored samples: 14 / 16382
   Writing to EEPROM: all

In particular, you can see this way how many samples have been stored and how much room still remains in EEPROM to accommodate new samples.

If you want to see the values being received by the master (as they are collected and stored), execute “show on”. “show off” will cancel that.

The sampling is synchronized by the master, such that it happens at the same instants at all collectors, even though the arrival times of samples at the master may be different. This is intentional: the transmissions are spread in time to avoid collisions. Note that during some initial period (while the collectors are still getting the parameters from the master), they may be out of sync.

Note: the storage size at the master allows it to accommodate up to 16,382 samples. Thus, for example, 5 collectors running every 30 seconds will use it up in 16,382/(5x2) minutes (i.e., about 27 hours).

When you execute stop, the master will cease to store any new samples arriving from the collectors.

If you want to see the dialogue between the script and the master (i.e., the actual messages exchanged by the two, which may be useful for debugging), use “echo on”. Normally, you don't want to see them.

To extract all samples available in the master's storage execute

extract filename

where filename identifies the file where you want them stored. Usually, you will execute extract after stop (in the stopped state), although it is legal to do it on line. In principle, the extraction will not interfere with ongoing collection. The operation may take a while (the script displays its progress by showing you the sample numbers as they are being extracted). In the future, we may want to speed up this operation a bit.

The samples are stored as a trivial txt file, which can be easily read in by the Excel Wizard. Here is the list of fields:

1. The time stamp in the format dd.hh:mm:ss, where dd is the day number (the first day of the experiment is numbered 0), and the rest is the time. When you start an experiment from the script (with a computer attached to the master node), the sampling time is initialized from the computer clock.
2. The collector number
3. The PAR sensor, two values: raw + converted
4. The temperature sensor, two values
5. The humidity sensor, two values
6. The moisture sensor, two values
7. A dummy (nonexistent) sensor; the two values indicate the sample count

Note that the second value of each pair is the one that matters. For the temperature and humidity sensors, that value should be authoritative, while the remaining two values (PAR and moisture) may have to be re-calibrated.

Talking to collectors

One reason why you may want to talk to a collector is to read its stored set of samples; another reason would be to reset the node for stand-alone operation. Only these commands applicable to a collector: extract, virgin, stop, and status (+ echo). Sample extraction works the same way as for the aggregator. The only difference is that the list of fields stored in the file does not include item 2.

Here is a sample output of “status” for a collector:

Collector 202:
   Sampling interval: 30s
   Uptime: 12102s
   Stored samples: 16 / 32766
   Writing to EEPROM: not confirmed

It says that the collector is only storing in its memory those samples that have not been confirmed by the aggregator. This is the typical status for a collector interfaced to an aggregator.

The role of the “virgin” command is to reset the node to factory defaults, erase its memory, and, optionally, prepare it for stand alone operation (see below).

Recipes

Normal operation: a bunch of collectors supervised by a master

1. Outfit the collectors with sensors and switch them on. Note that the PAR sensor (as well as the moisture sensor) plug into the right socket (looking from the top, with the sockets facing forward), while the SHT combo plugs into the left socket. A collector is ON when the switch is is positioned towards the outside of the box (to the left in the above sense).
2. Connect the aggregator to the USB dongle. The green wire of the plug should be on the side of the switch.
3. If you are going to leave the aggregator disconnected from the PC (to be powered from a battery), switch it on, i.e., move the switch to the outside (away from the USB socket). Otherwise, if the node is going to remain connected to the PC (and be powered from the dongle) for the ENTIRE duration of the experiment, move the switch to the inside (this is the OFF position).
4. Invoke the script and give it the COM port number of the dongle device.
5. Execute “start”, as explained above.
6. Now (assuming the aggregator's switch is in the left position), you may disconnect the dongle and leave the node alone. You will come back later to collect the data.
7. When you plug the node to the PC again, you may switch it off, i.e., move the switch to the right. Execute “stop” followed by “extract”.

A bunch of collectors supervised by a master with automatic startup

You do not have the laptop at startup, so you want to prepare the nodes at the hotel and start them later.

1. Outfit the collectors with sensors without switching them on.
2. Connect the aggregator to the dongle. The switch can be OFF (in the right position).
3. Invoke the script as before.
4. Execute “virgin n”, where n is the sampling interval, and wait until the operation completes.
5. Unplug the node.
6. Now, you can deploy your setup. Switch the nodes on. It makes sense if the aggregator is the last node to be switched on. Write down the time when you turn the switch. You will use it as a reference to offset the time stamps of the samples, which will now start at 0.00:00:00.
7. The rest is as before.
Independent collectors

There is no aggregator. You want to deploy a few collectors operating by themselves.

1. Do this for each collector. First, connect the collector to the USB dongle. The switch should be in the OFF position for now. No need to outfit the node with its sensors at this stage.
2. Invoke the script, as before.
3. Execute “virgin n”, where n is the sampling interval, and wait for the operation to complete. When prompted by the script, remove the USB plug from the node. The node is now turned off.
4. Outfit the collectors with their sensors.
5. When you switch the collector on, write down the time. You will have to offset the time stamps of the samples as in the previous case.
6. At the end of the experiment switch the collectors off (so they won't be collecting any unwanted samples).
7. When you get to the computer, plug the collector in (the switch should remain in the OFF position). Invoke the script (the usual way) and execute “stop”. This makes sure that the collector will not try to collect any samples while you are dealing with it.
8. Extract the samples as explained above.

Note: if you have been using a collector for stand-alone operation, and you want to put it back into a set orchestrated by the aggregator, you will have to reset it to factory defaults. For that, connect it to the script and execute “virgin” (without the interval argument). You can do that whenever you suspect that something may be wrong with the node. Generally, there should be no need to do it for the aggregator, but it won't hurt.