# The Seawolf Project

Object Exchange Protocol
Image Format
Reference Praxis

Version 0.01
May 30, 2008

Proprietary and confidential
# Assumptions

This document describes the reliable object exchange protocol for wireless devices in immediate proximity. The protocol assumes that the devices can communicate directly, i.e., they are within each other's transmission range. The protocol is carried out outside TARP, preferably in a way that does not interfere with (low-bandwidth) TARP transmissions, e.g., using a separate channel (and a different transmission rate setting). The interested devices will have to switch to a special mode before an object exchange can be carried out.

As a prerequisite, the interested parties are supposed to know their distinct 16-bit identifiers, which can be extracts from the nodes' ESNs or separate identifiers pre-negotiated in the low-bandwidth mode. Objects to be exchanged are identified by 16-bit types and 16-bit numbers. Objects of different types can share the same number while being different. The protocol is primarily intended for exchanging pictures to be displayed on the LCD; however, general objects whose length may be considerable and whose integrity of reception is important can be accommodated.

# Packet format

Figure 1 shows the general layout of a packet exchanged by the protocol. All multi-byte components are sent in little endian order. The trailing CRC field is not directly visible to the program and is only included for completeness. The initial LID (Link ID) component formally belongs to the PHY; however, the protocol interprets it and sets as required. For this purpose, the RF driver must be set to the transparent network ID mode, which is accomplished by setting the node's network ID to 0xFFFF (with PHYSOPT_SETSID). In this mode, the driver will pass through all received packets (regardless of the LID field) and also honor the LID value passed to an outgoing packet by the praxis.

Figure 1: Packet format
The CM field indicates the packet type, i.e., the specific “command” of the protocol. The RN field carries the request number used for matching replies to requests. The idea is this. When a node requests something from another node, then it will send a packet with its own LID and set RN to some value. Typically, the node will increment RN (modulo 256) with every new request. It is also assumed that RN is never zero (value zero is reserved for special requests that need not be numbered). Any packet constituting a reply (or part of a reply) to the request will include the requester LID and RN matching the original values from the request packet. This way that requester will recognize packets that are relevant to its request (ignoring any any late packets from previous requests).

The length of the PAYLOAD field depends on the packet type (CM). For some CM codes, the payload length is fixed; for some others, it may vary. The packet length attribute (returned by tcv_left) can be used in such cases to determine the actual payload length. In all cases, that length is even.

# The object exchange protocol

One of the two nodes, call it the retriever, decides that it wants to acquire an object from another node, which we shall call the provider. A scenario is possible whereby the exchange is initiated by the provider, which tells the other node to retrieve an object from it; however, in such a case, the initiating message does not formally belong to the exchange protocol.

Figure 2: WTR packet format
Thus, the retriever starts the exchange by sending a WTR (Willing To Receive) packet in the format shown in Figure 2. The LID field of the packet contains the Link ID of the retriever. The RN value is chosen by the retriever. From now on, until the end of the exchange (successful or not), the pair [R_LID, RN] will identify the request. This means that all packets belonging to the exchange will have identical contents of these two fields.

The three payload fields have the following meaning:

P_LID	This is the Link ID of the provider. Any node receiving the packet will	check this field and ignore the packet if P_LID does not match the	node's Link ID.
OTYPE	This is the type of the object to be retrieved.
OID	This is the ID of the object. As we said earlier, objects are uniquely	identified by these two numbers.
The retriever will be retransmitting periodically the WTR packet at reasonable intervals, until it receives a reply from the provider, or until it timer expires (in which case it will give up). In the reference implementation, the retriever tries 24 times (probably an overkill) at slightly randomized 0.5 s intervals. There are two possibilities regarding a valid reply from the provider. If it has the requested object and is willing to send it, it will respond with an RTS (Ready To Send) packet shown in Figure 3.

Figure 3: RTS packet format
The RTS packet contains the R_LID and RN values from the WTR packet sent by the retriever. The first element of the payload is the object's size expressed as the number of 54-byte chunks. The layout of the remaining components, covered by the blanket name ODESC (object description) depends on the object type. Thus, the total size of an RTS packet may be different for different object types.

The purpose of the RTS packet is to convey to the retriever the relevant parameters of the object, notably its size. The reason why this size is expressed in 54-byte chunks is that those chunks are the transmission units, i.e., each chunk will be sent in a separate packet. The retriever is expected to keep a tally of the received chunks and be able to notify the provider which chunks are missing.

Some other attributes may be relevant for specific types of objects. For example, for an image, the retriever may want to know the geometry and encoding, such that it can immediately render the image as its chunks arrive.

Figure 4: ACK packet format
If the provider is unable to send the requested object, it will respond with a negative acknowledgment. The general layout of an acknowledgment packet (acknowledgments may also be sent in some other circumstances) is shown in Figure 4. The LID and RN fields are related to the request being acknowledged. CODE identifies the acknowledgment status. If it is zero, the acknowledgment is positive; otherwise, the nonzero value of CODE tells the reason for the failure.

In this particular case, should an acknowledgment arrive in response to WTR, it can only be negative (i.e., CODE cannot be zero). The LID field must be equal to R_LID of the request, and RN must match the request number. Otherwise, the retriever is free to ignore the packet.

Here is the list of possible CODEs. Only some of them can be given in response to a WTR packet.

1	General failure (no explicit reason given)	.
2	Busy. The node is currently handling a request.
3	Reject.
4	Not found (e.g., the node does not have the requested object).
5	Request format error.
6	Already done or already have it.
7	Unimplemented operation.

Only codes 2 and 4 can be returned in response to WTR. Erroneous WTR packets are ignored in the reference implementation (thus, no code 5 is returned), but this can be changed.

A negative acknowledgment packet is sent only once. If it is lost, the retriever will re-issue the WTR packet, which should trigger another negative acknowledgment (unless, e.g., the busy condition of the provider has been cleared). Regarding the RTS packet, the provider should retransmit it periodically until a response arrives from the retriever, or a timeout is triggered. The reference implementation will retransmit the RTS packet 24 times at slightly randomized 0.5 s intervals unless a response from the retriever arrives in the meantime.

The latter has two options. First, having seen the parameters of the requested object, it can conclude that the object is not needed after all. In such a case, the node will respond (once) with a negative acknowledgment using CODE 3 (reject). This is the reason why the RTS packet should be retransmitted periodically by the provider (rather than being triggered once by every WTR). If the retriever still wants to receive the object, it will initiate the first round by sending a GO packet.

From now on, the actual transmission of the object will be taking place. It will consist of rounds, whereby the retriever first notifies the provider which chunks of the object are still missing, and then the provider sends those chunks back-to-back, without expecting anything from the retriever until all chunks in the round have been sent. At the end of a round the retriever tallies up the chunks and, if some are still missing, tells so the provider, which then sends another batch of chunks as required. This operation continues until all chunks have been received or any of the two parties hits a timeout while expecting a reply from the other.

Figure 5: GO packet format
The retriever notifies the provider about missing chunks with a GO packet (see Figure 5). The payload consists of the list of missing chunks numbered from 0 up to the total number of chunks in the object –1. This list may contain individual chunk numbers (little endian 16-bit numbers) or ranges. For as long as the numbers in the list are increasing, they stand for individual chunks. A decreasing pair of numbers represent a continuous range of chunks between and including the two. For example, the sequence 3, 5, 6, 9, 13, 8, 17 describes chunks 3, 5, 6, 9, 8 through 13, and 17. Normally, the initial GO packet sent by the retriever specifies N-1, 0, i.e., the complete range of all chunks (its payload length is 4 bytes). Note, however, that if the retriever has a partially received version of the object (e.g., connectivity was lost during a previous session), it can naturally resume in the exact place where the previous reception was aborted.

In any case, a round is always started by a single GO packet, which means that the provider may only be able to learn about a subset of all those chunks that are still missing at the retriever. This will happen if the complete description of all those chunks cannot fit into a maximum-sized GO packet (23 16-bit numbers). Note, however, that the first GO packet of a reception starting from scratch asks the provider to send all chunks of the object. Thus, in the first round, the provider will send the entire object with all chunks sent back-to-back.

Having created a GO packet for the next round, the retriever should retransmit it periodically until it sees the first CHUNK packet arriving from the provider (or until it hits a timeout). The reference implementation will retransmit a GO packet 24 times at slightly randomized 0.5 s intervals.

If the retriever finds out that it has all the chunks in hand, it should notify the provider that the reception is over by sending it an empty GO packet (empty list of chunks). There will be no reply to such a packet: the provider will just shut down ending its part of the protocol. If the retriever wants to improve the chance that the provider has seen the packet, it can send the empty GO a few times. This isn't critical, as the provider will eventually time out while expecting a GO from the retriever and end the session anyway. The reference implementation sends the empty GO packet twice separated with a slightly randomized 0.5 s interval.

Figure 6: CHUNK packet format

The only valid response to GO is a CHUNK packet. Normally, the provider sends multiple CHUNK packets in response to a single GO, as many of them, as many chunks have been requested (in fact more – see below). The layout of such a packet is shown in Figure 6.N is the chunk number (starting from zero). The number of chunk bytes is always 54, with the possible exception of the last chunk, which can be partial. Note that this number is always even. Consequently, if the object consists of an odd number of bytes (and this fact is relevant), this information must be conveyed to the retriever in the RTS packet.

Note that chunks are not expected to be sent (or arrive) in any particular order. The provider is free to send them in any order, possibly duplicating some, possibly missing some from the requested list. The latter could have been missing due to losses in the wireless channel, so it should make no difference to the retriever. For example, the provider may not have enough memory to be “accurate” about the retriever's request. The protocol operates according to the principle of pushing the system towards the target state, with the quality of the “pushes” self scalable to the circumstances, be it the node footprint or the channel quality.

Having completed the current round, i.e., transmitted all the chunks that it was going to send in response to the last GO request from the retriever, the provider send an empty CHUNK packet, i.e., one with no payload. This packet is sent periodically until the provider sees another GO from the retriever (or until it hits a timeout). The reference implementation retransmits the empty CHUNK packet 24 times at slightly randomized 0.5 s intervals.

# Image format

The praxis directory contains a script named cbm.tcl for converting Windows bitmap images to the internal format for storing and displaying on the Nokia LCD. The present version converts only 24-bit images. This is how you call it:

cbm.tcl image.bmp image.nok

Converts file image.bmp (containing a 24-bit Windows bitmap image) to image.nok in 12-bit format. This is equivalent to:

cbm.tcl -12 image.bmp image.nok

This way:

cbm.tcl -8 image.bmp image.nok

you will create an 8-bit version of the image.

The program will prompt you for a “label”, which can be any piece of string intended to briefly describe the image. Its maximum useful length is 34 characters. When images are stored in the board's flash, labels can be used to identify them.

The maximum resolution of an image accepted by the script is 130x130 pixels (this is the maximum size picture that can be displayed on the LCD).

Here is the layout of the image file (all numbers are little endian):

Bytes 0-3	ASCII characters 'o' 'l' 's' 'o' intended as a magic code.
Bytes 4-5	An integer number identifying the message type. Only two values are used	are used at present: 0 – 12 bits per pixel, 1 – 8 bits per pixel.
Bytes 6-7	X resolution (the number of pixels in a row).
Bytes 8-9	Y resolution (the number of rows).
Bytes 10-11	Label length in bytes.

This is followed by the label (exactly the specified number of bytes), which, in turn, is followed by the pixels stored by rows. With the 8bpp format, each pixel takes exactly one byte (encoded as described in reference documentation for Nokia LCD – Phillips PCF8833). With the 12bpp format, two consecutive pixels take three bytes. If the total number of pixels is even, the total number of bytes is divisible by 3. Otherwise, the last pixel takes two bytes.

To be continued ...